## Slide 1
2021. 10. 05
JVET-X0058: AHG12: Bilateral matching SMVD mode
Donghyun Kim, Hyoungjin Kwon, Jongho Kim, Woong Lim, Se Yoon Jeong

## Slide 2
Introduction
I
Symmetric MVD (SMVD) and DMVR
  Both require reference pictures with different temporal directions and equal POC distance
  In SMVD, MVD0 is signaled, and
  In DMVR, is implicitly derived, and
To reduce the signaling overhead of MVD0 in SMVD, a new BM-SMVD mode, which derives MV difference using Bilateral Matching (BM), is proposed.

## Slide 3
Proposed method: BM-SMVD
II
Syntax related to BM-SMVD mode
When BM-SMVD flag is true, indices of AMVR and BCW are set to IMV_OFF and BCW_DEFAULT, respectively
BM-SMVD was implemented on VTM-13.0 and ECM-2.0
SMVD?
BM-SMVD?
(flag)
NO
NO
implicitly derived using BM
SMVD
(MVD0 signaled)
Other modes
Yes
Yes

## Slide 4
 | Random Access Main 10 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.08% | -0.11% | -0.05% | 101% | 100%
Class A2 | -0.09% | 0.00% | -0.14% | 101% | 100%
Class B | -0.08% | -0.02% | -0.02% | 102% | 100%
Class C | -0.06% | 0.01% | -0.14% | 101% | 99%
Class E |  |  |  |  | 
Overall | -0.08% | -0.03% | -0.08% | 101% | 100%
Class D | -0.11% | -0.13% | -0.07% | 100% | 99%
Class F |  |  |  |  | 
Proposed method: BM-SMVD
II
BM-SMVD on VTM-13.0
  For BM refinement, DMVR in VVC is used
    Constraint on block size (, same as DMVR)
  BDOF is used for further refinement
  To avoid a latency issue, initial MV is used for spatial MV propagation as in DMVR

## Slide 5
 | Random Access Main 10 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.15% | -0.22% | -0.11% | 103% | 100%
Class C | -0.19% | -0.21% | -0.19% | 102% | 100%
Class E |  |  |  |  | 
Overall |  |  |  |  | 
Class D | -0.21% | -0.12% | -0.26% | 103% | 100%
Class F |  |  |  |  | 
Proposed method: BM-SMVD
II
BM-SMVD on ECM-2.0
  Since, DMVR is replaced by MPDMVR in ECM
    For BM refinement, MPDMVR is used
    No constraint on block size (same as MPDMVR)
    Refined MV is used for both spatial and temporal MV propagation
  LIC and OBMC are disabled when BM-SMVD mode flag is true
(Both anchor and test set inter template matching tools to 0)

## Slide 6
Thank you