## Slide 1: JVET-X0142 Non-EE2: Extended MRL candidate list
Keming Cao, Yao-Jen Chang, Bappaditya Ray, Vadim Seregin, Marta Karczewicz Qualcomm Inc.

## Slide 2: Extended MRL candidate list
In current ECM-2.0, MRL candidate list is : {1, 2}
Proposed extended MRL list: {1, 3, 5, 7, 12}
MRL list for TIMD: {1, 3}
Thank Kwai for crosschecking
 | All Intra Main10 |  |  |  | 
 | Over ECM-2.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.04% | 0.04% | -0.06% | 99% | 97%
Class A2 | -0.09% | -0.10% | -0.09% | 101% | 99%
Class B | -0.12% | -0.04% | -0.06% | 102% | 98%
Class C | -0.11% | 0.00% | 0.09% | 102% | 97%
Class E | -0.10% | -0.16% | 0.09% | 102% | 97%
Overall | -0.10% | -0.05% | -0.01% | 101% | 98%
Class D | -0.05% | 0.06% | -0.04% | 102% | 100%
Class F | -0.21% | -0.16% | -0.12% | 100% | 96%
Class TGM | -0.20% | -0.14% | -0.09% | 99% | 97%
 | Random Access Main 10 |  |  |  | 
 | Over ECM-2.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.06% | 0.03% | -0.03% | 100% | 99%
Class A2 | -0.05% | -0.19% | 0.06% | 99% | 98%
Class B | -0.06% | 0.01% | 0.03% | 102% | 101%
Class C | -0.04% | 0.07% | 0.14% | 102% | 101%
Class E |  |  |  |  | 
Overall | -0.05% | -0.01% | 0.06% | 101% | 100%
Class D | 0.00% | -0.24% | 0.23% | 103% | 102%
Class F | -0.07% | -0.06% | -0.02% | 101% | 101%
Class TGM | -0.11% | -0.10% | -0.12% | 100% | 101%