## Slide 1: JVET-X0147 EE2-related : intra mode derivation based on TIMD for GPM inter/intra
H. Jang, S. Kim, J. Lim (LGE)
Y. Kidani, H. Kato and K. Kawamura (KDDI)

## Slide 2
Summary
Proposal
  Without extra signaling, applying intra mode derived by “TIMD” for intra coded GPM separate region
    Identical approach in CIIP + TIMD
  Restriction of the case for GPM-Intra/Intra for inter CU
    Identical with option2 in JVET-X0166
  In supplemental test, applying GPM storage modification introduced
    Identical with option5 in JVET-X0166
Simulation result
RA : -0.06%, -0.15%, -0.11% / 101% EncT, 100% DecT
LDB : -0.13%, -0.54%, -0.59% / 102% EncT, 100% DecT
LDP : -0.48%, -1.64%, -1.19% / 106% EncT, 99% DecT
Supplemental simulation result
RA : TBD%, TBD %, TBD % / TBD % EncT, TBD % DecT
LDB : TBD %, TBD %, TBD % / TBD % EncT, TBD % DecT
LDP : -0.54%, -1.60%, -1.35% / 106% EncT, 98% DecT

## Slide 3
Proposed method.
1. Intra mode derivation from TIMD
the intra prediction mode with the smallest SATD values in the TIMD mode list is selected and mapped to one of the 67 regular intra prediction modes.
2. Restriction the combination intra-intra GPM block
intra
inter
intra
intra
allowed
disallowed

## Slide 4
Considering throughput in Low delay Scenario
Current ECM-2.0, by the CIIP
  In LDB, Bi-directional motion compensation with intra predictor blending is allowed
  In LDP, Uni-directional motion compensation with intra predictor blending is also allowed
With the propose method,
  There is no additional requirement for memory bandwidth and throughput delay.
  In LDP, if one of GPM separate region is coded as inter, the other is implicitly derived to be coded as intra.
  So far, GPM is not allowed due to the restriction for bi-directional prediction in LDP.
  This proposed method can enabled GPM in LDP without any additional requirement.
inter
inter
disallowed
intra
inter
forced
intra
inter

## Slide 5
Simulation result
 | RA |  |  |  |  | LB |  |  |  |  | LP |  |  |  | 
Class | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT | Y | U | V | EncT | _DecT
A1 | -0.06% | -0.10% | -0.05% | 100% | 99% |  |  |  |  |  |  |  |  |  | 
A2 | -0.03% | -0.17% | -0.01% | 101% | 99% |  |  |  |  |  |  |  |  |  | 
B | -0.07% | -0.18% | -0.23% | 102% | 101% | -0.18% | -0.46% | -0.44% | 101% | 99% | -0.45% | -1.37% | -1.15% | 105% | 100%
C | -0.08% | -0.14% | -0.07% | 102% | 102% | -0.18% | -0.67% | -0.45% | 102% | 101% | -0.78% | -2.29% | -1.46% | 106% | 98%
E |  |  |  |  |  | 0.02% | -0.49% | -1.01% | 103% | 102% | -0.11% | -1.23% | -0.88% | 106% | 99%
Overall | -0.06% | -0.15% | -0.11% | 101% | 100% | -0.13% | -0.54% | -0.59% | 102% | 100% | -0.48% | -1.64% | -1.19% | 106% | 99%
D | 0.01% | -0.29% | 0.00% | 102% | 101% | -0.02% | -0.23% | -0.98% | 102% | 101% | -0.33% | -1.53% | -1.46% | 106% | 101%
F | -0.01% | -0.18% | -0.17% | 102% | 101% | -0.17% | -0.62% | -0.09% | 101% | 101% | -0.44% | -0.96% | -0.42% | 103% | 100%
Intra mode derived from TIMD for GPM intra region
Restrict intra/intra blending

## Slide 6
Supplemental simulation result
 | RA |  |  |  |  | LB |  |  |  |  | LP |  |  |  | 
Class | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT | Y | U | V | EncT | _DecT
A1 | -0.32% | -0.70% | 0.05% | 100% | 100% |  |  |  |  |  |  |  |  |  | 
A2 | TBD | TBD | TBD | TBD | TBD |  |  |  |  |  |  |  |  |  | 
B | -0.10% | -0.27% | -0.28% | 100% | 100% | TBD | TBD | TBD | TBD | TBD | -0.50% | -1.50% | -1.34% | 104% | 98%
C | -0.17% | -0.38% | -0.25% | 102% | 102% | -0.38% | -0.77% | -0.48% | 101% | 99% | -0.79% | -2.14% | -1.56% | 106% | 99%
E |  |  |  |  |  | 0.04% | -0.11% | -0.65% | 102% | 100% | -0.27% | -1.05% | -1.08% | 107% | 99%
Overall | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | TBD | -0.54% | -1.60% | -1.35% | 106% | 98%
D | -0.12% | -0.49% | -0.07% | 101% | 100% | -0.19% | -0.42% | -1.14% | 102% | 101% | -0.31% | -1.14% | -1.48% | 107% | 102%
F | -0.09% | -0.25% | -0.14% | 101% | 100% | -0.32% | -0.70% | 0.05% | 100% | 100% | -0.54% | -1.60% | -1.35% | 106% | 98%
Intra mode derived from TIMD for GPM intra region
Restrict intra/intra blending
GPM storage modification (option 5 in JVET-X0166)

## Slide 7
Conclusion
This contribution suggest GPM intra/inter mode using conventional TIMD intra mode derivation as is,
without additional throughput delay and bandwidth requirement.
Therefore, It is suggest to consider to adopt Next ECM software.