## Slide 1
JVET-Y0054 Update on a VVC software decoder, BVC, for heterogeneous CPU plus GPU systems
Lingyu Li, Haibin Yin, Li Zhang, Yang Zhang
Bytedance Inc.

## Slide 2: Introduction
BVC decoder:
  As a follow-up of JEVT-V0128
  A VVC software decoder for heterogeneous CPU plus GPU systems.
Notes: Tools supported
  Almost all the tools in Main 10 Profile
  IBC, BDPCM, BDOF, DMVR, ALF, etc.
Tools not supported yet
  Tools for 360 applications
  Wrap-around motion compensation
  Projection formats

## Slide 3: Optimization

## Slide 4: Supported platform
Apple/arm AArch64:
  iOS
  MacOS M1

## Slide 5: Test settings
Platform & Device
  MacOS, Mac mini (Apple M1)
  iOS, iPhone 13 (Apple A15)
Bitstreams
  Generated using VTM-11.0, CTC RA configuration
  CTC conditions except internal bit depth is set to 8

## Slide 6: Performance on Mac M1
For 4K 8-bit CTC bitstreams
  Achieve 39 fps with single thread on average
  10x faster than the VTM11.0 reference decoder with single thread
 | BVC (CPU+GPU) vs. VTM-11.0 |  |  |  |  |  | 
 | RA |  |  |  |  |  | 
 | VTM-11.0 (fps) | BVC (CPU+GPU)(fps) |  |  | Speedup ratio |  | 
 |  | T-1 | T-2 | T-4 | T-1 | T-2 | T-4
class A1 | 3.75 | 42.98 | 79.51 | 129.79 | 11.46 | 21.19 | 34.6
class A2 | 3.37 | 34.25 | 63.73 | 105.33 | 10.17 | 18.92 | 31.27
class B | 14.8 | 154.58 | 280.01 | 423.69 | 10.45 | 18.92 | 28.63
class C | 70.75 | 605.52 | 872.22 | 1161.9 | 8.56 | 12.33 | 16.42
class D | 264.51 | 1592.07 | 1856.28 | 2439.1 | 6.02 | 7.02 | 9.22
class F | 54.23 | 710.23 | 998.03 | 1236 | 13.1 | 18.4 | 22.79
Notes: CPU: 8 (4× high-performance + 4× high-efficiency)
GPU: Apple-designed integrated graphics (up to 8 cores)

## Slide 7: Performance on iPhone13
For 4K 8-bit CTC bitstreams
  Achieve 35 fps with single thread on average
  15x faster than the VTM11.0 reference decoder with single thread
 | BVC (CPU+GPU) vs. VTM-11.0 |  |  |  |  |  | 
 | RA |  |  |  |  |  | 
 | VTM-11.0 (fps) | BVC (CPU+GPU)(fps) |  |  | Speedup ratio |  | 
 |  | T-1 | T-2 | T-4 | T-1 | T-2 | T-4
class A1 | 2.2 | 39.5 | 60.7 | 67.7 | 17.6 | 27.2 | 30.3
class A2 | 2.0 | 30.8 | 48.8 | 54.1 | 15.3 | 24.2 | 26.8
class B | 9.8 | 144.3 | 205.0 | 217.7 | 14.8 | 21.0 | 22.3
class C | 53.5 | 473.3 | 563.7 | 630.3 | 8.9 | 10.5 | 11.8
class D | 206.6 | 970.5 | 1043.5 | 1074.2 | 4.7 | 5.1 | 5.2
class F | 43.6 | 444.1 | 527.6 | 616.0 | 10.2 | 12.1 | 14.1
Notes: CPU: (2 "big" Lightning + 4 "little" Thunder)
GPU: Apple-designed 4 core

## Slide 8: Conclusion
BVC decoder employs GPU to accelerate VVC decoding for heterogeneous CPU plus GPU systems
  For videos @30fps with 8 bit coding, using Mac M1 or iPhone 13
    The BVC decoder achieves real-time decoding speed for 4K resolution with single thread

## Slide 9: Reference
Y. He, L. Li, Y. Li, H. Yin, J. Zhang, L. Zhang, Y. Zhang (Bytedance), “Performance of a VVC software decoder - BVC”, doc. JVET-V0128 of ITU-T/ISO/IEC Joint Video Experts Team (JVET), 22nd meeting: April 2021.

## Slide 10
Thanks