## Slide 1: JVET-Y0068 EE1-2.1-related: RPR encoder with multiple scale factors
Junghak Nam, Sunmi Yoo, Jaehyun Lim, Seung-Hwan Kim

## Slide 2: Introduction
In EE1-2.1, the performance of RPR tool in VVC is reported to compare performance of contributions in super-resolution category
  Scaling factor ×2.0 only
  Multi-pass coding to choose either with or without RPR
  QP adjustment for each sequence/QP points
In JVET-W0082, GOP-based RPR control scheme was proposed
  Determine encoding picture size based on self-similarity and QP
If a smart RPR encoder could find optimal encoding parameters such as encoding picture size (resolution), QP, frame rate and coding tool configurations, coding gain could be achieved

## Slide 3: Proposed method
The proposed RPR encoder supports two scale factors
  Scale factors: ×2.0 (half size) and ×1.5 (2/3 size)
  Select a scale factor in the GOP level
  QP adjustment for the target bitrate: −6 for ×2.0, −4 for ×1.5
  Determine a scale factor as follows:
    Calculate a PSNR to estimate frame complexity
    Determine a scale factor among{×2.0, ×1.5, ×1.0} comparing self-similarity based on PSNR as follows,
DnUpPSNRi : down-up scaled PSNR for the first picture of i-th GOP
BasePSNR : 45 (RA), 42 (AI)
BaseQP : 37
OffsetPSNR : 3
QPi : initial QP for the first picture of i-th GOP
      0.5 dB adjustment per QP difference

## Slide 4: Experimental results (QP 22 ~ QP 42)
AI
RA
 | Y-PSNR | U-PSNR | V-PSNR | Y-MSIM | U-MSIM | V-MSIM | EncT | DecT CPU | DecT GPU | bit DIFF
Class A1 | -1.55% | 2.38% | 2.60% | -4.34% | 2.99% | 4.09% | 110% | 65% | #DIV/0! | 7%
Class A2 | -2.81% | 12.66% | 9.69% | -6.91% | 9.98% | 8.04% | 95% | 74% | #DIV/0! | 4%
Class B | 0.52% | 2.13% | 2.27% | -1.41% | 3.09% | 3.92% | 100% | 88% | #DIV/0! | 0%
Class C | 0.00% | 0.00% | 0.00% | -0.01% | -0.09% | -0.04% | 100% | 100% | #DIV/0! | 0%
Class E | 0.09% | 0.25% | 0.27% | -0.36% | 0.68% | 0.42% | 101% | 97% | #DIV/0! | 0%
Overall | -0.57% | 3.14% | 2.73% | -2.33% | 3.11% | 3.17% | 101% | 85% | #DIV/0! | 2%
Class D | 0.02% | 0.06% | 0.05% | 0.00% | 0.06% | 0.05% | 101% | 100% | #DIV/0! | 0%
Class F | 0.00% | 0.00% | 0.00% | 0.06% | -0.01% | 0.03% | 101% | 102% | #DIV/0! | 0%
 | Y-PSNR | U-PSNR | V-PSNR | Y-MSIM | U-MSIM | V-MSIM | EncT | DecT CPU | DecT GPU | bit DIFF
Class A1 | -3.48% | 2.23% | 3.71% | -6.91% | 0.83% | 0.87% | 78% | 54% | #DIV/0! | 4%
Class A2 | -1.55% | 7.82% | 6.70% | -4.61% | 8.45% | 6.82% | 86% | 73% | #DIV/0! | 2%
Class B | 0.08% | 1.83% | 1.27% | -1.06% | 1.88% | 1.31% | 97% | 89% | #DIV/0! | 0%
Class C | 0.00% | 0.00% | 0.00% | 0.00% | -0.07% | -0.03% | 100% | 99% | #DIV/0! | 0%
Class E |  |  |  |  |  |  |  |  |  | 
Overall | -0.98% | 2.62% | 2.50% | -2.66% | 2.46% | 1.97% | 92% | 80% | #DIV/0! | 1%
Class D | 0.00% | 0.00% | 0.00% | 0.03% | -0.01% | 0.03% | 100% | 101% | #DIV/0! | 0%
Class F | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 101% | 100% | #DIV/0! | 2%

## Slide 5: Additional experimental results (QP 27 ~ QP 47)
AI
RA
 | Y-PSNR | U-PSNR | V-PSNR | Y-MSIM | U-MSIM | V-MSIM | EncT | DecT CPU | DecT GPU | bit DIFF
Class A1 | -4.87% | 5.83% | 4.06% | -8.22% | 3.00% | 2.74% | 114% | 53% | #DIV/0! | 9%
Class A2 | -5.66% | 25.61% | 18.95% | -9.77% | 14.19% | 12.40% | 101% | 61% | #DIV/0! | 6%
Class B | 0.00% | 3.39% | 3.66% | -2.36% | 3.82% | 4.90% | 105% | 79% | #DIV/0! | 1%
Class C | 0.00% | -0.05% | -0.03% | -0.06% | -0.11% | -0.02% | 101% | 99% | #DIV/0! | 0%
Class E | 0.50% | 0.05% | 0.18% | -2.41% | 0.79% | 1.50% | 102% | 84% | #DIV/0! | 1%
Overall | -1.67% | 6.18% | 4.87% | -4.07% | 4.03% | 4.13% | 104% | 75% | #DIV/0! | 3%
Class D | 0.02% | 0.07% | 0.05% | -0.04% | 0.06% | -0.01% | 101% | 100% | #DIV/0! | 0%
Class F | 0.01% | -0.01% | 0.01% | 0.01% | -0.06% | -0.13% | 101% | 99% | #DIV/0! | 0%
 | Y-PSNR | U-PSNR | V-PSNR | Y-MSIM | U-MSIM | V-MSIM | EncT | DecT CPU | DecT GPU | bit DIFF
Class A1 | -7.22% | 3.40% | 3.85% | -10.97% | 1.61% | 0.59% | 76% | 43% | #DIV/0! | 5%
Class A2 | -4.17% | 19.43% | 16.12% | -9.00% | 18.23% | 15.89% | 79% | 57% | #DIV/0! | 3%
Class B | -0.43% | 3.75% | 3.11% | -2.42% | 3.63% | 3.35% | 95% | 82% | #DIV/0! | 1%
Class C | 0.00% | 0.00% | 0.00% | 0.00% | -0.05% | 0.01% | 100% | 100% | #DIV/0! | 0%
Class E |  |  |  |  |  |  |  |  |  | 
Overall | -2.42% | 5.82% | 5.03% | -4.80% | 5.16% | 4.42% | 89% | 71% | #DIV/0! | 2%
Class D | 0.00% | 0.00% | 0.00% | 0.01% | 0.00% | 0.03% | 100% | 101% | #DIV/0! | 0%
Class F | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 102% | 99% | #DIV/0! | 0%

## Slide 6: Conclusion
In this contribution, we proposed to determine encoding resolution for RPR
  Half and 2/3 of the original picture size
  To select the optimal resolution among candidates for the better coding performance
In the future, the proposed scheme could further be extended to select an arbitrary resolution for the better coding performance
Thank Ericsson for crosscheck