## Slide 1: AHG9: Complexity description for NNR post-filter SEI message
JVET-Y0075
Sharp Corporation
Keiichiro Takada, Yukinobu Yasugi, Takeshi Chujoh and Tomohiro Ikai

## Slide 2: Introduction
Copyright © All rights reserved, SHARP CORPORATION
This contribution proposes an NNR post-filter SEI message based on JVET-X0112 [1].
PROBLEM STATEMENT
There is no simple means to decide the applicability of the neural network model specified by the URI or payload in the SEI.
In order to obtain the complexity of the neural network necessary to determine the applicability, the topology of the neural network model must be analyzed.
PROPOSAL
Add information on the complexity and precision of neural network based post-filters.
[1] Miska M. Hannuksela, Emre B. Aksu, Francesco Cricri, Hamed R. Tavakoli and Maria Santamaria, “AHG9: On post-filter SEI,” Joint Video Experts Team Document, JVET-X0112, teleconference, Oct. 2021.

## Slide 3: NNR post-filter SEI message syntax
nnr_post_filter( payloadSize ) { | Descriptor
nnrpf_id | u(21)
nnrpf_mode_idc | u(2)
if( nnrpf_mode_idc > 0 ) { | 
nnrpf_persistence_flag | u(1)
nnrpf_parameter_type_idc | u(4)
nnrpf_num_parameters_idc | u(8)
nnrpf_num_kmac_operations_idc | ue(v)
while( !byte_aligned( ) ) | 
nnrpf_alignment_zero_bit /* equal to 0 */ | f(1)
} | 
if( nnrpf_mode_idc = = 1 ) { | 
i = 0 | 
do | 
nnrpf_uri[ i ] | b(8)
while( nnrpf_uri[ i++ ] != 0 ) | 
} | 
if( nnrpf_mode_idc = = 2 ¦ ¦ nnrpf_mode_idc = = 3 ) { | 
for( i = 0; i < payloadSize − 3 ; i++ ) | 
nnrpf_payload_byte[ i ] | b(8)
} | 
} | 
Copyright © All rights reserved, SHARP CORPORATION
NNR post-filter SEI message syntax
The additional relative to JVET-X0112 are highlighted as yellow marker.
nnrpf_parameter_type_idc specifies the most complex variable type of neural network parameters.
nnrpf_num_parameters_idc specifies the maximum number of neural network parameters for the post processing filter in units of a power of 2048.
value | the most complex variable type
0 | only integer parameters
1 | floating point parameters or integer parameters
value | the maximum number of neural network parameters
0 | not specified
non-zero | (2048 << nnrpf_num_parameters_idc) − 1
nnrpf_num_kmac_operations_idc specifies the maximum number of operations per pixel of the post-processing filter.
value | the number of MAC operation (multiply-accumulate) per pixel
0 | not specified
non-zero | nnrpf_num_kmac_operations_idc * 1000
nnrpf_alignment_zero_bit shall be equal to 0.