## Slide 1: JVET-Y0102 On the balance of ECM coding gains between luma and chroma
F.Le Léannec, P.Andrivon, E.Thomas,

## Slide 2: Observation
ECM coding gains over VVC are significantly higher in chroma than in luma
 | All Intra Main 10 |  |  |  | 
 | Over VTM-14.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -6.98% | -12.44% | -16.63% | 290% | 248%
Class A2 | -6.44% | -13.13% | -11.99% | 277% | 235%
Class B | -6.05% | -13.75% | -14.21% | 276% | 240%
Class C | -7.06% | -10.21% | -10.67% | 269% | 225%
Class E | -7.58% | -11.55% | -12.41% | 263% | 259%
Overall | -6.75% | -12.28% | -13.16% | 275% | 240%
Class D | -5.86% | -8.45% | -8.23% | 265% | 225%
Class F | -10.80% | -15.69% | -15.66% | 193% | 285%
Class TGM | -15.62% | -18.73% | -18.25% | 265% | 431%
 | Low delay B Main 10 |  |  |  | 
 | Over VTM-14.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -12.28% | -24.89% | -24.11% | 258% | 373%
Class C | -12.51% | -18.81% | -18.94% | 264% | 329%
Class E | -12.11% | -17.24% | -19.15% | 248% | 372%
Overall | -12.31% | -20.95% | -21.14% | 257% | 357%
Class D | -14.09% | -20.17% | -19.36% | 254% | 342%
Class F | -12.15% | -18.99% | -18.67% | 246% | 389%
Class TGM | -14.02% | -21.79% | -22.13% | #NOMBRE! | #NOMBRE!
 | Random Access Main 10 |  |  |  | 
 | Over VTM-14.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -14.95% | -16.42% | -21.85% | 347% | 541%
Class A2 | -15.84% | -20.38% | -20.42% | 339% | 604%
Class B | -13.57% | -19.94% | -19.32% | 315% | 540%
Class C | -15.35% | -17.27% | -16.98% | 321% | 487%
Class E |  |  |  |  | 
Overall | -14.77% | -18.61% | -19.42% | 327% | 538%
Class D | -16.10% | -17.65% | -16.99% | 319% | 501%
Class F | -13.54% | -18.02% | -17.76% | 274% | 429%
Class TGM | -14.65% | -18.96% | -19.20% | 302% | 323%

## Slide 3: Proposal
Balance the luma and chroma gains
2 proposed configurations to modify ECM CTCs:
 | AI | RA | LDB
ECM-3.1 QpInValCb | 17 27 32 44 | 17 22 34 42 | 17 22 34 42
ECM-3.1 QpOutValCb | 17 29 34 41 | 17 23 35 39 | 17 23 35 39
proposed config 1 | 17 30 35 42 | 17 23 36 40 | 17 24 36 40
proposed config 2 | 17 29 35 42 | 17 23 35 41 | 17 23 36 40

## Slide 4: Results: AI
AI
 | All Intra Main 10 |  |  |  | 
 | Over VTM-14.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -6.98% | -12.44% | -16.63% | 290% | 248%
Class A2 | -6.44% | -13.13% | -11.99% | 277% | 235%
Class B | -6.05% | -13.75% | -14.21% | 276% | 240%
Class C | -7.06% | -10.21% | -10.67% | 269% | 225%
Class E | -7.58% | -11.55% | -12.41% | 263% | 259%
Overall | -6.75% | -12.28% | -13.16% | 275% | 240%
Class D | -5.86% | -8.45% | -8.23% | 265% | 225%
Class F | -10.80% | -15.69% | -15.66% | 193% | 285%
Class TGM | -15.62% | -18.73% | -18.25% | 265% | 431%
 | All Intra Main 10 |  |  |  | 
 | Over VTM-11.0 + V0056 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -8.49% | -0.75% | -8.01% | 287% | 248%
Class A2 | -9.03% | -2.60% | -2.27% | 272% | 233%
Class B | -7.01% | -3.62% | -3.22% | 274% | 240%
Class C | -8.08% | -0.75% | -1.03% | 265% | 225%
Class E | -8.34% | -2.99% | -3.44% | 259% | 266%
Overall | -8.05% | -2.23% | -3.41% | 271% | 241%
Class D | -6.82% | 1.17% | 1.58% | 262% | 228%
Class F | -11.86% | -8.95% | -9.01% | 192% | 287%
Class TGM | -17.28% | -16.59% | -16.04% | 196% | 321%
 | All Intra Main 10 |  |  |  | 
 | Over VTM-11.0+V0056 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -7.65% | -7.87% | -13.30% | 289% | 249%
Class A2 | -7.40% | -9.55% | -8.78% | 275% | 235%
Class B | -6.41% | -9.39% | -8.90% | 275% | 241%
Class C | -7.50% | -5.69% | -5.77% | 268% | 225%
Class E | -7.98% | -6.94% | -7.64% | 262% | 260%
Overall | -7.29% | -7.93% | -8.71% | 273% | 241%
Class D | -6.29% | -3.72% | -3.28% | 265% | 227%
Class F | -11.26% | -12.41% | -12.38% | 193% | 287%
Class TGM | -16.28% | -17.74% | -17.30% | 196% | 321%
Proposed config 1
Proposed config 2
Current ECM-3.1 config

## Slide 5: Results: RA
RA
Proposed config 1
Proposed config 2
 | Random Access Main 10 |  |  |  | 
 | Over VTM-14.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -14.95% | -16.42% | -21.85% | 347% | 541%
Class A2 | -15.84% | -20.38% | -20.42% | 339% | 604%
Class B | -13.57% | -19.94% | -19.32% | 315% | 540%
Class C | -15.35% | -17.27% | -16.98% | 321% | 487%
Class E |  |  |  |  | 
Overall | -14.77% | -18.61% | -19.42% | 327% | 538%
Class D | -16.10% | -17.65% | -16.99% | 319% | 501%
Class F | -13.54% | -18.02% | -17.76% | 274% | 429%
Class TGM | -14.65% | -18.96% | -19.20% | 302% | 323%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-11.0 + V0056 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -16.44% | -8.48% | -16.84% | 346% | 544%
Class A2 | -17.29% | -14.32% | -14.90% | 338% | 602%
Class B | -14.01% | -12.66% | -11.70% | 317% | 543%
Class C | -15.85% | -10.22% | -9.63% | 322% | 490%
Class E |  |  |  |  | 
Overall | -15.64% | -11.51% | -12.82% | 328% | 540%
Class D | -16.52% | -10.82% | -9.94% | 320% | 506%
Class F | -14.38% | -12.93% | -12.52% | 273% | 430%
Class TGM | -15.96% | -16.59% | -16.80% | 302% | 346%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-11.0+V0056 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -16.05% | -13.78% | -20.74% | 346% | 542%
Class A2 | -16.28% | -19.47% | -19.42% | 337% | 601%
Class B | -13.73% | -18.53% | -17.70% | 316% | 544%
Class C | -15.51% | -15.95% | -15.43% | 322% | 490%
Class E |  |  |  |  | 
Overall | -15.18% | -17.08% | -18.05% | 328% | 539%
Class D | -16.24% | -16.63% | -15.78% | 319% | 505%
Class F | -13.87% | -16.59% | -16.11% | 273% | 431%
Class TGM | -15.38% | -17.83% | -18.18% | 294% | 329%
Current ECM-3.1 config

## Slide 6: Results: LDB
LDB
Proposed config 1
Proposed config 2
Current ECM-3.1 config
 | Low delay B Main 10 |  |  |  | 
 | Over VTM-11.0 + V0056 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -12.98% | -10.74% | -8.64% | 259% | 372%
Class C | -13.43% | -3.76% | -3.75% | 264% | 356%
Class E | -12.47% | -2.40% | -5.23% | 248% | 405%
Overall | -13.00% | -6.33% | -6.16% | 258% | 374%
Class D | -14.68% | -5.15% | -4.00% | 254% | 347%
Class F | -13.48% | -9.28% | -8.63% | 246% | 419%
Class TGM | -15.69% | -17.99% | -18.55% | 276% | 352%
 | Low delay B Main 10 |  |  |  | 
 | Over VTM-14.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -12.28% | -24.89% | -24.11% | 258% | 373%
Class C | -12.51% | -18.81% | -18.94% | 264% | 329%
Class E | -12.11% | -17.24% | -19.15% | 248% | 372%
Overall | -12.31% | -20.95% | -21.14% | 257% | 357%
Class D | -14.09% | -20.17% | -19.36% | 254% | 342%
Class F | -12.15% | -18.99% | -18.67% | 246% | 389%
Class TGM | -14.02% | -21.79% | -22.13% | #NOMBRE! | #NOMBRE!
 | Low delay B Main 10 |  |  |  | 
 | Over VTM-11.0+V0056 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -12.84% | -13.60% | -11.86% | 260% | 371%
Class C | -13.24% | -7.13% | -7.08% | 266% | 329%
Class E | -12.45% | -6.96% | -10.05% | 249% | 372%
Overall | -12.88% | -9.79% | -9.81% | 259% | 357%
Class D | -14.58% | -8.31% | -7.89% | 256% | 344%
Class F | -13.18% | -11.16% | -10.26% | 247% | 391%
Class TGM | -15.38% | -18.73% | -19.19% | 278% | 345%

## Slide 7: Results: impact on ECM-3.1
Proposed config 1
Proposed config 2
 | All Intra Main 10 |  |  |  | 
 | Over ECM-3.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -1.62% | 13.97% | 10.58% | 99% | 100%
Class A2 | -2.78% | 12.84% | 11.29% | 98% | 99%
Class B | -1.03% | 12.27% | 12.98% | 99% | 100%
Class C | -1.10% | 10.62% | 10.81% | 99% | 100%
Class E | -0.83% | 9.79% | 10.57% | 99% | 103%
Overall | -1.40% | 11.87% | 11.42% | 99% | 100%
Class D | -1.03% | 10.42% | 10.52% | 99% | 101%
Class F | -1.20% | 8.14% | 8.05% | 99% | 101%
Class TGM | -2.03% | 2.77% | 2.88% | 74% | 75%
 | Random Access Main 10 |  |  |  | 
 | Over ECM-3.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -1.70% | 9.21% | 6.39% | 100% | 101%
Class A2 | -1.67% | 7.66% | 6.78% | 100% | 100%
Class B | -0.50% | 8.73% | 9.06% | 101% | 101%
Class C | -0.58% | 8.21% | 8.53% | 100% | 101%
Class E |  |  |  |  | 
Overall | -1.00% | 8.47% | 7.93% | 100% | 100%
Class D | -0.49% | 7.82% | 7.97% | 101% | 101%
Class F | -0.95% | 6.09% | 6.24% | 100% | 100%
Class TGM | -1.52% | 3.03% | 3.14% | 100% | 107%
 | Low delay B Main 10 |  |  |  | 
 | Over ECM-3.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.80% | 19.45% | 21.21% | 100% | 100%
Class C | -1.06% | 18.68% | 18.91% | 100% | 108%
Class E | -0.42% | 18.31% | 17.48% | 100% | 109%
Overall | -0.79% | 18.91% | 19.51% | 100% | 105%
Class D | -0.67% | 18.96% | 19.05% | 100% | 101%
Class F | -1.52% | 12.31% | 12.70% | 100% | 108%
Class TGM | -1.97% | 5.43% | 5.43% | #DIV/0! | #DIV/0!
 | All Intra Main 10 |  |  |  | 
 | Over ECM-3.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.70% | 4.92% | 3.57% | 100% | 100%
Class A2 | -1.00% | 3.81% | 3.23% | 99% | 100%
Class B | -0.37% | 4.56% | 5.51% | 100% | 100%
Class C | -0.46% | 4.51% | 4.88% | 100% | 100%
Class E | -0.43% | 4.72% | 5.03% | 100% | 101%
Overall | -0.56% | 4.51% | 4.58% | 100% | 100%
Class D | -0.45% | 4.60% | 4.78% | 100% | 101%
Class F | -0.50% | 3.51% | 3.53% | 100% | 101%
Class TGM | -0.76% | 1.16% | 1.11% | 74% | 75%
 | Random Access Main 10 |  |  |  | 
 | Over ECM-3.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -1.21% | 2.83% | 1.20% | 100% | 100%
Class A2 | -0.50% | 1.05% | 1.04% | 100% | 100%
Class B | -0.18% | 1.42% | 1.68% | 100% | 101%
Class C | -0.18% | 1.34% | 1.57% | 100% | 101%
Class E |  |  |  |  | 
Overall | -0.45% | 1.60% | 1.43% | 100% | 100%
Class D | -0.15% | 1.02% | 1.27% | 100% | 101%
Class F | -0.37% | 1.57% | 1.77% | 100% | 101%
Class TGM | -0.83% | 1.28% | 1.23% | 97% | 102%
 | Low delay B Main 10 |  |  |  | 
 | Over ECM-3.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.64% | 14.39% | 15.44% | 100% | 100%
Class C | -0.83% | 13.68% | 13.91% | 101% | 100%
Class E | -0.40% | 11.98% | 10.68% | 100% | 100%
Overall | -0.64% | 13.55% | 13.74% | 101% | 100%
Class D | -0.55% | 14.08% | 13.42% | 101% | 100%
Class F | -1.14% | 9.20% | 9.89% | 101% | 100%
Class TGM | -1.54% | 3.96% | 4.06% | #DIV/0! | #DIV/0!

## Slide 8: Conclusion
Propose to balance luma/chroma gains of ECM by shifting some chroma gains to luma
Achieved through adjusting the chroma QP mapping tables for AI, RA, LDB
Suggested configs from these tests are:
  Configuration 1 for AI and RA
  Configuration 2 for LDB
  AI: -1.4% / 11.9% / 11.4% ; RA: -1% ; 8.5% ; 7.9% ; LB: -0.64% / 13.55% / 13.74%
Related contributions at this meeting:
  JVET-Y0113 varies chroma residual scaling
  JVET-Y0223 combines Y0102 and Y0113