## Slide 1: JVET-Y0128 Non-EE2: fixing issues for RPR enabling and non-CTC configuration in ECM
Zhi Zhang, Han Huang, Chun-Chi Chen,
Vadim Seregin, Marta Karczewicz (Qualcomm)
Philippe Bordes (InterDigital)

## Slide 2: Introduction
        Merge Request 47 (MR47) : fix RPR_ENABLE for TMVP when all ref are scaled and with X0049, X0083
        Adaptive DMVR and BM AMVP-merge mode enabling condition
At least one unscaled reference picture is from the past of the current picture
At least one unscaled reference picture is from the future of the current picture

## Slide 3: Problem
        Adaptive DMVR flag and BM AMVP-merge flag is signaled regardless of the enabling condition is fulfilled or not
Redundant signaling
        Merge list construction regardless of the enabling condition is fulfilled or not
Zero padding of adaptive DMVR may not fulfill the enabling condition
Merge candidates of AMVP-merge mode may not fulfill the enabling condition
        LIC and TM-AMVP
LIC flag is signaled when reference picture is scaled
TM-AMVP using scaled reference picture to select and refine MVP by using Template Matching

## Slide 4: Proposal
        Slice level enabling condition check for Adaptive DMVR and BM AMVP-merge
Avoid redundant flag signaling
Checking the enabling condition when constructing merge list
        LIC flag is not signaled when reference picture is scaled
        TM-AMVP mode is disabled when reference picture is scaled, MVP index is signaled instead of selecting by Template Matching

## Slide 5: Simulations
Configuration 1: (Each frame is scaled) |  | Configuration 2: (Resolution switch after every 16 frames) | 
ScalingRatioHor | 2.0 | ScalingRatioHor | 2.0
ScalingRatioVer | 2.0 | ScalingRatioVer | 2.0
FractionNumFrames | 1.0 | FractionNumFrames | 1.0
RPR | 1 | RPR | 1
UpscaledOutput | 2 | UpscaledOutput | 1
SwitchPocPeriod | -1 | SwitchPocPeriod | 16
        PSNR1 values output from ECM software: measured on the decoded picture size by calculating MSE for each picture, accumulating MSEs for all pictures and calculating average PSNR from the accumulated MSE.
        PSNR2 values output from ECM software: measured after up-sampling of the decoded picture if the decoded picture size is in smaller resolution.

## Slide 6: Simulation 4.1 and 4.2 report PSNR1 results QPs { 22, 27, 32, 37 } Anchor is ECM3.1 CTC full size
 | Random Access |  |  |  | 
 | Over ECM-3.1 CTC |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -60.27% | -42.22% | -34.68% | 25% | 28%
Class A2 | -56.36% | -72.64% | -66.13% | 25% | 28%
Class B | -57.66% | -61.74% | -49.38% | 26% | 28%
Class C | -61.10% | -56.30% | -49.23% | 28% | 29%
Class E |  |  |  |  | 
Overall | -58.84% | -58.57% | -49.75% | 26% | 28%
Class D | -62.49% | -54.73% | -50.66% | 25% | 31%
Class F | -36.53% | -37.82% | -35.33% | 34% | 28%
 | Low-delay B |  |  |  | 
 | Over ECM-3.1 CTC |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -56.53% | -57.90% | -43.80% | 28% | 26%
Class C | -62.86% | -55.52% | -46.97% | 26% | 27%
Class E | -51.43% | -37.90% | -35.36% | 30% | 24%
Overall | -57.37% | -52.10% | -42.75% | 28% | 26%
Class D | -62.91% | -54.02% | -46.58% | 24% | 27%
Class F | -36.95% | -30.20% | -27.80% | 32% | 27%
Configuration 1
Configuration 2
 | Low-delay B |  |  |  | 
 | Over ECM-3.1 CTC |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -31.29% | -40.69% | -27.05% | 83% | 68%
Class C | -28.04% | -27.17% | -17.90% | 69% | 68%
Class E | -28.35% | -29.92% | -29.05% | 84% | 67%
Overall | -29.47% | -33.49% | -24.50% | 78% | 68%
Class D | -27.32% | -28.98% | -20.95% | 69% | 67%
Class F | -6.86% | -8.14% | -5.09% | 81% | 72%
 | Random Access |  |  |  | 
 | Over ECM-3.1 CTC |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -33.79% | -16.41% | -12.28% | 68% | 64%
Class A2 | -26.64% | -48.70% | -38.52% | 69% | 65%
Class B | -30.31% | -42.36% | -28.62% | 69% | 64%
Class C | -21.37% | -23.98% | -15.89% | 68% | 64%
Class E |  |  |  |  | 
Overall | -27.89% | -33.54% | -23.94% | 69% | 64%
Class D | -21.31% | -22.23% | -16.48% | 70% | 66%
Class F | -5.02% | -7.79% | -5.54% | 76% | 67%

## Slide 7: Simulation 4.3 and 4.4 report PSNR2 results QPs { 22, 27, 32, 37, 42 } Anchor is ECM3.1 CTC full size
Configuration 1
Configuration 2
 | Random Access |  |  |  | 
 | Over ECM-3.1 CTC |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.32% | 25.09% | 20.87% | 26% | 28%
Class A2 | 18.88% | 81.32% | 48.85% | 26% | 27%
Overall | 9.60% | 53.20% | 34.86% | 26% | 28%
 | Random Access |  |  |  | 
 | Over ECM-3.1 CTC |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 16.52% | 22.69% | 22.94% | 68% | 64%
Class A2 | 30.65% | 39.72% | 39.23% | 70% | 65%
Overall | 23.58% | 31.21% | 31.09% | 69% | 64%
Simulation 4.5 report PSNR2 results Suggested QP selection as in JVET-Y0061
 | Random Access |  |  |  |  |  |  |  |  | 
 | ECM-3.1 RPR enabling Over ECM-3.1 CTC |  |  |  |  | JVET-Y0128 RPR enabling Over ECM-3.1 CTC |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -1.66% | 3.40% | 5.11% | 71% | 61% | -1.66% | 3.42% | 5.11% | 71% | 61%
Class A2 | -0.37% | 15.96% | 10.96% | 79% | 73% | -0.37% | 15.95% | 10.95% | 79% | 73%
Overall | -1.01% | 9.68% | 8.03% | 75% | 67% | -1.02% | 9.68% | 8.03% | 75% | 67%
Configuration 1