## Slide 1: JVET-Y0130 EE2-related : Unification of availability check for intra mode coding
Sunmi Yoo, Hyeongmun Jang, Junghak Nam, Jangwon Choi, Jaehyun Lim, Seung-Hwan Kim

## Slide 2: Summary
Proposal
  Unification of availability check for above neighbor intra modes
    Method #1 : Using the above intra modes only within the CTU boundary
    Method #2 : No restriction to use above neighbor intra modes
  No coding performance impact, but method #1 can be aligned with what is done in the previous video coding standards.
Experimental results
  Method #1 : 0.01%, -0.05%, -0.05% (Y/U/V AI) / 0.01%, 0.04%, 0.11% (Y/U/V RA)
  Method #2 : -0.01%, -0.011%, -0.03% (Y/U/V AI) / 0.01%, 0.04%, 0.09% (Y/U/V RA)
  No significant difference in EncT / DecT
Thank Bytedance for crosscheck

## Slide 3: Problem statement
For some of above neighbor candidates newly considered in ECM, they can be included without being checked whether they are within the current CTU.
  Case #1 : In MPM, the order is adaptive for left and above modes according to the block shape, but the CTU boundary check is done only for the secondly checked neighbor mode.
MPM List
A
L
A
L
CTU boundary
A
L
A
L
CTU boundary
MPM List
When block width > block height (as the way done in VVC) :
A
L
A
L
CTU boundary
A
L
A
L
CTU boundary
MPM List
MPM List
When block width <= block height :

## Slide 4: Problem statement
For some of above neighbor candidates newly considered in ECM, they can be included without being checked whether they are within the current CTU.
  Case #2 : In TIMD, intra modes from right above and left above neighbors can be used when they are out of the current CTU, whereas the above neighbor mode is not considered.
A
L
A
L
AR
AL
BL
CTU boundary
BL
AR
AL
TIMD candidates

## Slide 5: Problem statement
Intra block
For some of above neighbor candidates newly considered in ECM, they can be included without being checked whether they are within the current CTU.
  Case #3 : In MPM, propagated intra modes in inter block (IPM) can be always included without any CTU boundary condition check.
Inter block
Inter block
Inter block
A
L
A
L
AR
AL
BL
CTU boundary
BL
AR
AL
MPM List

## Slide 6: Proposed method
In the latest video coding standards, the above neighbor intra modes from the other CTUs are not considered.
  If the intra modes above CTU boundary are used, the intra modes should be kept in the line buffer memory.
The unified CTU boundary check is proposed in method #1.
  For the above, above-right, and above-left candidates, it is checked if they are in the same CTU.
  For the left candidate, it is always considered regardless of the CTU boundary and the block shape.
The maximal performance from the neighbor modes is shown in method #2.

## Slide 7: Experimental results
Method #1
Method #2
 | All Intra Main 10 |  |  |  | 
 | Over ECM-3.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | -0.14% | 0.02% | 98% | 99%
Class A2 | -0.01% | 0.06% | 0.03% | 99% | 99%
Class B | 0.00% | -0.03% | -0.14% | 99% | 100%
Class C | 0.00% | 0.03% | -0.09% | 98% | 99%
Class E | 0.04% | -0.22% | -0.01% | 99% | 98%
Overall | 0.01% | -0.05% | -0.05% | 98% | 99%
Class D | 0.02% | 0.07% | -0.06% | 99% | 99%
Class F | 0.03% | 0.04% | -0.06% | 101% | 100%
 | Random Access Main 10 |  |  |  | 
 | Over ECM-3.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | -0.01% | -0.09% | 99% | 101%
Class A2 | 0.00% | 0.06% | 0.07% | 100% | 101%
Class B | 0.02% | 0.02% | 0.08% | 99% | 100%
Class C | 0.02% | 0.11% | 0.32% | 99% | 100%
Class E |  |  |  |  | 
Overall | 0.01% | 0.04% | 0.11% | 99% | 100%
Class D | 0.00% | 0.01% | -0.14% | 99% | 99%
Class F | 0.02% | 0.19% | 0.02% | 97% | 99%
 | All Intra Main 10 |  |  |  | 
 | Over ECM-3.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.06% | -0.04% | 98% | 99%
Class A2 | -0.01% | 0.02% | 0.05% | 98% | 99%
Class B | -0.01% | -0.03% | -0.11% | 98% | 99%
Class C | -0.01% | -0.02% | -0.01% | 97% | 98%
Class E | 0.00% | -0.09% | 0.03% | 97% | 97%
Overall | -0.01% | -0.01% | -0.03% | 98% | 98%
Class D | 0.01% | 0.04% | -0.11% | 98% | 98%
Class F | 0.01% | 0.15% | 0.01% | 101% | 101%
 | Random Access Main 10 |  |  |  | 
 | Over ECM-3.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.02% | 0.03% | -0.17% | 98% | 98%
Class A2 | -0.02% | 0.01% | -0.06% | 99% | 99%
Class B | 0.00% | 0.05% | 0.21% | 100% | 99%
Class C | -0.01% | 0.07% | 0.25% | 100% | 100%
Class E |  |  |  |  | 
Overall | 0.00% | 0.04% | 0.09% | 99% | 99%
Class D | 0.00% | 0.20% | -0.09% | 100% | 100%
Class F | 0.02% | 0.01% | -0.25% | 100% | 100%

## Slide 8: Conclusion
The unified availability check for neighbor intra modes is proposed.
From the result of method #2, the performance of using the neighbor modes from the out of the current CTU is negligible.
It is suggested that method #1 is adopted to the next version of ECM.

## Slide 9
Thank you