## Slide 1: JVET-Y0131 EE2-related : Clean-up on DIMD
Sunmi Yoo, Hyeongmun Jang, Junghak Nam, Jangwon Choi, Jaehyun Lim, Seung-Hwan Kim

## Slide 2: Summary
Proposal
  To avoid for an intra mode being coded in the multiple ways.
    Method #1 : Always blending the DIMD predictor with planar prediction block
    Method #2 : Set DC as DIMD default mode on top of method #1
Experimental result
  Method #1
    AI : 0.00% / -0.05% / -0.02% (Y/U/V)
    RA : 0.00% / 0.05% / 0.04% (Y/U/V)
  Method #2
    AI : 0.00% / -0.04% / 0.03% (Y/U/V)
    RA : 0.00% / 0.00% / 0.08% (Y/U/V)
  No impact on complexity
Thank Kwai for crosscheck

## Slide 3: Problem statement
In ECM, there are multi paths to code the same intra prediction mode when only one intra prediction mode is derived in the DIMD process.
  How to code directional intra mode in ECM
    If there is only one mode derived from the neighbor pixels, this predictor is not combined with the planar predictor.
DIMD?
First mode
available?
MPM?
Planar
(DIMD default mode)
Planar
mode?
Planar
…
…
Second mode
available?
YES
NO
YES
NO
YES
NO
…
YES
NO
YES
NO
Intra mode (MODE_32)
Intra mode (MODE_32)
: Path to code MODE_32
…

## Slide 4: Proposed method #1
Always combining planar prediction block to intra predictor(s) is proposed
  It modifies the prediction block when the intra mode is same in the different paths.
: Path to code MODE_32
DIMD?
First mode
available?
MPM?
Planar
(DIMD default mode)
Planar
mode?
Planar
…
…
Second mode
available?
YES
NO
YES
NO
YES
NO
…
YES
NO
YES
NO
Intra mode (MODE_32)
: Path to code MODE_32
Blend mode
(MODE_32 + PLANAR)
…

## Slide 5: Problem statement
In ECM, there are multi paths to code the same intra prediction mode when only one intra prediction mode is derived in the DIMD process.
  How to code planar mode in ECM
    If there is no neighbor pixel or no gradient found from the neighbor pixels, the planar mode is set to the DIMD intra mode as default.
    Since the planar mode is always included in the MPM list, there are two paths to code planar mode.
DIMD?
First mode
available?
MPM?
Planar
(DIMD default mode)
Planar
mode?
Planar
…
…
…
YES
NO
YES
NO
YES
NO
…
YES
NO
: Path to code planar

## Slide 6: Proposed method #2
On top of method #1, the default DIMD intra mode is initialized to DC.
  It modifies the prediction block when the DIMD intra mode is not available.
DIMD?
First mode
available?
MPM?
Planar
mode?
Planar
…
…
…
YES
NO
YES
NO
YES
NO
…
YES
NO
Blend mode
(DC + Planar)
*DIMD default mode
: Path to code planar

## Slide 7: Experimental results
Method #1
Method #2
 | All Intra Main 10 |  |  |  | 
 | Over ECM-3.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | -0.06% | -0.05% | 101% | 101%
Class A2 | 0.00% | -0.01% | 0.01% | 100% | 100%
Class B | 0.00% | -0.10% | -0.04% | 100% | 100%
Class C | 0.00% | 0.04% | 0.06% | 101% | 100%
Class E | 0.00% | -0.10% | -0.07% | 100% | 101%
Overall | 0.00% | -0.05% | -0.02% | 100% | 100%
Class D | 0.00% | 0.11% | -0.03% | 100% | 99%
Class F | 0.05% | 0.03% | -0.02% | 100% | 102%
 | Random Access Main 10 |  |  |  | 
 | Over ECM-3.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | 0.04% | -0.08% | 100% | 100%
Class A2 | -0.01% | 0.18% | 0.03% | 100% | 101%
Class B | 0.02% | 0.07% | 0.13% | 100% | 99%
Class C | -0.02% | -0.09% | 0.02% | 99% | 99%
Class E |  |  |  |  | 
Overall | 0.00% | 0.05% | 0.04% | 100% | 100%
Class D | 0.03% | 0.13% | 0.12% | 100% | 99%
Class F | 0.00% | 0.06% | 0.03% | 98% | 98%
 | All Intra Main 10 |  |  |  | 
 | Over ECM-3.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | -0.12% | 0.02% | 101% | 100%
Class A2 | 0.00% | 0.05% | 0.02% | 102% | 101%
Class B | -0.01% | -0.03% | 0.02% | 101% | 101%
Class C | 0.00% | 0.01% | 0.09% | 100% | 100%
Class E | 0.00% | -0.15% | -0.04% | 100% | 100%
Overall | 0.00% | -0.04% | 0.03% | 101% | 100%
Class D | 0.01% | 0.04% | -0.12% | 102% | 99%
Class F | 0.04% | 0.14% | -0.01% | 101% | 101%
 | Random Access Main 10 |  |  |  | 
 | Over ECM-3.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | 0.01% | -0.12% | 101% | 101%
Class A2 | 0.01% | 0.11% | 0.14% | 101% | 101%
Class B | 0.00% | -0.06% | 0.10% | 99% | 99%
Class C | -0.01% | 0.00% | 0.15% | 100% | 100%
Class E |  |  |  |  | 
Overall | 0.00% | 0.00% | 0.08% | 100% | 100%
Class D | 0.03% | 0.14% | -0.03% | 100% | 99%
Class F | -0.01% | 0.04% | -0.20% | 100% | 100%

## Slide 8: Conclusion
It is proposed to combine planar prediction block to the intra predictor when only one derived DIMD intra mode is available.
  It is avoidable to code an intra mode in the different ways.
  Initializing the DIMD intra mode to DC (method #2) can completely prevent the problem.
It is suggested to adopt the proposal to the next version of ECM.

## Slide 9
Thank you