## Slide 1: Non-EE2: DIMD Flag Signaling Clean-up (JVET-Y0144)
Jie Zhao and Seung Hwan Kim
LG Electronics

## Slide 2: Introduction
In ECM3.1, the signaling position of dimd_flag is separated from other intra mode related syntax elements, and it unnecessarily complicates the software and signalling logic.
This contribution proposes to change the signaling position of dimd_flag, and place it right before timd_flag.
It is asserted that this change makes the code and signalling logic cleaner, and consistent with other intra syntax elements.
It has little impact on coding performance.

## Slide 3: Background: DIMD signalling in ECM3.1
// Decoder: CABACReader.cpp
void CABACReader::coding_unit( CodingUnit &cu, Partitioner &partitioner, CUCtx& cuCtx )
{ ..
// prediction mode and partitioning data
pred_mode ( cu );
cu_dimd_flag( cu );
if (CU::isIntra(cu))
{
adaptive_color_transform(cu);
}
if (CU::isPLT(cu))
{ ..
cu_palette_info ..
..
return;
}
// prediction data ( intra prediction modes / reference indexes + motion vectors )
cu_pred_data( cu );
..
}
All other intra mode related syntax elements are located inside function cu_pred_data() which includes the function intra_luma_pred_mode()

## Slide 4: Background: DIMD signalling in ECM3.1
// EncCU.cpp
bool EncCu::xCheckRDCostIntra ..
{
..
m_CABACEstimator->pred_mode ( cu );
m_CABACEstimator->cu_dimd_flag ( cu );
m_CABACEstimator->adaptive_color_transform(cu);
m_CABACEstimator->cu_pred_data ( cu );
..
}
All other intra mode related syntax elements are located inside function cu_pred_data() which includes the function intra_luma_pred_mode().
There is more than one such places in ECM3.1. In addition, it seems that rate of dimd_flag bit is missed in some other part of RD decision, such as xFracModeBitsIntra().
Basically, there is no reason that the dimd_flag is at such a special location different from other intra mode syntax elements.
Its current position unnecessarily complicates the code and signalling logic.

## Slide 5: Proposed Changes
Propose to move the dimd_flag signalling to be right before timd_flag. This simple change would make the code cleaner, and consistent with timd_flag signalling.
Putting dimd_flag and timd_flag next to each other also have the potential benefit for easier DIMD and TIMD flag joint signalling if in the future DIMD and TIMD get harmonized.
Signaling Order in ECM3.1 | Proposed signaling order
dimd_flag ACT PLT BDPCM TM (template matching) MIP timd_flag MRL … | dimd_flag ACT PLT BDPCM TM MIP dimd_flag timd_flag MRL …

## Slide 6: Syntax Tables
Currently, there is no spec text yet. The syntax table corresponding to ECM3.1 would be as shown in the table.
Blue highlighted are deletions, and green high lighted are additions.
coding_unit( x0, y0, cbWidth, cbHeight, cqtDepth, treeType, modeType ) { | Descriptor
if( CuPredMode[ chType ][ x0 ][ y0 ] = = MODE_INTRA && sps_palette_enabled_flag && … ) ) | 
pred_mode_plt_flag | ae(v)
if (CuPredMode[ chType ][ x0 ][ y0 ] = = MODE_INTRA && sps_dimd_enable_flag ) | 
intra_dimd_flag | ae(v)
if( CuPredMode[ chType ][ x0 ][ y0 ] = = MODE_INTRA && … ) | 
cu_act_enabled_flag | ae(v)
… | 
if( treeType = = SINGLE_TREE ¦ ¦ treeType = = DUAL_TREE_LUMA ) { | 
if( pred_mode_plt_flag ) | 
palette_coding( x0, y0, cbWidth, cbHeight, treeType ) | 
else { | 
if( sps_bdpcm_enabled_flag && && cbWidth <= MaxTsSize && cbHeight <= MaxTsSize && && !intra_dimd_flag ) | 
intra_bdpcm_luma_flag | ae(v)
if( intra_bdpcm_luma_flag ) | 
intra_bdpcm_luma_dir_flag | ae(v)
else { | 
if( sps_tmp_enable_flag && cbWidth <= TMP_MaxSize && cbHeight <= TMP_MaxSize && !intra_dimd_flag ) | 
intra_tmp_flag | ae(v)

## Slide 7: Syntax Tables (Contd.)
Cont.
if ( !intra_tmp_flag && !intra_dimd_flag) { | 
if( sps_mip_enabled_flag ) | 
intra_mip_flag | ae(v)
if( intra_mip_flag ) { | 
intra_mip_transposed_flag[ x0 ][ y0 ] | ae(v)
intra_mip_mode[ x0 ][ y0 ] | ae(v)
} else { | 
if (sps_dimd_enable_flag ) | 
intra_dimd_flag | 
if (!intra_dimd_flag) { | 
if ( sps_timd_enable_flag && (sh_slice_type != I ¦¦ (sh_slice_type == I && cbWidth * cbHeight <=1024 ) )) | 
intra_timd_flag | ae(v)
if( sps_mrl_enabled_flag && ( ( y0 % CtbSizeY ) > 0 ) ) | 
intra_luma_ref_idx | ae(v)
if( sps_isp_enabled_flag && …) | 
intra_subpartitions_mode_flag | ae(v)
} | 
if (!intra_timd_flag && !intra_dimd_flag) { | 
if( intra_luma_ref_idx = = 0 ) | 
intra_luma_mpm_flag[ x0 ][ y0 ] | ae(v)
… | 
} | 
} | 

## Slide 8: Experimental Results
For class A –E,
  RD Change is due to dimd_flag is moved after MIP.
  MIP is not enabled in LD. So no change in LD.
For class F and TGM, BDPCM and TM are also enabled. so RD impact is slightly more noticeable. Class F seems to have a small gain.
Overall all, very little impact on coding performance. Some of the small RD changes may be RD noise.
 | All Intra Main 10 |  |  |  | 
 | Over ECM-3.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.05% | 0.04% | 101% | 100%
Class A2 | -0.01% | 0.01% | 0.01% | 100% | 99%
Class B | -0.01% | -0.07% | -0.01% | 100% | 100%
Class C | -0.01% | -0.03% | 0.01% | 100% | 99%
Class E | 0.00% | -0.06% | -0.07% | 101% | 101%
Overall | -0.01% | -0.03% | 0.00% | 100% | 100%
Class D | 0.02% | -0.03% | -0.22% | 101% | 100%
Class F | -0.04% | 0.11% | -0.11% | 100% | 101%
Class TGM | 0.00% | -0.02% | -0.02% | 100% | 99%
 | Random Access Main 10 |  |  |  | 
 | Over ECM-3.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.03% | -0.04% | 0.04% | 100% | 100%
Class A2 | 0.00% | 0.14% | 0.11% | 100% | 100%
Class B | 0.01% | 0.08% | 0.09% | 100% | 100%
Class C | 0.00% | 0.04% | 0.13% | 100% | 100%
Class E |  |  |  |  | 
Overall | 0.01% | 0.06% | 0.10% | 100% | 100%
Class D | 0.01% | 0.19% | -0.22% | 100% | 100%
Class F | -0.02% | 0.00% | -0.28% | 100% | 99%
Class TGM | -0.04% | -0.05% | 0.02% | 100% | 100%
 | Low delay B Main 10 |  |  |  | 
 | Over ECM-3.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.00% | 0.00% | 0.00% | 100% | 100%
Class C | 0.00% | 0.00% | 0.00% | 100% | 100%
Class E | 0.00% | 0.00% | 0.00% | 101% | 100%
Overall | 0.00% | 0.00% | 0.00% | 100% | 100%
Class D | 0.00% | 0.00% | 0.00% | 100% | 100%
Class F | -0.10% | -1.13% | -0.52% | 101% | 99%
Class TGM | 0.03% | -0.10% | 0.15% | 100% | 101%

## Slide 9: Conclusion
Propose to move the position of dimd_flag to right before timd_flag
The purpose is software and signalling logic clean up, consistency with other intra mode syntaxes (e.g. timd_flag).
Little impact on performance.
Propose to adopt this simple change into ECM software.
Thanks Keming Cao @ Qualcomm for cross-checking (JVET-Y0179)