## Slide 1: JVET-Y0153 EE2-3.11: Non-adjacent spatial neighbors for affine Merge mode
Wei Chen, Xiaoyu Xiu, Yi-Wen Chen, Hong-Jheng Jhu, Che-Wei Kuo, Xianglin Wang

## Slide 2: Introduction
Background
  In VVC, only adjacent spatial neighbors are considered for regular merge mode and affine merge mode.
  In ECM3.1, non-adjacent spatial candidates are included into merge candidate list.
In JVET-X0151, it is proposed to use non-adjacent spatial neighbors for affine merge mode.
  Inherited affine merge candidates from non-adjacent neighbors
  The first type of constructed affine merge candidates from non-adjacent neighbors
In this EE, it is proposed to use non-adjacent spatial neighbors for both affine merge and affine AMVP mode.
  Inherited affine merge candidates from non-adjacent neighbors
  Inherited affine AMVP candidates from non-adjacent neighbors
  The first type of constructed affine merge candidates from non-adjacent neighbors
  The second type of constructed affine merge candidates from non-adjacent neighbors

## Slide 3: Proposal
Non-adjacent neighbors for inherited affine merge and affine AMVP candidates
  Distance of non-adjacent neighbors to one CU is defined based on the width/height of the CU
  The checking order of non-adjacent spatial neighbors:
    Distance: from near to far
    Direction: Bottom-to-up and right-to-left for left and above neighbors
    At a specific distance, the first available neighbor from each side is selected.
    The core derivation is kept exactly the same as the existing affine inherited merge

## Slide 4: Proposal
Non-adjacent neighbors for the first type of constructed affine merge candidates
  The same positions and checking orders of non-adjacent neighbors as non-adjacent inherited merge candidates
  Derivation method
    Step One: selecting left and above neighbors; then determining top-left neighbor to form a virtual block.
    Step Two: generating the CPMVs at the A, B and C of the virtual block.
    Step Three: projecting the CPMVs of the virtual block to the current CU.
Pattern of non-adjacent spatial neighbors for deriving constructed affine merge candidates
Derivation method

## Slide 5: Proposal
Non-adjacent neighbors for the second type of constructed affine merge candidates
  Similarly derived as the EE2-3.12a, for each candidate
    the translational affine parameters inherited from the adjacent neighboring 4x4 blocks (same as EE2-3.12a)
    the non-translational affine parameters inherited from the non-adjacent spatial neighbors (different from EE2-3.12a)

## Slide 6: Proposal
The modified affine merge candidate list
  SbTMVP candidate, if available
  Inherited from adjacent neighbors
  Inherited from non-adjacent neighbors
  Constructed from adjacent neighbors
  The second type of constructed affine candidates from non-adjacent neighbors
  The first type of constructed affine candidates from non-adjacent neighbors
  Zero MVs
The modified affine AMVP candidate list
  Inherited from adjacent neighbors
  Constructed from adjacent neighbors
  Translational MVs from adjacent neighbors
  Translational MVs from temporal neighbors
  Inherited from non-adjacent neighbors
  Zero MVs
The size of the existing affine merge candidate list is increased from 5 to 15. The subgroup size of ARMC in affine merge mode is increased from 3 to 15.

## Slide 7: Performance evaluation
Anchor: ECM-3.1
Tested: The proposed method (EE2-3.11)
 | Over ECM-3.1 |  |  |  |  |  |  |  |  | 
 | Random Access |  |  |  |  | Low Delay B |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.35% | -0.26% | -0.35% | 100% | 100% |  |  |  |  | 
Class A2 | -0.57% | -0.25% | -0.40% | 101% | 101% |  |  |  |  | 
Class B | -0.33% | -0.08% | -0.13% | 100% | 100% | -0.57% | -0.66% | -0.69% | 102% | 101%
Class C | -0.22% | 0.02% | -0.10% | 100% | 100% | -0.49% | -0.39% | -0.41% | 101% | 102%
Class E |  |  |  |  |  | -0.23% | 0.45% | -0.45% | 101% | 100%
Overall | -0.35% | -0.12% | -0.22% | 100% | 100% | -0.46% | -0.29% | -0.53% | 101% | 101%
Class D | -0.25% | -0.18% | -0.02% | 100% | 100% | -0.74% | -0.22% | -0.97% | 101% | 101%
Class F | -0.23% | -0.27% | -0.28% | 100% | 100% | -0.55% | -0.53% | 0.21% | 101% | 102%

## Slide 8: Performance evaluation
Anchor: ECM-3.1
Tested: Only increasing the affine merge list size and ARMC subgroup size
 | Over ECM-3.1 |  |  |  |  |  |  |  |  | 
 | Random Access |  |  |  |  | Low Delay B |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.02% | -0.11% | -0.05% | 101% | 101% |  |  |  |  | 
Class A2 | -0.01% | 0.03% | 0.03% | 101% | 100% |  |  |  |  | 
Class B | 0.00% | -0.06% | 0.12% | 100% | 100% | -0.04% | -0.27% | -0.23% | 101% | 101%
Class C | 0.01% | 0.05% | 0.14% | 100% | 99% | -0.02% | 0.03% | 0.02% | 101% | 101%
Class E |  |  |  |  |  | 0.05% | 0.56% | -0.26% | 101% | 101%
Overall | 0.00% | -0.02% | 0.07% | 100% | 100% | -0.01% | 0.04% | -0.16% | 101% | 101%
Class D | -0.02% | -0.03% | 0.14% | 101% | 100% | 0.17% | -0.03% | -0.58% | 101% | 100%
Class F | 0.02% | 0.06% | -0.01% | 100% | 100% | 0.22% | 0.10% | 0.15% | 101% | 100%

## Slide 9: Conclusion
  Performance of the proposed non-adjacent spatial neighbors for affine mode (NSAM) is tested in EE2-3.11
  It is recommended to adopt the NSAM in the next ECM.
 | Y | U | V | Enc | Dec
RA | -0.35% | -0.12% | -0.22% | 100% | 100%
LDB | -0.46% | -0.29% | -0.53% | 101% | 101%
  Thanks to Qualcomm for the crosschecking!