## Slide 1: AHG7: GDR without encoder constraints for ECM JVET-Y0163
L. Wang, S. Hong, K. Panusopone,
M.M. Hannuksela, J. Lainema

## Slide 2
VTM-like GDR needs to add constraints on each coding tool to avoid leaks
For CUs in clean area of GDR/recovering picture, reconstructed pixels and coding information in dirty areas of current picture and reference pictures are considered as “not available”, and if needed, set to pre-determined values
CUs in dirty area are allowed to use coding information in both clean and dirty areas
New GDR Implementation

## Slide 3
Tests under LDP configuration specified in JVET-Y0043
Test 1: new GDR over VTM-like GDR
  With turning off ECM tools
Test 2: new GDR over LDP anchor
  With ECM tools, except new loop filter tools
Experimental Results
Test 1
Test 2

## Slide 4
It may not be easy to make VTM-like GDR run with all the new ECM coding tools
New GDR
    is more friendly and flexible with coding tools
    requires less effort to maintain GDR feature in ECM
    reduces # of code lines significantly
    has better coding performance
It is suggested to include new GDR implementation in ECM
We would like to thank InterDigital for crosschecking (JVET-Y0200)
Summary

## Slide 5
ECM 3.0 adds more than 40 new features and coding tools on top of VTM
VTM-like GDR can run with turning off new ECM features and coding tools
New GDR can run with all new ECM features and coding tools, (except new loop filter tools)
  In VTM, loop filters are disabled at virtual boundary
  This part of code is currently missing for new loop filters
Current Status