## Slide 1: JVET-Y0174
EE2-1.1–related: additional tests on partitioning flexibility
F. Urban, K. Naser, F. Galpin (Interdigital)
K. Zhang, L. Zhang, Z. Deng, N. Zhang, Y. Wang (Bytedance)

## Slide 2: additional tests on partitioning flexibility
Improvement in compression gain comes from coding modes diversity
  Increase the RDO search space
  Increase encoder run-time in an exhaustive RDO algorithm
  But the impact of new tool can be very limited on the decoder side
Codec complexity is not only encoder complexity
  Ex: contribution JVET-Y0126 improves VTM performances by modifying encoder while increasing encoding time
  RDO optimisation is a key feature for encoder developers
    find good trade-offs between encoding time and compression gains.
    Heuristics improve with time

## Slide 3: additional tests on partitioning flexibility
BD-rate gains in AI configuration, in JEM7 for QTBT and QTBT+ABT, achieved with a fast split decision based on CNN.
From JVET-J0034
Fast encoder: best trade-off is to use simple partitioning
High efficiency, more encoding time: best trade off includes more flexible partitioning
Gain in JEM7 as functions of encoding time (% of HM)

## Slide 4: additional tests on partitioning flexibility in ECM 3.1 base on EE2 – 1.1 ABT tool
Effect of partitioning flexibility on compression performance.
The parameter MaxMTTHierarchyDepthByTiD has been set to different values from 2 to 5
Higher gains are obtained with ABT.
ECM gains saturates when enabling more encoding time
Encoder benefits from flexible partitioning
  Low complexity at decoder
  Only transforms for non-power of 2 block size
  No additional complexity for power of 2 blocks
Chart: Class B
| 1 | 1.8562898247213455 | 2.2649237635027286 | 2.7288448667409457 | 3.2630015582571703
ECM | 0 | -0.0097513 | -0.012263 | -0.013725 | -0.015224
ABT | -0.0043103 | -0.0071032 | -0.012258 | -0.014644 | -0.017795

## Slide 5: Conclusion
More partitioning flexibility should be enabled in ECM
EE2 1.1 may be adopted in software, but reduced configuration in CTC
Thank you

## Slide 6: additional tests on partitioning flexibility in ECM 3.1 base on EE2 – 1.1 ABT tool
MaxMTTHierarchyDepthByTiD has been set to different values for the ECM-3.1 and EE2-1.1
 | Overall |  | Class B | 
ECM-3.1 | 0.00% | 100% | 0.00% | 100%
ECM-3.1 444433 | -0.91% | 174% | -0.98% | 186%
ECM-3.1 444444 | -1.16% | 219% | -1.23% | 226%
ECM-3.1 554444 |  |  | -1.37% | 273%
ECM-3.1 555544 |  |  | -1.52% | 326%
ABT 333222 (AB) | -0.38% | 137% | -0.43% | 133%
ABT | -0.68% | 158% | -0.71% | 155%
ABT 333333 |  |  | -1.23% | 200%
ABT 443333 |  |  | -1.46% | 240%
ABT 444433 | #VALUE! | #NUM! | -1.78% | 303%
ABT 444444 |  |  | #VALUE! | #NUM!
 | Class A-B |  | Class C-D | 
 | MaxMTTHierarchyDepth | MaxMTTHierarchyDepthByTid | MaxMTTHierarchyDepth | MaxMTTHierarchyDepthByTid
ECM-3.1 | 4 | 3 3 3 3 2 2 | 4 | 3 3 3 3 3 3
ECM-3.1 444433 | 4 | 4 4 4 4 3 3 | 4 | 4 4 4 4 3 3
ECM-3.1 444444 | 4 | 444444 |  | 
ECM-3.1 554444 | 4 | 554444 |  | 
ECM-3.1 555544 | 4 | 555544 |  | 
ABT 333222 | 4 | 333222 | 4 | 333332
ABT | 4 | 333322 | 4 | 333333
ABT 333333 | 4 | 333333 |  | 
ABT 443333 | 4 | 443333 |  | 
ABT 444433 | 4 | 444433 | 4 | 444433
ABT 444444 | 4 | 444444 |  | 

## Slide 7: additional tests on partitioning flexibility in ECM 3.1 base on EE2 – 1.1 ABT tool
Effect of partitioning flexibility on compression performance.
The parameter MaxMTTHierarchyDepthByTiD has been set to different values from 2 to 5
Chart: Class B
| 1 | 1.8562898247213455 | 2.2649237635027286 | 2.7288448667409457 | 3.2630015582571703
ECM | 0 | -0.0097513 | -0.012263 | -0.013725 | -0.015224
ABT | -0.0043103 | -0.0071032 | -0.012258 | -0.014644 | -0.017795
Chart: Overall
| 1 | 1.743077668627349 | 2.18567242846358
ECM | 0 | -0.00912 | -0.011574
ABT | -0.0037995 | -0.0068146 | -0.016424