## Slide 1: JVET-Y0181: AHG12: CABAC Initialization from Previous Inter Slice
Vadim Seregin, Jie Dong, Nan Hu, Marta Karczewicz
Qualcomm

## Slide 2: Introduction
Propose two methods to improve the probability estimation for CABAC
  Temporal CABAC initialization
  Adaptive window size adjustment

## Slide 3: Temporal CABAC Initialization
Basic idea
  Initialize context models using probability states saved from a previous slice, instead of using pre-defined values.
Details
  Slices are inter.
  Slices are coded with the same sliceQP
  Location of CTU
  min ((W + C)/2 + 1, C)
  C: Number of CTUs in the slice
  W: Number of CTUs in a row

## Slide 4: Adaptive Window Size Adjustment
VVC/ECM
  use two probability states for each context mode, pStateL and pStateH.
Proposed
  Per bin, adjust the window sizes
  deltaL and deltaH each has the range -7 to 7 (15 different valid values)
  if( binVal = = 1 ) { pStateL += ( (210-1) - pStateL ) >> shiftL pStateH += ( (214-1) - pStateH ) >> shiftH } else {
  pStateL -= pStateL >> shiftL pStateH -= pStateH >> shiftH }
shiftL
shiftH
shiftL + deltaL
shiftH + deltaH
shiftL’ = max(2, shiftL + deltaL)
shiftH’ = max(2, shiftH + deltaH)

## Slide 5: Adaptive Window Size Adjustment
delatL and deltaH derivation
  For each context model, we store M preceding bins (M =12)
  Retrieve the M bins and use them as the index to look up a pre-defined table (see figure) .
  Convert an LUT entry to delatL and deltaH

## Slide 6: Experimental Results
Temporal CABAC initialization
Temporal CABAC initialization + Adaptive Window Size Adjustment
Class A1 | -0.11% | -0.01% | 0.07% | 88% | 91%
Class A2 | -0.07% | 0.07% | 0.08% | 92% | 92%
Class B | -0.09% | -0.01% | -0.11% | 94% | 81%
Class C | -0.09% | -0.14% | -0.06% | 97% | 87%
Class E | -0.12% | -0.15% | -0.12% | 103% | 88%
Overall | -0.09% | -0.05% | -0.04% | 95% | 87%
Class D | -0.06% | -0.02% | -0.15% | 103% | 91%
Class F | -0.20% | -0.25% | -0.19% | 93% | 81%
Class A1 | -0.35% | 0.10% | -0.17% | 92% | 90%
Class A2 | -0.21% | -0.05% | 0.02% | 94% | 91%
Class B | -0.31% | 0.18% | 0.26% | 89% | 82%
Class C | -0.28% | 0.10% | 0.53% | 90% | 86%
Class E |  |  |  |  | 
Overall | -0.29% | 0.09% | 0.20% | 91% | 86%
Class D | -0.46% | 0.47% | 0.24% | 103% | 92%
Class F | -0.34% | -0.36% | -0.45% | 96% | 85%
Class B | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class C | -0.38% | -0.18% | 0.99% | 78% | 78%
Class E | -0.24% | 0.98% | -0.42% | 72% | 75%
Overall | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class D | -0.67% | 0.94% | 2.32% | 77% | 81%
Class F | -0.40% | -1.10% | -1.00% | 80% | 82%
Class A1 | -0.20% | 0.10% | -0.22% | 100% | 99%
Class A2 | -0.06% | 0.03% | -0.06% | 99% | 98%
Class B | -0.19% | 0.22% | 0.18% | 100% | 100%
Class C | -0.17% | 0.08% | 0.28% | 99% | 101%
Class E |  |  |  |  | 
Overall | -0.16% | 0.12% | 0.08% | 99% | 100%
Class D | -0.37% | 0.14% | 0.20% | 100% | 101%
Class F | -0.23% | -0.20% | -0.19% | 98% | 100%
Class TGM | -0.52% | -0.58% | -0.56% | 99% | 101%
Class B | -0.26% | 0.27% | 0.56% | 102% | 101%
Class C | -0.30% | -0.07% | 0.89% | 101% | 100%
Class E | -0.13% | 0.52% | 0.28% | 103% | 101%
Overall | -0.24% | 0.22% | 0.60% | 102% | 101%
Class D | -0.50% | 1.32% | 1.56% | 99% | 104%
Class F | -0.43% | -0.05% | -0.41% | 99% | 99%
Class TGM | -0.88% | -1.03% | -1.08% | 96% | 99%
AI
RA
LDB
RA
LDB

## Slide 7: Conclusion
Two methods to improve the probability estimation for CABAC
  Temporal CABAC initialization:
      RA -0.16%, LDB -0.24%
  Temporal CABAC initialization + Adaptive window size adjustment:
      AI: -0.09%, RA: -0.29%, LDB: -0.32%*
Suggest to study this proposal in EE
Thank Oppo for cross-check.