## Slide 1: AHG12: Convolutional cross-component model (CCCM) for intra prediction JVET-Z0064
Pekka Astola, Jani Lainema, Ramin Ghaznavi Youvalari, Alireza Aminlou, Krit Panusopone

## Slide 2
Chroma samples are predicted using (downsampled) luma samples in the spirit of CCLM modes:
predChromaVal = c0C + c1N + c2S + c3E + c4W + c5P + c6B
Input to the above convolution consists of the 7 filter coefficients ci and:
Collocated luma sample C and its neighbors N, S, W, E
Nonlinear term P:
P = ( C*C + midVal ) >> bitDepth
Bias term B:
B = midVal
Convolutional cross-component model (CCCM)

## Slide 3
As in CCLM, the filter coefficients are calculated using least squares minimization between the reconstructed chroma and predicted chroma samples in the reference area of the PU.
Calculate autocorrelation matrix and cross-correlation vector
LDL decomposition of the autocorrelation matrix
Use back-substitution to find the final filter coefficients
Process follows the strategy currently used to find ALF coefficients, but:
LDL instead of Cholesky to avoid square root operations
Using integer arithmetic
CCCM filter coefficient calculation

## Slide 4
Reference area extends 6 sample lines above and left of the PU
One-line extensions to support the “side samples” of the filter
CCCM reference area

## Slide 5
Dual model CCCM follows the multi-model CCLM concept
Using average reference luma sample as the classification threshold
One CCCM model for samples above the threshold and another for the rest
Signaling using a single flag which
Enables/disables single model CCCM if intra mode is LM_CHROMA_IDX
Enables/disables dual model CCCM if intra mode is MMLM_CHROMA_IDX
Encoder search
RDO check for both single model and dual model CCCM mode
Further detail

## Slide 6
Experimental results
 | All Intra Main10 |  |  |  | 
 | Over ECM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -1.28 % | -3.67 % | -5.88 % | 101 % | 104 %
Class A2 | -5.64 % | -5.02 % | -7.59 % | 102 % | 104 %
Class B | -0.65 % | -4.15 % | -2.54 % | 101 % | 104 %
Class C | -0.16 % | -1.25 % | -1.12 % | 102 % | 102 %
Class E | -0.37 % | -3.75 % | -1.77 % | 102 % | 102 %
Overall | -1.43 % | -3.51 % | -3.50 % | 102 % | 103 %
Class D | -0.09 % | -0.77 % | -0.70 % | 102 % | 102 %
Class F | -0.83 % | -3.11 % | -3.00 % | 101 % | 102 %
Class TGM | -2.66 % | -5.12 % | -4.93 % | 101 % | 103 %
 | Random Access Main 10 |  |  |  | 
 | Over ECM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -1.13 % | -2.55 % | -4.32 % | 100 % | 101 %
Class A2 | -2.10 % | -2.55 % | -4.26 % | 100 % | 100 %
Class B | -0.37 % | -3.57 % | -2.68 % | 101 % | 100 %
Class C | -0.07 % | -0.83 % | -0.61 % | 102 % | 100 %
Class E |  |  |  |  | 
Overall | -0.79 % | -2.43 % | -2.77 % | 101 % | 100 %
Class D | -0.02 % | -0.83 % | -0.71 % | 102 % | 99 %
Class F | -1.11 % | -2.93 % | -3.08 % | 101 % | 100 %
Class TGM | -1.54 % | -2.48 % | -2.35 % | 100 % | 101 %

## Slide 7
Experimental results (variants)
 | Proposed | Nonlinear off | 3 ref lines | 2 ref lines above CTU | Min PU 64 | Multi-mode off | 3 flags
vs. ECM4 | Test 1 | Test 2 | Test 3 | Test 4 | Test 5 | Test 6 | Test 7
Class A1 | -1.28 % | -0.94 % | -1.05 % | -1.24 % | -1.31 % | -0.99 % | -1.23 %
Class A2 | -5.64 % | -5.59 % | -5.50 % | -5.59 % | -5.82 % | -5.53 % | -5.57 %
Class B | -0.65 % | -0.55 % | -0.61 % | -0.63 % | -0.65 % | -0.59 % | -0.63 %
Class C | -0.16 % | -0.09 % | -0.15 % | -0.14 % | -0.16 % | -0.12 % | -0.15 %
Class E | -0.37 % | -0.34 % | -0.33 % | -0.37 % | -0.38 % | -0.34 % | -0.34 %
Y | -1.43 % | -1.32 % | -1.35 % | -1.41 % | -1.47 % | -1.34 % | -1.40 %
UV | -3.50 % | -2.98 % | -2.60 % | -3.41 % | -3.07 % | -2.88 % | -4.92 %
Class D | -0.09 % | -0.07 % | -0.08 % | -0.09 % | -0.11 % | -0.09 % | -0.10 %
Class F | -0.83 % | -0.73 % | -0.65 % | -0.81 % | -0.77 % | -0.64 % | -0.85 %
vs. Test 1 | Test 1 | Test 2 | Test 3 | Test 4 | Test 5 | Test 6 | Test 7
Class A1 | 0.00 % | 0.35 % | 0.23 % | 0.05 % | -0.02 % | 0.29 % | 0.05 %
Class A2 | 0.00 % | 0.05 % | 0.14 % | 0.05 % | -0.18 % | 0.11 % | 0.07 %
Class B | 0.00 % | 0.09 % | 0.04 % | 0.02 % | -0.01 % | 0.06 % | 0.01 %
Class C | 0.00 % | 0.07 % | 0.01 % | 0.02 % | -0.01 % | 0.04 % | 0.01 %
Class E | 0.00 % | 0.04 % | 0.04 % | 0.00 % | 0.00 % | 0.03 % | 0.04 %
Y | 0.00 % | 0.11 % | 0.08 % | 0.03 % | -0.04 % | 0.10 % | 0.03 %
UV | 0.00 % | 0.52 % | 0.91 % | 0.09 % | 0.43 % | 0.62 % | -1.42 %
Class D | 0.00 % | 0.03 % | 0.02 % | 0.01 % | -0.02 % | 0.01 % | 0.00 %
Class F | 0.00 % | 0.11 % | 0.18 % | 0.02 % | 0.07 % | 0.19 % | -0.02 %
Test 1: Proposed method
Test 2: Disabling the nonlinear term
Test 3: Using 3 lines of reference samples
Test 4: Using 2 lines of reference samples above the CTU
Test 5: Enable CCCM modes only if chroma PU has at least 64 samples
Test 6: Enable only single model CCCM mode
Test 7: 3 extra flags for PU level - activate nonlinear term - select 3 or 6 reference lines - select 5-tap (+) or 3-tap (-) filter - ~15% extra encoder runtime

## Slide 8
Proposing convolutional cross-component based chroma prediction
Provides significant coding efficiency improvements
Has minimal impact on encoder/decoder runtimes
It is suggested to include the technique in the next round of EEs.
Thanks to Qualcomm for cross-check.
Summary