## Slide 1: JVET-Z0083 Non-EE2: Fix on MHP parsing condition
N. Park, J. Nam, J. Lim, S. Kim

## Slide 2: Problem statement
In previous meeting, MVD sign prediction (MVSD) was adopted in ECM4.0.
From this adoption, Multi-Hypothesis Prediction (MHP) syntaxes were moved to in front of MVSD.
  Because MVSD index is parsed only if explicitly signaled MHP data is NOT present. : Dependency #1
  (At the same time, sign of MVD is not parsed.)
bcw_idx, mh_pred_data
imv
mvsd_idx
ref_idx, mvp_flag, mvd
ref_idx, mvp_flag, mvd
imv
bcw_idx, mh_pred_data
<ECM3.0>
<ECM4.0>
Dependency #1

## Slide 3: Problem statement
How about MHP syntax after moved?
  Still following conditions are considered.
  mh_pred_data() is referencing AMVR index (imv), which is not parsed yet : Dependency #2
  ECM4.0 is not working by parsing error when BcwFast option in Cfg file is set to 0.
slice_type != B
IBC mode
CIIP Mode
GPM-MERGE
TM-MERGE mode
BM-MERGE mode
!merge_flag && bcw_idx == Default (Equal weight)
!merge_flag && affine && imv != 0
cbWidth * cbHeight <=64 || min(cbWidth, cbHeight) < 8
bcw_idx, mh_pred_data
imv
mvsd_idx
ref_idx, mvp_flag, mvd
<ECM4.0>
Dependency #2

## Slide 4: Proposed methods
To resolve the problem, two solutions are proposed.
  Solution 1: remove dependency between AMVR and MHP
  Solution 2: relocate MHP parsing behind AMVR syntax and remove dependency between MHP and MVSD

## Slide 5: Proposed methods
Solution 1: remove dependency between AMVR and MHP
  One of conditions for MHP parsing is removed : Removal of Dependency #2
  MHP of affine inter mode has no dependency with AMVR.
bcw_idx, mh_pred_data
imv
mvsd_idx
ref_idx, mvp_flag, mvd
Dependency #2
slice_type != B
IBC mode
CIIP Mode
GPM-MERGE
TM-MERGE mode
BM-MERGE mode
!merge_flag && bcw_idx == Default (Equal weight)
!merge_flag && affine && imv != 0
cbWidth * cbHeight <=64 || min(cbWidth, cbHeight) < 8
<Proposed Solution 1>

## Slide 6: Proposed methods
Solution 2: relocate MHP parsing behind AMVR syntax and remove dependency between MHP and MVSD
  MHP is relocated behind AMVR syntax : keep Dependency #2 with no parsing problem
  MVSD is not referencing MHP data : removal of Dependency #1
bcw_idx, mh_pred_data
imv
mvsd_idx
ref_idx, mvp_flag, mvd
<ECM4.0>
bcw_idx, mh_pred_data
imv
mvsd_idx
ref_idx, mvp_flag, mvd
Keep
Dependency #2
with no parsing problem
<Proposed Solution 2>
Removal of
Dependency #1

## Slide 7: Simulation results
Solution 1: remove dependency between AMVR and MHP
  No Changes.
  In ECM software, there are many encoder optimization techniques to speed up by skipping to check possible modes.
  Especially, MHP of affine inter mode is allowed only AMVR index with 0.
Solution 2: relocate MHP parsing behind AMVR syntax and remove dependency between MHP and MVSD
 | Over ECM4.0 |  |  |  |  |  |  |  |  | 
 | Random access Main10 |  |  |  |  | Low delay B Main10 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.01% | 0.00% | 101% | 101% |  |  |  |  | 
Class A2 | 0.00% | -0.02% | -0.01% | 101% | 101% |  |  |  |  | 
Class B | -0.01% | 0.01% | -0.04% | 100% | 101% | 0.00% | -0.04% | -0.37% | 102% | 101%
Class C | -0.01% | 0.01% | -0.10% | 100% | 100% | -0.03% | 0.15% | -0.29% | 100% | 101%
Class E |  |  |  |  |  | -0.08% | -0.13% | -0.52% | 100% | 101%
Overall | -0.01% | 0.00% | -0.04% | 101% | 101% | -0.03% | 0.00% | -0.38% | 101% | 101%
Class D | 0.02% | -0.01% | -0.02% | 100% | 100% | -0.01% | 0.72% | 0.82% | 99% | 99%
Class F | 0.00% | -0.05% | -0.01% | 100% | 100% | 0.11% | 0.09% | -0.20% | 100% | 101%

## Slide 8: Conclusion
This contribution reports a parsing error on MHP parsing condition in ECM4.0.
To resolve the problem, two solutions are proposed.
  Solution 1: remove dependency between AMVR and MHP
  Solution 2: relocate MHP parsing behind AMVR syntax and remove dependency between MHP and MVSD
The simulation results
  Solution 1: same as ECM-4.0 anchor because of fast encoder option (BcwFast = 1 in CTC)
  Solution 2: -0.01% in RA and -0.03% in LB
  The proposed modifications make no parsing error on ECM-4.0 when BcwFast option is set to 0.
It is recommended to adopt Solution 1 in the next ECM.
Thanks to Qualcomm(JVET-Z0238) and Kwai(JVET-Z0217)
for cross-checking