## Slide 1: JVET-Z0131 EE2-related: Block Vector Difference Binarization
Keming Cao, Vadim Seregin, Marta Karczewicz
Qualcomm Inc.

## Slide 2: Block Vector Difference Binarization
In current ECM-4.0, Block vector difference binarization shares the same method as motion vector difference binarization
We propose:
  Remove greater than 1 flag
  Context code the first 5 bins of EG1 prefix

## Slide 3: Block Vector Difference Binarization
Proposed method
Combined with EE2-3.6l
 | All Intra Main 10 |  |  |  | 
 | Over ECM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | -0.73% | -0.49% | -0.54% | 98% | 94%
Class TGM | -1.53% | -1.36% | -1.33% | 96% | 93%
 | Random Access Main 10 |  |  |  | 
 | Over ECM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | -0.32% | -0.55% | -0.47% | 98% | 98%
Class TGM | -0.98% | -0.82% | -0.78% | 101% | 100%
EE2-3.6l from Z0165
 | All Intra Main 10 |  |  |  | 
 | Over ECM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | -4.54% | -4.08% | -4.33% | 118% | 98%
Class TGM | -9.56% | -8.74% | -8.71% | 108% | 93%
 | Random Access Main 10 |  |  |  | 
 | Over ECM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | -2.99% | -3.10% | -3.18% | 110% | 99%
Class TGM | -6.57% | -6.20% | -6.48% | 106% | 97%
 | All Intra Main 10 |  |  |  | 
 | Over ECM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | -5.11% | -4.65% | -4.75% | 130% | 101%
Class TGM | -10.82% | -9.97% | -9.96% | 113% | 96%
 | Random Access Main 10 |  |  |  | 
 | Over ECM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | -3.35% | -3.34% | -3.41% | 110% | 101%
Class TGM | -7.43% | -6.99% | -7.24% | 106% | 99%

## Slide 4: Block Vector Difference Binarization
Proposed method
 | All Intra Main 10 |  |  |  | 
 | Over ECM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | -0.73% | -0.49% | -0.54% | 98% | 94%
Class TGM | -1.53% | -1.36% | -1.33% | 96% | 93%
 | Random Access Main 10 |  |  |  | 
 | Over ECM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | -0.32% | -0.55% | -0.47% | 98% | 98%
Class TGM | -0.98% | -0.82% | -0.78% | 101% | 100%
Keeping greater than 1 flag
 | All Intra Main 10 |  |  |  | 
 | Over ECM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | -0.69% | -0.31% | -0.49% | 104% | 100%
Class TGM | -1.49% | -1.31% | -1.30% | 102% | 101%
 | Random Access Main 10 |  |  |  | 
 | Over ECM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | -0.38% | -0.48% | -0.46% | 101% | 100%
Class TGM | -0.89% | -0.81% | -0.78% | 103% | 102%