## Slide 1
JVET-Z0137: Non-EE2: Adaptive Blending for GPM
Han Gao, Xiaoyu Xiu, Wei Chen, Hong-Jheng Jhu, Che-Wei Kuo, Ning Yan, Xianglin Wang

## Slide 2: Introduction
Blending area width is fixed as
Weighting depends on distance
Fixed blending hard to fix all contents

## Slide 3: Proposed method
Blending area width is adaptively selected at CU-level as
The blending strength index is signaled into the bitstream
Shiftable value based make sure that current equation is reusable

## Slide 4: Experimental results
Experimental results shows
  0.14%/0.17% RA/LDB gain for nature content
  1.90%/2.61% RA/LDB gain for TGM
Proposed to be included in the next EE
 | Random Access Main 10 |  |  |  | 
 | Over ECM3.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.16% | -0.58% | -0.14% | 102% | 99%
Class A2 | 0.02% | -0.03% | 0.02% | 98% | 100%
Class B | -0.13% | -0.23% | -0.16% | 103% | 100%
Class C | -0.28% | -0.18% | -0.14% | 101% | 103%
Class E |  |  |  |  | 
Overall | -0.14% | -0.25% | -0.12% | 101% | 100%
Class D | -0.18% | -0.28% | 0.05% | 100% | 102%
Class F | -0.62% | -0.68% | -0.57% | 105% | 98%
Class TGM | -1.90% | -1.30% | -1.26% | 101% | 98%
 | Low delay B Main 10 |  |  |  | 
 | Over ECM3.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.10% | 0.04% | 0.09% | 103% | 101%
Class C | -0.31% | -0.05% | -0.54% | 105% | 102%
Class E | -0.08% | -0.18% | 0.66% | 99% | 98%
Overall | -0.17% | -0.04% | 0.02% | 102% | 100%
Class D | -0.30% | 0.05% | -0.12% | 102% | 102%
Class F | -0.69% | 0.09% | -0.88% | 102% | 99%
Class TGM | -2.61% | -2.11% | -2.12% | 102% | 98%

## Slide 5: Thank you!