## Slide 1
JVET-Z0140
AHG12: Enhanced CCLM
Che-Wei Kuo, Xiaoyu Xiu, Ning Yan, Hong-Jheng Jhu, Wei Chen, Han Gao, and Xianglin Wang

## Slide 2: Introduction
Dramatic luma intensity change (gradient) may lead to corresponding chroma value change, known as the purple fringing problem
  high luminance blooming which incurs saturated photodiode quantum-well and charge leakage in a charge coupled device (CCD)
  demosaicing built in cameras to interpolate missing colors due to Bayer pattern Color Filter Array (CFA) arrangement, which may introduce aliasing
  chromatic aberration caused by different refractive indices for different RGB wavelengths, leading to different focal lengths that affect color accuracy

## Slide 3: Introduction
In CCLM, only single (downsampled) luma sample is considered when deriving the linear model
  neglecting the spatial correlation among neighbouring luma samples
Two methods are proposed to tackle the situation when luma gradients are highly correlated to chroma values
  Filter-based Linear Model
  Gradient Linear Model

## Slide 4: Method 1: Filter-based Linear Model (FLM)
Extend Simple Linear Regression in CCLM to Multiple Linear Regression
Decoder derives MLR parameters (, ) through Cholesky decomposition
Switch filter shapes at CU level with ranging from 2 to 6
C
N
to-be-predicted chroma sample
-th reconstructed luma sample surround the chroma sample
-th coefficient
offset
number of the involved luma samples

## Slide 5: Method 2: Gradient Linear Model (GLM)
Reuse CCLM process, but use gradient to derive the linear model
Other designs of CCLM are kept unchanged
  parameter derivation, prediction, template area…etc.
When CCLM is enabled
  Signal 2 flags for Cb/Cr to indicate if GLM is enabled
  Signal 1 syntax element to select one of four Sobel based gradient patterns
1 | 4 | 1 | /8 | → | 1 | 2 | 1
1 | 4 | 1 |  |  | -1 | -2 | -1
1 | 4 | 1 | /8 | → | 1 | 2 | 1
1 | 4 | 1 |  |  | -1 | -2 | -1

## Slide 6: Simulation Results
 | All Intra Main10 |  |  |  | 
 | Over ECM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.17% | -0.14% | -0.08% | 100% | 101%
Class A2 | -4.72% | -1.54% | -3.85% | 99% | 100%
Class B | -0.13% | -0.40% | 0.19% | 100% | 100%
Class C | 0.02% | -0.13% | -0.07% | 101% | 101%
Class E | -0.05% | -0.44% | -0.38% | 99% | 98%
Overall | -0.85% | -0.49% | -0.68% | 100% | 100%
Class D | 0.05% | 0.13% | -0.03% | 100% | 99%
Class F | -0.67% | -2.13% | -1.76% | 99% | 99%
Class TGM | -3.11% | -6.22% | -5.83% | #VALUE! | #VALUE!
 | Random Access Main 10 |  |  |  | 
 | Over ECM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.11% | -0.24% | 0.01% | 100% | 100%
Class A2 | -1.56% | -0.73% | -2.04% | 100% | 100%
Class B | -0.07% | -0.50% | 0.01% | 100% | 100%
Class C | 0.00% | -0.07% | 0.18% | 101% | 100%
Class E |  |  |  |  | 
Overall | -0.36% | -0.38% | -0.35% | 100% | 100%
Class D | 0.02% | 0.06% | -0.05% | 99% | 99%
Class F | -1.10% | -2.48% | -2.22% | 99% | 99%
Class TGM | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
 | All Intra Main10 |  |  |  | 
 | Over ECM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.02% | -0.24% | 0.00% | 104% | 98%
Class A2 | -3.12% | -1.63% | -3.36% | 109% | 98%
Class B | -0.08% | -0.35% | -0.10% | 104% | 98%
Class C | 0.03% | -0.01% | 0.04% | 105% | 99%
Class E | -0.02% | -0.07% | 0.17% | 104% | 100%
Overall | -0.53% | -0.42% | -0.55% | 105% | 99%
Class D | 0.04% | 0.24% | -0.06% | 105% | 100%
Class F | -0.46% | -2.53% | -1.57% | 103% | 99%
Class TGM | -3.09% | -8.63% | -8.00% | #VALUE! | #VALUE!
 | Random Access Main 10 |  |  |  | 
 | Over ECM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | -0.28% | 0.19% | 102% | 100%
Class A2 | -1.05% | -0.85% | -1.44% | 102% | 100%
Class B | -0.03% | -0.16% | -0.02% | 102% | 99%
Class C | 0.02% | 0.01% | 0.25% | 101% | 98%
Class E |  |  |  |  | 
Overall | -0.21% | -0.28% | -0.19% | 102% | 99%
Class D | 0.02% | 0.21% | -0.04% | 100% | 98%
Class F | -1.05% | -2.60% | -1.92% | 101% | 99%
Class TGM | -2.12% | -4.25% | -4.12% | #VALUE! | #VALUE!
FLM
GLM

## Slide 7: Conclusion
Propose two methods to tackle the situation when luma gradients are highly correlated to chroma values
  Filter-based Linear Model (FLM)
  Gradient Linear Model (GLM)
Significant luma/chroma gains on colorful sequences containing dramatic luma intensity change, as well as screen content sequences
Suggest to study both methods in EE
Thank Nokia for crosscheck

## Slide 8
Thanks