## Slide 1: JVET-Z0143: Non-EE2: Chroma intra modes derived from collocated luma blocks and neighboring chroma blocks
Yao-Jen Chang, Keming Cao, Bappaditya Ray, Vadim Seregin, Marta Karczewicz

## Slide 2: Introduction
In ECM, there are 11 intra prediction modes for chroma intra coding
  6 CCLM: LM (0), MMLM (10), LM_L, LM_A, MMLM_L, and MMLM_A (11 + 2-bit fix length coding)
  5 traditional intra modes: DM (0), 4 default modes (1 + 2-bit fix length coding)
Direct Mode (DM): the intra prediction mode of the corresponding luma block covering the center position of the current chroma block.
Luma partition
Chroma partition
CurrCU

## Slide 3: Proposed chroma intra modes
Replace 5 non-CCLM chroma modes (DM and 4 default modes) with 9 proposed chroma modes
The first 9 unique modes are added into the non-CCLM chroma mode list in the following order:
  Multiple DMs (MDM): the intra prediction mode of collocated luma block corresponding to a position (C, TL, TR, BL, BR) in current chroma CU.
  The neighbouring chroma modes (NCM): the intra prediction mode of neighbouring chroma blocks (0, 1, 2, 3, 4)
  The secondary chroma modes (SCM): the chroma intra mode is derived by offsetting +1 or -1 to the first two chroma intra modes in the non-CCLM chroma mode list (M0 - 1, M0 + 1, M1 – 1, M1 + 1)
  Default modes: PLANAR_IDX, VER_IDX, HOR_IDX, DC_IDX, VDIA_IDX, VER_IDX - 4, VER_IDX + 4, HOR_IDX - 4, HOR_IDX + 4
A truncated unary coding (0, 10, 110, 1110, …, 11111110, 11111111) is used to code the index of the nine chroma intra modes.
Luma partition
Chroma partition
CurrCU

## Slide 4: Test results
Implemented on top of ECM-4.0
 | All Intra Main 10 |  |  |  | 
 | Over ECM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.06% | -0.56% | -0.40% | 101% | 100%
Class A2 | -0.07% | -0.76% | -0.78% | 102% | 100%
Class B | -0.07% | -0.66% | -0.74% | 100% | 98%
Class C | -0.08% | -0.51% | -0.51% | 101% | 100%
Class E | -0.16% | -1.39% | -0.90% | 100% | 97%
Overall | -0.08% | -0.75% | -0.67% | 101% | 99%
Class D | -0.07% | -0.34% | -0.54% | 102% | 100%
Class F | -0.06% | -0.09% | -0.54% | 101% | 99%
 | Random Access Main 10 |  |  |  | 
 | Over ECM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.03% | -0.31% | -0.08% | 101% | 101%
Class A2 | -0.04% | -0.36% | -0.23% | 100% | 100%
Class B | -0.04% | -0.44% | -0.46% | 99% | 99%
Class C | -0.04% | -0.29% | -0.07% | 99% | 99%
Class E |  |  |  |  | 
Overall | -0.04% | -0.36% | -0.23% | 100% | 100%
Class D | 0.00% | -0.42% | -0.37% | 99% | 99%
Class F | 0.00% | -0.26% | -0.42% | 100% | 100%

## Slide 5: Comparisons
 | Non-CCLM mode list | DIMD derivation for chroma | Performance
ECM | DM, 4 default modes | N/A | N/A
1.3b: 1.1 + 1.2b + Chroma DIMD | DM, DIMD, 4 default modes | Y/Cb/Cr neighbouring samples for gradients, histogram, and sorting | AI: -0.12% -2.13% -2.03% 103% 100% RA: -0.05% -1.02% -0.89% 101% 100%
1.1 + 1.2b + Z0143 | 9 chroma modes (intra prediction modes from collocated and neighbouring blocks) | N/A | AI: -0.13% -2.37% -2.22% 102% 95% RA: -0.05% -1.05% -0.98% 100% 99%
1.3b:
  1.1: CCLM slope adjustment
  1.2b: Fusion of chroma intra modes
  DIMD chroma mode
Luma partition
Chroma partition
CurrCU
Z0143
  Multiple DMs
  Neighbouring chroma modes
  Secondary chroma modes (M0±1, M1±1)

## Slide 6: Comparisons between proposed method and DIMD
1.3b: ECM-4.0 + EE2-1.1 + EE2-1.2b + DIMD chroma mode
Test: ECM-4.0 + EE2-1.1 + EE2-1.2b + Z0143
 | All Intra Main 10 |  | 
 | Over 1.3b |  | 
 | Y | U | V
Class A1 | -0.02% | -0.02% | -0.17%
Class A2 | -0.02% | -0.21% | -0.16%
Class B | 0.00% | -0.27% | -0.24%
Class C | -0.01% | -0.16% | -0.21%
Class E | -0.04% | -0.55% | -0.15%
Overall | -0.02% | -0.24% | -0.20%
Class D | 0.00% | -0.37% | -0.19%
Class F | -0.02% | -0.23% | -0.29%
 | Random Access Main 10 |  | 
 | Over 1.3b |  | 
 | Y | U | V
Class A1 | 0.00% | -0.04% | -0.05%
Class A2 | -0.02% | -0.15% | 0.00%
Class B | -0.02% | 0.02% | -0.14%
Class C | 0.04% | -0.01% | -0.11%
Class E |  |  | 
Overall | 0.00% | -0.03% | -0.09%
Class D | -0.02% | 0.30% | -0.04%
Class F | -0.08% | 0.25% | 0.02%