## Slide 1: JVET-Z0147: Improvement of Inter-MTS in ECM
Bappaditya Ray, Vadim Seregin, Marta Karczewicz (Qualcomm)

## Slide 2: Inter-MTS in ECM-4.0
MTS is applied to inter-coding.
Four transform choices: {(DST7, DST7), (DST7, DCT8), (DCT8, DST7), (DCT8, DCT8)}.
Signaled in the CU level (up to CTU size) – 256 (for classA), 128 (for rest classes).
Poor tradeoff – NOT part of CTC.
 |  |  | Random access Main10 |  | 
 |  |  | Over ECM-2.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.31% | 0.29% | 0.56% | 122% | 103%
Class A2 | -0.52% | 0.50% | 0.47% | 121% | 101%
Class B | -0.35% | 0.54% | 0.44% | 122% | 104%
Class C | -0.22% | 0.60% | 0.66% | 122% | 111%
Class E |  |  |  |  | 
Overall | -0.34% | 0.50% | 0.53% | 122% | 105%
Class D | -0.25% | 0.64% | 0.39% | 120% | 105%
Class F | -0.12% | 0.15% | 0.18% | 115% | 113%
 |  |  | Low delay B Main10 |  | 
 |  |  | Over ECM-2.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.62% | 0.71% | 0.57% | 126% | 104%
Class C | -0.34% | 0.99% | 0.52% | 130% | 107%
Class E | -0.28% | 0.55% | 1.18% | 119% | 114%
Overall | -0.45% | 0.76% | 0.70% | 126% | 108%
Class D | -0.39% | 1.42% | 1.04% | 124% | 102%
Class F | -0.11% | 1.01% | 0.04% | 118% | 105%

## Slide 3: Proposed modification:
Modification 1:
Limit the maximum CU size for MTS could be applied is made resolution dependent.
SPS flag signaled to indicate maxCUSize.
  Width > 1080  maxCUSize: 32
  Width <= 1080  maxCUSize: 16.
Modification 2 (from JVET-D0126):
For smaller blocks (width <=16 && height <=16), DST7 and DCT8 is replaced with KLT0 and KLT1 respectively.
Two 4x4 matrices + Two 8x8 matrices + Two 16x16 matrices.
 |  |  | Random access Main10 |  | 
 |  |  | Over ECM-4.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.17% | 0.20% | 0.46% | 104% | 101%
Class A2 | -0.42% | 0.30% | 0.33% | 105% | 100%
Class B | -0.24% | 0.39% | 0.27% | 102% | 101%
Class C | -0.23% | 0.23% | 0.28% | 104% | 101%
Class E |  |  |  |  | 
Overall | -0.26% | 0.29% | 0.32% | 104% | 101%
Class D | -0.29% | 0.44% | 0.45% | 105% | 101%
Class F | -0.07% | -0.01% | 0.00% | 102% | 100%
 |  |  | Low delay B Main10 |  | 
 |  |  | Over ECM-4.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.24% | 0.26% | 0.27% | 102% | 101%
Class C | -0.41% | 0.61% | 0.27% | 107% | 101%
Class E | -0.20% | -0.07% | 0.10% | 101% | 101%
Overall | -0.29% | 0.29% | 0.23% | 104% | 101%
Class D | -0.37% | 0.89% | 0.47% | 107% | 101%
Class F | -0.05% | 0.77% | 0.79% | 103% | 100%

## Slide 4: Encoder speedup
 |  |  | Random access Main10 |  | 
 |  |  | Over ECM-4.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.17% | 0.20% | 0.46% | 104% | 101%
Class A2 | -0.42% | 0.30% | 0.33% | 105% | 100%
Class B | -0.24% | 0.39% | 0.27% | 102% | 101%
Class C | -0.23% | 0.23% | 0.28% | 104% | 101%
Class E |  |  |  |  | 
Overall | -0.26% | 0.29% | 0.32% | 104% | 101%
Class D | -0.29% | 0.44% | 0.45% | 105% | 101%
Class F | -0.07% | -0.01% | 0.00% | 102% | 100%
 |  |  | Low delay B Main10 |  | 
 |  |  | Over ECM-4.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.24% | 0.26% | 0.27% | 102% | 101%
Class C | -0.41% | 0.61% | 0.27% | 107% | 101%
Class E | -0.20% | -0.07% | 0.10% | 101% | 101%
Overall | -0.29% | 0.29% | 0.23% | 104% | 101%
Class D | -0.37% | 0.89% | 0.47% | 107% | 101%
Class F | -0.05% | 0.77% | 0.79% | 103% | 100%
 |  |  | Random access Main10 |  | 
 |  |  | Over ECM-4.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.15% | -0.01% | 0.25% | 101% | 102%
Class A2 | -0.34% | 0.24% | 0.31% | 101% | 98%
Class B | -0.19% | 0.35% | 0.22% | 101% | 100%
Class C | -0.22% | 0.34% | 0.32% | 102% | 100%
Class E |  |  |  |  | 
Overall | -0.22% | 0.25% | 0.27% | 101% | 100%
Class D | -0.27% | 0.53% | 0.44% | 103% | 100%
Class F | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
 |  |  | Low delay B Main10 |  | 
 |  |  | Over ECM-4.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class C | -0.39% | 0.61% | 0.36% | 105% | 101%
Class E | -0.20% | -0.23% | 0.44% | 100% | 100%
Overall | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class D | -0.42% | 1.51% | 0.72% | 103% | 100%
Class F | -0.05% | 0.73% | 0.30% | 100% | 97%