## Slide 1: Memory usage report on VTM / ECM
JVET-Z0150
Tomonori Hashimoto
Yukinobu Yasugi
Tomohiro Ikai

## Slide 2: Introduction
ECM encoder requires more and more memory per meetings.
This contribution proposes to add a print out code into VTM / ECM software.
Additional information about memory reduction tests are also provided.

## Slide 3: Current Memory Usage of ECM / VTM
With the development of ECM, encoder requires more and more memory.
  ECM4 requires about 18GiB in the worst case.
  Reduce the number of parallelism in cluster machines with limited memory
    e.g. 256GB memory machine use only 14 CPUs even if it has 20 or more.
The lack of amount of memory usage information in development stage.
RA | VTM16 | ECM1 | ECM2 | ECM3 | ECM4
classA | 8.8 | 14.9 | 15.0 | 16.1 | 18.1
classB | 2.8 | 6.1 | 6.2 | 7.0 | 8.1
classC | 1.0 | 3.3 | 3.5 | 3.6 | 4.4
classD | 0.6 | 2.8 | 2.9 | 3.0 | 3.7
classF | 2.6 | 5.7 | 5.9 | 6.8 | 7.8
maximum amount of VmPeak (Peak virtual memory size)

## Slide 4: Proposal
Add a print out code into VTM / ECM software
  Changes are less than 50 lines.
  It supports for Linux environment.
    reads /proc/self/status as the log file about memory usage.
Example of memory log

## Slide 5: Memory reduction tests (information)
Investigate where and how much memory is used
  Small sequences : REUSE_CU_RESULTS
  Large sequences : REUSE_CU_RESULTS, picture, ALF
Noted: measured in QP37, RA and 9 frames

## Slide 6: Test1 (information)
REUSE_CU_RESULTS off test for memory reduction
  Set REUSE_CU_RESULTS to 0 in TypeDef.h (with a few fixes)
  Cording performance
  Memory usage
 | All Intra Main10 |  |  |  |  | Random Access Main 10 |  |  |  |  | Low delay B Main10 |  |  |  | 
 | Over ECM-4.0 |  |  |  |  | Over ECM-4.0 |  |  |  |  | Over ECM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.04% | -0.07% | 0.07% | 106% | 100% | -0.03% | -0.18% | 0.21% | 106% | 99% |  |  |  |  | 
Class A2 | -0.04% | -0.04% | 0.08% | 106% | 99% | -0.03% | -0.14% | 0.01% | 105% | 100% |  |  |  |  | 
Class B | -0.04% | 0.06% | 0.08% | 107% | 100% | -0.05% | 0.04% | -0.05% | 106% | 100% | 0.02% | -0.04% | -0.05% | 104% | 98%
Class C | -0.06% | 0.00% | 0.08% | 107% | 101% | -0.04% | -0.08% | 0.16% | 111% | 101% | -0.04% | 0.71% | -0.25% | 107% | 99%
Class E | -0.04% | 0.08% | 0.01% | 106% | 100% |  |  |  |  |  | -0.28% | 0.34% | -0.06% | 106% | 99%
Overall | -0.05% | 0.01% | 0.07% | 106% | 100% | -0.04% | -0.07% | 0.07% | 107% | 100% | -0.07% | 0.30% | -0.12% | 106% | 99%
Class D | -0.03% | 0.09% | -0.04% | 108% | 107% | -0.01% | -0.28% | -0.08% | 112% | 105% | -0.04% | 0.59% | 0.86% | 111% | 106%
Class F | -0.11% | 0.34% | 0.06% | 104% | 99% | 0.04% | -0.28% | -0.02% | 104% | 100% | -0.13% | 1.16% | 0.05% | 104% | 99%
AI | ECM4 | Test1 | ratio
classA | 6.7 | 4.1 | 61.2%
classB | 5.2 | 2.7 | 50.7%
classC | 3.8 | 1.2 | 31.0%
classD | 3.5 | 0.9 | 25.2%
classE | 4.2 | 1.6 | 38.1%
classF | 5.5 | 2.9 | 52.7%
RA | ECM4 | Test1 | ratio
classA | 18.1 | 15.6 | 85.9%
classB | 8.1 | 5.6 | 68.7%
classC | 4.4 | 1.8 | 41.3%
classD | 3.7 | 1.1 | 30.5%
classE |  |  | 
classF | 7.8 | 5.2 | 67.6%
LDB | ECM4 | Test1 | ratio
classA |  |  | 
classB | 7.7 | 4.9 | 63.8%
classC | 4.3 | 1.7 | 39.2%
classD | 3.5 | 1.0 | 26.9%
classE | 5.5 | 2.9 | 53.1%
classF | 6.1 | 3.5 | 57.5%
14 % reduction is possible with 106% EncT

## Slide 7: Test2 (information)
ALF memory reduction test
  Replaces double with float (only double variables in AlfCovariance struct)
    sizeof(AlfCovariance) * numClasses * numClassifier * numfixedFilterSets * numCTUsInPic * m_filterShapes * MAX_NUM_COMPONENT
  Cording performance
  Memory usage
 | All Intra Main10 |  |  |  |  | Random Access Main 10 |  |  |  |  | Low delay B Main10 |  |  |  | 
 | Over ECM-4.0 |  |  |  |  | Over ECM-4.0 |  |  |  |  | Over ECM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.00% | -0.01% | -0.01% | 105% | 99% | 0.02% | -0.11% | 0.09% | 101% | 99% |  |  |  |  | 
Class A2 | 0.00% | -0.01% | 0.00% | 102% | 98% | 0.02% | -0.07% | 0.03% | 101% | 99% |  |  |  |  | 
Class B | 0.00% | -0.01% | 0.02% | 103% | 99% | 0.01% | -0.03% | 0.04% | 101% | 99% | 0.01% | -0.28% | -0.03% | 100% | 98%
Class C | 0.00% | 0.00% | 0.00% | 101% | 101% | 0.00% | -0.07% | -0.02% | 105% | 98% | -0.04% | 0.26% | -0.17% | 101% | 98%
Class E | 0.00% | 0.00% | 0.01% | 103% | 101% |  |  |  |  |  | -0.07% | -0.07% | 0.30% | 106% | 99%
Overall | 0.00% | -0.01% | 0.01% | 103% | 100% | 0.01% | -0.07% | 0.03% | 102% | 99% | -0.03% | -0.05% | 0.01% | 102% | 98%
Class D | 0.00% | 0.00% | -0.01% | 102% | 99% | -0.01% | -0.01% | -0.02% | 104% | 102% | 0.05% | -0.11% | 0.11% | 106% | 106%
Class F | 0.00% | 0.00% | 0.00% | 101% | 99% | -0.01% | -0.07% | -0.07% | 104% | 99% | 0.01% | 0.10% | -0.26% | 103% | 97%
AI | ECM4 | Test2 | ratio
classA | 6.7 | 6.0 | 89.6%
classB | 5.2 | 4.6 | 86.8%
classC | 3.8 | 3.6 | 96.0%
classD | 3.5 | 3.4 | 98.6%
classE | 4.2 | 3.9 | 92.6%
classF | 5.5 | 4.8 | 87.4%
RA | ECM4 | Test2 | ratio
classA | 18.1 | 17.5 | 96.7%
classB | 8.1 | 7.5 | 91.9%
classC | 4.4 | 4.3 | 96.4%
classD | 3.7 | 3.7 | 98.7%
classE |  |  | 
classF | 7.8 | 7.2 | 92.8%
LDB | ECM4 | Test2 | ratio
classA |  |  | 
classB | 7.7 | 6.9 | 88.7%
classC | 4.3 | 4.1 | 95.1%
classD | 3.5 | 3.5 | 98.6%
classE | 5.5 | 5.2 | 94.6%
classF | 6.1 | 5.4 | 89.1%
3% reduction is possible with 103% EncT

## Slide 8: Conclusion
This contribution proposes to add a print out code into VTM / ECM software
  Changes are less than 50 lines.
This contribution also provides memory reduction tests (just information).
  Maintenance of parallelism with memory reduction could be reasonable even if run-time increases if ECM encoder require more and more memory .
Thanks KDDI for crosschecking!