## Slide 1: EE2-3.2-related: IBC Adaptation for Camera-Captured Contents
Jizheng Xu

## Slide 2: Based on EE2.TEST_3.2
For CTU size being 128x128
  Two CTU row above is included in the IBC reference area
Change 1: for CTU being 256x256
  One CTU row above is included in the IBC reference area
  Does not influence the performance for classF and TGM
Change 2 (non-normative): change the 2-D per-sample search (or called local search range to be [-12,12]x[-12,12]
…
…
…
…

## Slide 3: Experimental results
Per 1% gain’s encoding time increase
ECM-4.0 vs. VTM-11.0ecm
  AI: 21.98%
Proposed vs. ECM-4.0
  AI: 15.02%
Thanks to Ofinno for cross-checking (JVET-Z0199)
 | All Intra Main 10 |  |  |  | 
 | Over ECM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.06% | -0.03% | -0.08% | 110% | 100%
Class A2 | -0.94% | -1.40% | -1.31% | 111% | 101%
Class B | -0.67% | -0.72% | -0.78% | 107% | 100%
Class C | -0.18% | -0.20% | -0.06% | 107% | 101%
Class E | -0.96% | -1.01% | -1.02% | 107% | 100%
Overall | -0.55% | -0.65% | -0.63% | 108% | 100%
Class D | -0.49% | -0.49% | -0.74% | 104% | 98%
 | Low delay B Main 10 |  |  |  | 
 | Over ECM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.03% | -0.06% | -0.45% | 106% | 98%
Class C | -0.05% | 0.22% | -0.23% | 104% | 99%
Class E | -0.25% | -0.24% | -0.50% | 103% | 99%
Overall | -0.09% | -0.01% | -0.39% | 105% | 99%
Class D | -0.02% | -0.15% | 0.01% | 105% | 101%
 | Random Access Main 10 |  |  |  | 
 | Over ECM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.10% | -0.09% | 0.20% | 99% | 101%
Class A2 | -0.22% | -0.40% | -0.21% | 98% | 97%
Class B | -0.20% | -0.32% | -0.34% | 99% | 100%
Class C | 0.23% | -0.05% | 0.18% | 98% | 100%
Class E |  |  |  |  | 
Overall | -0.03% | -0.22% | -0.07% | 99% | 100%
Class D | 0.19% | -0.27% | -0.48% | 97% | 99%

## Slide 4: Propose to
Enable IBC with the proposed adaptation for class A to E in CTC
  For class F and class TGM, keep the current TEST_3.2 setting

## Slide 5: EE2_3.2 with only the encoder change
 | All Intra Main 10 |  |  |  | 
 | Over ECM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.07% | -0.03% | -0.06% | 113% | 103%
Class A2 | -0.94% | -1.44% | -1.32% | 114% | 101%
Class B | -0.67% | -0.72% | -0.78% | 107% | 100%
Class C | -0.18% | -0.20% | -0.06% | 107% | 101%
Class E | -0.96% | -1.01% | -1.02% | 107% | 100%
Overall | -0.55% | -0.66% | -0.63% | 109% | 101%
Class D | -0.49% | -0.49% | -0.74% | 104% | 98%
 | Random Access Main 10 |  |  |  | 
 | Over ECM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.08% | -0.10% | 0.21% | 101% | 101%
Class A2 | -0.19% | -0.38% | -0.18% | 99% | 100%
Class B | -0.20% | -0.32% | -0.34% | 99% | 100%
Class C | 0.23% | -0.05% | 0.18% | 98% | 100%
Class E |  |  |  |  | 
Overall | -0.03% | -0.22% | -0.06% | 99% | 100%
Class D | 0.19% | -0.27% | -0.48% | 97% | 99%
 | Low delay B Main 10 |  |  |  | 
 | Over ECM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.03% | -0.06% | -0.45% | 106% | 98%
Class C | -0.05% | 0.22% | -0.23% | 104% | 99%
Class E | -0.25% | -0.24% | -0.50% | 103% | 99%
Overall | -0.09% | -0.01% | -0.39% | 105% | 99%
Class D | -0.02% | -0.15% | 0.01% | 105% | 101%