## Slide 1: JVET-AA0100 AHG9: On auxiliary input and separate colour description in the neural-network post-filter characteristics SEI message
Joint Video Experts Team (JVET) of ITU-T SG 16 WP 3 and ISO/IEC JTC 1/SC 29
27th Meeting, by teleconference, 13–22 july 2022
T. Shao, A. Arora, P. Yin, S. McCarthy, T. Lu, F. Pu, W. Husak (Dolby), M. M. Hannuksela, F. Cricri, M. Santamaria Gomez (Nokia), T. Chujoh, Y. Yasugi, T. Ikai (Sharp)

## Slide 2: Overview
This contribution proposes the following syntax elements for the neural-network post-filter characteristics (nnpfc) SEI message to be added to the next draft of Additional SEI messages for VSEI (JVET-Z2006):
nnpfc_auxiliary_inp_idc to indicate that auxiliary input data may be present in the neural network input tensor for any luma-chroma configuration allowed, e.g., luma-only, chroma-only, and luma-chroma configuration.
2. nnpfc_separate_colour_description_present_flag to indicate that the colour description information of the picture that results from the neural-network post filtering may be different from that of the input to the filter. When the flag equal to 1, the syntax elements nnpfc_colour_primaries, nnpfc_transfer_characteristic, and nnpfc_matrix_coeffs are present to specify the colour primaries, transfer characteristics, and matrix coefficients of the output picture.
JVET-AA0100

## Slide 3: Motivation: presence of auxiliary data in the neural-network tensor
In JVET-Z2006, auxiliary input data can be present in the neural-network input tensor only when the value of nnpfc_inp_order_idc is equal to 3.
Auxiliary input data can be present for all input tensor configurations, e.g., luma-chroma, luma-only, chroma-only.
JVET-AA0100
1. Auxiliary input

## Slide 4: nnpfc_auxiliary_inp_idc
nnpfc_auxiliary_inp_idc not equal to 0 specifies auxiliary input data is present in the input tensor of the neural-network post-filter. nnpfc_auxiliary_inp_idc equal to 0 indicates that auxiliary input data is not present in the input tensor.
nnpfc_auxiliary_inp_idc equal to 1 specifies that auxiliary input tensor is derived as specified in Table 23: adding an extra dimension of Luma SliceQP to the tensor.
JVET-AA0100

## Slide 5: Motivation: indication of colour description of neural-network output tensors
Colour description information for neural-network output tensors cannot be signalled using the current text of JVET-Z2006.
Colour description information for neural-network output tensors can be beneficial, e.g., the output filtering result for display is ICTCP resulting from neural-network post filtering of an HDR WCG signal.
JVET-AA0100
NN post filtering
An example of application of nnpfc colour description SEI
Decoded HDR/WCG frames
Filtered ICTCP frames
nnpfc colour description SEI message
Decoder
Display device
2. Separate colour description

## Slide 6: nnpfc colour description information SEI message
It is proposed to add syntax elements nnpfc_separate_colour_description_present_flag, nnpfc_colour_primaries, nnpfc_transfer_characteristic, and nnpfc_matrix_coeffs and corresponding semantics to the nnpfc SEI message
nnpfc_separate_colour_description_present_flag equal to 1 indicates that a distinct combination of colour primaries, transfer characteristics, and matrix coefficients is specified in the SEI message
nnpfc_colour_primaries, nnpfc_transfer_characteristic, and nnpfc_matrix_coeffs have the same semantics as the vui_colour_primaries, vui_transfer_characteristic, and vui_matrix_coeffs defined in ITU-T Rec. H.273.
JVET-AA0100

## Slide 7: Recommendation
Adopt the proposed syntax elements and semantics for the neural-network post-filter characteristics (nnpfc) SEI message to be added to the next draft of Additional SEI messages for VSEI (JVET-Z2006):
nnpfc_auxiliary_inp_idc to indicate that auxiliary input data may be present in the neural network input tensor for any luma-chroma configuration allowed.
nnpfc_separate_colour_description_present_flag as well as nnpfc_colour_primaries, nnpfc_transfer_characteristic, and nnpfc_matrix_coeffs to indicate and specify the colour primaries, transfer characteristics, and matrix coefficients of the output picture after filtering.
JVET-AA0100