## Slide 1: JVET-AA0119 EE2-1.4a related: Modifications of Spatial GPM Fan Wang Yue Yu, Haoping Yu, Dong Wang

## Slide 2: Introduction
In JVET-Z0124, SGPM was proposed to extend GPM in intra prediction.
SGPM employs a template-reordered candidate list and only signals the candidate index, where each candidate comprises a combination of the one partition mode and the two associated intra prediction modes.
The SGPM method was studied EE2-1.4 (JVET-AA0118). The performance in EE2-1.4a is reported as follow:
  AI {-0.20% Y, -0.08% U, -0.07% V, 123% EncT, 100% DecT}
  RA {-0.12% Y, -0.01% U, -0.12% V, 104% EncT, 101% DecT}

## Slide 3: Proposed method 1/2
Extend SGPM to smaller blocks
  i.e., SGPM can be further applied to 4x8, 8x4, 4x16 and 16x4 blocks.
Block restriction in EE2-1.4
  8<=width<=64
  8<=height<=64
  width<height*8
  height<width*8
Block restriction in this contribution
  4<=width<=64
  4<=height<=64
  width<height*8
  height<width*8
  width*height>=32

## Slide 4: Proposed method 2/2
Adaptive SGPM blending
  blending width of SGPM is directly decided by the block size. No signalling is needed for the proposed adaptive blending
  Assuming the original blending width in VVC and ECM is τ,
  the proposed adaptive SGPM blending can be described as follows:
    If min(width, height)==4, 1/2 τ is selected
    else if min(width, height)==8, τ is selected
    else if min(width, height)==16, 2 τ is selected
    else, 4 τ is selected
  In addition, similar to EE2-2.7, the range of the weights is increased from [0, 8] to [0, 32] to accommodate the increased width of the SGPM blending area.
Figure 1 Example of blending weight

## Slide 5: Simulation results

## Slide 6: Simulation results
Number of full RD for SGPM is further reduced compared with EE2-1.4
Compared with EE2-1.4, half EncT is reduced, while BD rate improved
This proposal
EE2-1.4

## Slide 7: Conclusion
This contribution proposes two modifications to the SGPM method in the EE2-1.4a test. One modification is to extend SGPM to smaller blocks, and the other is to apply an adaptive SGPM blending in the transition region between the two partitions.
It is reported that with these modifications, on top of ECM-5.0, the simulation results are
AI {-0.22% Y, -0.17% U, -0.19% V, 113% EncT, 103% DecT}, RA {-0.12% Y, -0.06% U, -0.18% V, x% EncT, x% DecT}.
It is recommended to adopt the proposed method in ECM software.

## Slide 8
Thanks to Kwai for crosschecking !