## Slide 1: JVET-AA0134 Non-EE2: POC based BCW weights derivation
Zhi Zhang, Han Huang, Chun-Chi Chen,
Vadim Seregin, Marta Karczewicz (Qualcomm)

## Slide 2: Introduction and Proposal
        In ECM, negative BCW weights are not used for non-low-delay pictures
        Weight for low-delay picture { -2, 3, 4, 5, 10 } / 8
        Weight for non-low-delay picture { 3, 4, 5 } / 8
        Add BCW weights derived based on POC difference
        Weight for low-delay picture { -3, -2, 3, 4, 5, 10, 11 } / 8
        Weight for non-low-delay picture { -2, 2, 3, 4, 5, 6, 10 } / 8
        Used for AMVP and merge mode, BCW index list size is increased by one
        MHP is not used with POC based BCW weight for AMVP mode
        Assign POC base weight to pair-wise and zero merge candidate in addition to default weight

## Slide 3: Simulation Results
BcwFast = 1
BcwFast = 0
 | Random Access Main 10 |  |  |  | 
 | Over ECM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.09% | -0.12% | -0.23% | 103% | 100%
Class A2 | -0.11% | 0.01% | -0.07% | 104% | 100%
Class B | -0.11% | -0.22% | -0.13% | 103% | 100%
Class C | -0.08% | 0.07% | -0.08% | 102% | 100%
Class E |  |  |  |  | 
Overall | -0.10% | -0.08% | -0.12% | 103% | 100%
Class D | -0.06% | -0.28% | 0.04% | 101% | 100%
Class F | -0.16% | -0.22% | -0.21% | 102% | 100%
 | Low delay B Main 10 |  |  |  | 
 | Over ECM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.04% | -0.08% | -0.07% | 107% | 101%
Class C | -0.02% | -0.17% | 0.19% | 102% | 100%
Class E | -0.10% | 0.10% | 0.40% | 108% | 101%
Overall | -0.05% | -0.07% | 0.13% | 106% | 100%
Class D | -0.08% | 1.11% | 0.24% | 102% | 99%
Class F | -0.36% | -0.50% | -0.67% | 105% | 99%
 | Random Access Main 10 |  |  |  | 
 | Over ECM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.16% | -0.16% | -0.34% | 118% | 99%
Class A2 | -0.19% | -0.20% | -0.18% | 119% | 100%
Class B | -0.19% | -0.30% | -0.32% | 117% | 100%
Class C | -0.12% | -0.11% | -0.02% | 114% | 101%
Class E |  |  |  |  | 
Overall | -0.16% | -0.20% | -0.22% | 117% | 100%
Class D | -0.11% | -0.21% | -0.07% | 112% | 101%
Class F | -0.28% | -0.31% | -0.27% | 113% | 100%
 | Low delay B Main 10 |  |  |  | 
 | Over ECM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B |  |  |  |  | 
Class C | -0.11% | -0.26% | -0.24% | 128% | 101%
Class E | -0.21% | -0.08% | -0.29% | 142% | 101%
Overall |  |  |  |  | 
Class D | -0.16% | 0.91% | 0.86% | 123% | 100%
Class F | -0.39% | -0.24% | -0.10% | 127% | 99%

## Slide 4: Thanks for Alibaba and Kwai for cross checking