## Slide 1
JVET-AA0143
Non-EE2: Simplification methods for OBMC
K. Kim (Kyle), D. Kim, J. Son, J. Kwak
July, 2022
WILUS Inc.

## Slide 2: OBMC in ECM-5.0
Step 1. When OBMC is applied, the prediction value of CU boundary samples derivation approach is decided according to the template matching costs.
  3 blending mode & non-blending mode (obmc off mode)
Step 2. After a template matching based OBMC is applied, a sub-block OBMC is applied to all subblocks for the sub-block based coding tools.
  Only 1 blending mode
B
A
L
Current
sub-block
R
Template
Current
coding block
1. OBMC in CU boundary
based on TM cost
2. OBMC in sub-block
based on coding mode and condition

## Slide 3: Proposed method
1. Removal of ‘obmc_flag’ syntax
  The ‘obmc_flag’ syntax signalled in every CU is removed and is inferred to ‘true’ for inter CUs. For OBMC on/off decision, a template matching based OBMC in ECM-5.0 is used.
    Encoder would save memory associated with OBMC on/off decision and would reduce signaling overhead.
2. Disable a sub-block OBMC based on CU boundary OBMC
  If a template matching based OBMC has not been performed on any CU boundary block, a sub-block OBMC is also not applied for the CU.
    This approach would help improve coding efficiency, especially in the screen contents.
3. OBMC restriction in large block size
  In ECM-5.0, when the block size cbW x cbH is less than 32, OBMC is not applied.
  When the block size cbW * cbH is greater than or equal to 32 (ECM-5.0) and cbW and cbH is less than 128(additional restriction), OBMC is applied.
    This approach would help significantly reduce the complexity.

## Slide 4: Experimental results
Anchor: ECM-5.0
  Under CTC
 | Random Access Main 10 |  |  |  | 
 | Over ECM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.04% | 0.07% | -0.03% | 98% | 85%
Class A2 | 0.06% | 0.23% | 0.14% | 98% | 84%
Class B | 0.04% | 0.13% | 0.01% | 99% | 87%
Class C | 0.00% | 0.16% | 0.09% | 100% | 97%
Class E |  |  |  |  | 
Overall | 0.03% | 0.15% | 0.05% | 99% | 88%
Class D | 0.03% | -0.06% | 0.09% | 100% | 96%
Class F | -0.04% | 0.06% | 0.07% | 100% | 94%
Class TGM | -0.25% | -0.30% | -0.28% | 100% | 98%
 | Low delay B Main 10 |  |  |  | 
 | Over ECM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.04% | 0.01% | 0.26% | 101% | 93%
Class C | 0.01% | 0.10% | -0.08% | 101% | 99%
Class E | 0.07% | 0.80% | 0.09% | 101% | 95%
Overall | 0.04% | 0.24% | 0.10% | 101% | 96%
Class D | -0.03% | 0.87% | 1.05% | 101% | 99%
Class F | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class TGM | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!

## Slide 5: Conclusion
This contribution proposes several simplification methods about OBMC.
  By removal of ‘obmc_flag’ syntax, encoder would save a memory associated with OBMC on/off decision.
  The method about sub-block OBMC is a straight-forward design and help improve coding efficiency, especially in the screen contents.
  By restricting OBMC in large block size, the decoding run time significantly is reduced.
It is recommended to adopt the proposed method in the next version of ECM.
Thank kwai for crosscheck.

## Slide 6: THANK YOU