## Slide 1: JVET-AB0045 AHG10: study of VVC spatial scalability performance
P. de Lagrange, G. Marquant, C. Salmon-Legagneur, F. Urban (InterDigital)

## Slide 2: Context
VVC multilayer profile  scalability (quality, spatial, temporal)
  From version 1 (no extension, no external codec)
  With a single decoder
JVET-Y0047: HD+UHD visual test with equal EL/BL bitrate: losses vs single-layer
JVET-Y0048: exploring EL/BL rate allocation: strong performance impact (~on par or better than single-layer)
 Visual testing with optimized rate allocation, other scaling ratios ?
Notes: VVC = no extension to get scalability (in comparison with HEVC)
JVET-Y0047: VVC spatial scalability visual coding performance with equal bitrate for HD base layer (BL) and UHD enhancement layer (EL)
JVET-Y0048: showed that the bitrate balance has a significant impact on (objective) coding performance, in favor of more bitrate in the base layer .

## Slide 3: EL/BL rate balance exploration
Fixed HD base layer QP
  e.g. QP(BL) = [26, 29, 32, 36]
For each QP(BL), sweep UHD enhancement layer QP
  e.g. for QP(BL) = 26, test QP(EL) = 29 to 45
Single-layer UHD reference
  Select QP with quality similar to EL
HD base layer upscale as a 2nd reference
Notes: To draw quantitative conclusions on the performance impact of bitrate allocation in scalable VVC, we evaluate performance of single layer VVC vs dual layer VVC exploring various quantization parameters for the base layer and enhancement layer.
We can note that the two extremes of EL/BL bitrate allocation are:
• single layer (SL) on one side (no bitrate on base layer),
• and pure upscale on the other side (no bitrate on enhancement layer).
Test with VTM 17.0, 4:2:0 multilayer profile, RA CTC configuration + spatial scalability (HD+UHD)

## Slide 4: EL/BL rate balance exploration
For each base layer QP
  High QP(EL): low bitrate, starts on upscale curve
  Lower QP(EL): increasing bitrate, quality improves (can outperform single layer)
  Low QP(EL): bitrate increase, but slower quality increase. Inter-layer prediction not as useful, base layer becomes an overhead
High impact of EL/BL QP balance
Notes: This figure illustrates dual-layer coding performance comparison between DL / SL / UpsBL , depending on the Quantization parameters QP for each layer.
For multiple QP of the base layer, we vary the QP of the EL.
Quality is measured using PSNR of Y component.
The graph depicts PSNR curves: single layer (displayed as a dashed blue curve), and dual layer configurations for a set of (QPBL, QPEL) points.
Additionally, upscaled base layer is displayed as a dashed green curve
The figure shows that, for a given QPBL, a “coma”-shaped trace appears while following the QPEL sweep.
For each QPBL, sweep is expected to start on the upscaled base layer curve (with high enough QPEL), next quality increases with the EL bitrate and can outperform the single layer quality. Then, each “coma” slope diminishes when QPEL decreases

## Slide 5: EL/BL rate balance exploration
For each base layer QP
  High QP(EL): bitrate < 2%, starts on upscale curve
  Lower QP(EL): bitrate 2 to 15%, quality improves (can outperform single layer)
  Low QP(EL): bitrate > 15%, slower quality increase. Inter-layer prediction not as useful, base layer becomes an overhead
High impact of EL/BL QP balance
Notes: Exploring various quantization parameters on each layer is equivalent to study the bitrate allocation between base layer (BL) and enhancement layer (EL).
The figure displays the same RD results but with the ratio of the enhancement layer bitrate to the global bitrate.
It can be noticed that when the QPEL is very low, i.e. EL bitrate is large, then the enhancement layer does not improve any more the rate-distortion performance and the curve drops below the single layer (pink crosses in Figure) because of base layer overhead.
When allocating between 2% and 15% of the global bitrate to the enhancement layer and the remaining to the base layer, it can be noticed that, for low to medium bitrates, dual-layer coding can outperform both single-layer and upscaled base layer.
At high bitrates, quality of upscaled base layer saturates, while UHD details coded by EL or single layer start to make a significant difference. Actually, inter-layer prediction is less and less used when EL bitrate increases, ultimately making the BL a useless overhead. According to Figure, best results for dual layer are obtained using 5-15% of the global bitrate for the enhancement layer (generally when QPEL = QPBL + 7 (+/- 1))

## Slide 6: EL/BL rate balance, PSNR vs MS-SSIM
Notes: Just one example (see document for other examples)
Showing two rate balances: 10% total and 50/50
MS-SSIM more favorable to dual-layer. We will see that it correlates with visual observation.

## Slide 7: Test sequences
CampFire
CorsaireJoy
Procession
FoodMarket4
Fortnite
Marathon2

## Slide 8: BD-rates with selected QP pairs
Name | QPBL/EL | QPSL | BD-rate vs single layer (PSNR_Y) | BD-rate vs single layer (SSIM_Y) | BD-rate vs single layer (VMAF)
Campfire | 24/32, 28/36, 34/42, 38/46 | 29, 35, 40, 44 | -2.7 % | -8.7 % | -5.8 %
CorsaireJoy | 26/33, 29/36, 32/40, 36/44 | 31, 35, 38, 42 | -2.9 % | -8.7 % | -6.5 %
Procession | 29/36, 32/40, 36/44, 40/47 | 35, 38, 42, 46 | -3.9 % | -6.6 % | -6.2 %
FoodMarket4 | 30/38, 34/44, 38/48, 42/50 | 36, 40, 44, 48 | -4.9 % | -9.5 % | -7.7 %
Fortnite | 30/38, 34/42, 38/46, 42/51 | 36, 40, 44, 48 | +4.2 % | -7.2 % | -2.0 %
Marathon2 | 26/35, 32/44, 36/46, 40/50 | 32, 38, 43, 46 | +0.0% | -5.1% | -3.6%
Average |  |  | -1.7% | -7.6% | -5.3%
Dependent on bitrate: more gains at low bitrates, losses likely at high bitrates

## Slide 9: Visual tests results
CampFire
CorsaireJoy
Notes: 17 test subjects, 1 rejected

## Slide 10: Visual tests results
Procession
FoodMarket4

## Slide 11: Visual tests results
Fortnite
Marathon2

## Slide 12: Preliminary 3x tests
Lower performance than 2x
EL still provides quality improvement even at low additional bitrate
3x upscale crosses single layer at much lower bitrate than 2x (as expected)
Notes: Caveat: single-stage 3x downscale. Could be better with dual-stage (UHD > HD then HD > 720)