## Slide 1: JVET-AB0052 EE1-1.5: One luma model with IPB and/or skip for filtering intra and inter luma slices
Du Liu, Jacob Ström, Mitra Damghanian, Per Wennersten, Kenneth Andersson

## Slide 2: Overview
Propose to use one luma model with block type information and/or block skip information for NN-filtering
  Block type information: I, P, B
  Block skip information: bypassed or not
The proposed model is used for both intra luma and inter luma slices
Reduce the total number of models from 4 (JVET-AA0111, equivalent to NCS-1.0 filter set 1) to 3
Reduce the total number of parameters from 6.24M (JVET-AA0111) to 4.67M~4.70M
Use one model for both intra and inter slices:
Test 1.5.1 tests the model proposed in JVET-AA0090 which has two additional inputs IPB and skip.
Test 1.5.2 tests the model with one additional input IPB.
Test 1.5.3 tests the model with one additional input skip.
Test 1.5.4 tests the original inter luma model in JVET-AA0111, i.e., the model in Test 1.5.1 without IPB or skip.

## Slide 3: NN structure with IPB and skip
Head of the network
Eight residual blocks
Last part of the network

## Slide 4: Summary of complexity and performance
The intra chroma model has a complexity of 110 kMAC/sample and 1.566M parameters. The inter chroma model has a complexity of 107 kMAC/sample and 1.555M parameters
Test/Luma model | Nbr. of luma models | kMAC/ sample (Y) | kMAC/pix (YUV) for AI | kMAC/pix (YUV) for RA | kMAC/pix (YUV) worst case (frame-basis) | kMAC/pix (YUV) worst case (block-basis) | Nbr. of param. of the inter luma model (106) | Num. of param. in total (106) | Total mem. (106 bytes) | RA BDR-Y (vs. NNVC-2.0) | RA BDR-Y (vs. JVET-AA0111)
JVET-AA0111 floating | 2 | 429 for intra 418 for inter | 539 | 525 | 539 | 682 | 1.551 | 6.24 (luma inter + luma intra + chroma inter + chroma intra) | 24.94 | -9.42% | 0
Test 1.5.1: IPB+skip model | 1 | 440 | 550 | 547 | 550 | 696 | 1.576 | 4.70 (luma + chroma inter + chroma intra) | 18.79 | -9.57% | -0.17%
Test 1.5.2: IPB model | 1 | 429 | 539 | 536 | 539 | 682 | 1.563 | 4.68 (luma + chroma inter + chroma intra) | 18.74 | -9.52% | -0.11%
Test 1.5.3: Skip model | 1 | 429 | 539 | 536 | 539 | 682 | 1.563 | 4.68 (luma + chroma inter + chroma intra) | 18.74 | -9.37% | 0.04%
Test 1.5.4: Original model | 1 | 429 | 528 | 525 | 528 | 668 | 1.551 | 4.67 (luma + chroma inter + chroma intra) | 18.69 | -9.14% | 0.30%

## Slide 5: Training
Network Information in Training Stage |  | 
Mandatory | GPU Type | GPU: NVIDIA A100-PCIE-40GB
 | Framework: | PyTorch v1.9
 | Number of GPUs per Task | 1
 | Epoch: | 340
 | Batch size: | 32 (L1) and 16 (L2)
 | Loss function: | Weighted L1 and L2
 | Training time: | 15 days (Test 1) 14 days (Test 2) 14 days (Test 3) 12 days (Test 4)
 | Training data information: | DIV2K, BVI-DVC
 | Training configurations for generating compressed training data (if different to VTM CTC): | VTM-11.0 + new MCTF, qp {17, 22, 27, 32, 37, 42}
Optional |  | 
 | Number of iterations | 
 | Patch size | 256x256
 | Learning rate: | 1e-4 and 1e-5
 | Optimizer: | ADAM
 | Preprocessing: | 
 | Mini-batch selection process: | 
 | Other information: | 

## Slide 6: Inference
Network Information in Inference Stage |  | 
Mandatory | HW environment: | 
 | GPU Type | N/A
 | Framework: | SADL
 | Number of GPUs per Task | 0
 | Total Parameter Number | See Table 1
 | Parameter Precision (Bits) | fp32
 | Memory Parameter (MB) | See Table 1
 | Multiplay Accumulate (MAC) | See Table 1
Optional |  | 
 | Total Conv. Layers | 
 | Total FC Layers | 
 | Total Memory (MB) | 
 | Batch size: | 1
 | Patch size | 128x128, 256x256
 | Changes to network configuration or weights required to generate rate points | 
 | Peak Memory Usage (Total) | 
 | Peak Memory Usage (per Model) | 
 | Border handling | 
 | Other information: | 

## Slide 7: Results
Test 1.5.1 The IPB+skip model
  Worst case 696 kMAC/pix and num. of para. 4.70M
  Vs. NNVC-2.0, BDR-Y: -9.57% RA, -8.30% LDB, and -7.37% AI.
  Vs. JVET-AA0111, BDR-Y: -0.17% RA, 0.13% LDB, and -0.13% AI.
Test 1.5.2: Test the IPB model used for intra luma and inter luma slices.
  Worst case 682 kMAC/pix and num. of para. 4.68M
  Vs. NNVC-2.0, BDR-Y: -9.52% RA, -8.15% LDB, and -7.39% AI.
  Vs. JVET-AA0111, BDR-Y: -0.11% RA, 0.29% LDB, and -0.16% AI.

## Slide 8: Results
Test 1.5.3: Test the skip model used for intra luma and inter luma slices.
  Worst case 682 kMAC/pix and num. of para. 4.68M
  Vs. NNVC-2.0, BDR-Y: -9.37% RA, -8.23% LDB, and -7.36% AI.
  Vs. JVET-AA0111, BDR-Y: 0.04% RA, 0.20% LDB, and -0.12% AI.
Test 1.5.4: Test the original inter luma model from JVET-AA0111 (without IPB or skip) used for intra luma and inter luma slices.
  Worst case 668 kMAC/pix and num. of para. 4.67M
  Vs. NNVC-2.0, BDR-Y: -9.14% RA, -8.11% LDB, and -7.33% AI
  Vs. JVET-AA0111, BDR-Y: 0.30% RA, 0.33% LDB, and -0.09% AI

## Slide 9: Conclusions
This contribution contains four tests to show the impact of having the extra input IPB and the extra input skip where the network is used for both intra luma and inter luma slices.
It is reported that, comparing to JVET AA0111 under RA configuration
  Test 1.5.1 the IPB+skip model is 2.0% higher in complexity and gives 0.17% higher luma gain
  Test 1.5.2 the IPB model is of the same complexity and gives 0.11% higher luma gain
  Test 1.5.3 the skip model is of the same complexity and gives 0.04% luma loss
  Test 1.5.4 the original model is 2.0% lower in complexity and gives 0.30% luma loss.
All the tests reduce the number of models from 4 to 3, which saves the effort of training one extra model
The total number of parameters is reduced from 6.24M to 4.67~4.70M.
It is proposed to adopt the luma model in Test 1.5.1 or Test 1.5.2 into the NN common software base (NCS)
Thanks to Tencent for cross-checking!