## Slide 1: EE2-1.16 related : Modifications of picture-level geometry transform (JVET-AB0103)
Jangwon Choi

## Slide 2: Summary
Suggest two modifications, compare to EE2-1.16
  Method1 : only vertical flip geometry transform is considered
  Method2 : edge feature based geometry transform selection method on top of Method1, without picture size restriction
Experimental results (AI, based on ECM6 anchor)
  Method1 : Y -0.20%, Cb -0.31%, Cr -0.34% with 100% encoding complexity
  Method2 : Y -0.17%, Cb -0.29%. Cr -0.36% with 100% encoding complexity
Thanks to Bytedance for cross-checking (JVET-AB0222)

## Slide 3: Proposed method 1
Only vertical flip geometry transform is considered
  The vertical flip is only used, instead of previous 3 flip modes (vertical flip, horizontal flip, 180 rotation)
  One bit flag is signalled to indicate if the vertical flip is applied or not
  The number of RD comparing process is reduced in the encoding stage compared to EE2-1.16
 | All Intra Main 10 |  |  |  | 
 | Over ECM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.23% | -0.29% | -0.25% | 101% | 98%
Class A2 | -0.48% | -0.32% | -0.31% | 101% | 98%
Class B | -0.29% | -0.75% | -0.89% | 100% | 97%
Class C | 0.00% | 0.00% | 0.00% | 101% | 100%
Class E | 0.00% | 0.00% | 0.00% | 100% | 98%
Overall | -0.20% | -0.31% | -0.34% | 100% | 98%
Class D | 0.00% | 0.00% | 0.00% | 101% | 101%
Class F | -0.06% | -0.10% | 0.03% | 102% | 97%
Class TGM | -0.63% | -0.47% | -0.52% | 110% | 101%
Experimental result of Method1
 | Random Access Main 10 |  |  |  | 
 | Over ECM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class A2 | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class B | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class C | 0.00% | 0.00% | 0.00% | 99% | 98%
Class E |  |  |  |  | 
Overall | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class D | 0.00% | 0.00% | 0.00% | 99% | 98%
Class F | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class TGM | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!

## Slide 4: Proposed method 1
Only vertical flip geometry transform is considered
  Similar coding performance, compared to EE2-1.16, with some reduced encoding complexity
 | All Intra Main 10 |  |  |  | 
 | Over ECM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.23% | -0.29% | -0.25% | 101% | 98%
Class A2 | -0.48% | -0.32% | -0.31% | 101% | 98%
Class B | -0.29% | -0.75% | -0.89% | 100% | 97%
Class C | 0.00% | 0.00% | 0.00% | 101% | 100%
Class E | 0.00% | 0.00% | 0.00% | 100% | 98%
Overall | -0.20% | -0.31% | -0.34% | 100% | 98%
Class D | 0.00% | 0.00% | 0.00% | 101% | 101%
Class F | -0.06% | -0.10% | 0.03% | 102% | 97%
Class TGM | -0.63% | -0.47% | -0.52% | 110% | 101%
Experimental result of Method1
Experimental result of EE2-1.16
 | All Intra Main10 |  |  |  | 
 | Over ECM_6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.20% | -0.16% | 0.02% | 102% | 100%
Class A2 | -0.52% | -0.43% | -0.34% | 102% | 101%
Class B | -0.29% | -0.38% | -0.71% | 102% | 100%
Class C | 0.00% | 0.00% | 0.00% | 100% | 97%
Class E | 0.00% | 0.00% | 0.00% | 100% | 98%
Overall | -0.20% | -0.20% | -0.25% | 101% | 99%
Class D | 0.00% | 0.00% | 0.00% | 101% | 98%
Class F | -0.06% | -0.10% | 0.00% | 106% | 99%

## Slide 5: Proposed method 2
Edge feature based geometry transform selection method on top of Method1
  Replacing the RD comparing process of encoder in Method 1
  Also the size restriction of picture height in EE2-1.16 which is enabling the geometry transform over 720 is also removed
  Decision process of geometry transform in encoder :
    Robinson edge detection filters are applied in all pixels of picture, and decide the edge type of each pixel which is one of 8 directions (E, NE, N, NW, W, SW, S, SE)
    Calculate the number of pixels of each edge directions, and
    If , the vertical flip of geometry transform is applied in the corresponding picture
8 edge detection filter in Robinson method

## Slide 6: Proposed method 2
Edge feature based geometry transform selection method on top of Method1
  Replacing the RD comparing process of encoder in Method 1
  Also the size restriction of picture height in EE2-1.16 which is enabling the geometry transform over 720 is also removed
 | All Intra Main 10 |  |  |  | 
 | Over ECM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.25% | -0.31% | -0.29% | 99% | 97%
Class A2 | -0.25% | -0.28% | -0.27% | 100% | 98%
Class B | -0.32% | -0.73% | -0.95% | 99% | 97%
Class C | -0.01% | 0.02% | -0.03% | 100% | 98%
Class E | 0.01% | 0.04% | 0.02% | 100% | 97%
Overall | -0.17% | -0.29% | -0.36% | 100% | 97%
Class D | -0.05% | -0.18% | -0.16% | 100% | 102%
Class F | -0.11% | -0.21% | 0.07% | 100% | 96%
Class TGM | -0.55% | -0.40% | -0.48% | 102% | 102%
Experimental result of Method2
 | Random Access Main 10 |  |  |  | 
 | Over ECM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class A2 | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class B | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class C | 0.00% | -0.04% | 0.08% | 98% | 97%
Class E |  |  |  |  | 
Overall | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class D | 0.03% | 0.04% | -0.33% | 99% | 97%
Class F | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class TGM | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!