## Slide 1: JVET-AB0150 Crosscheck of JVET-AB0118 (EE2-2.5a: Enhanced temporal motion information derivation)
Lien-Fei Chen, Guichun Li, Xiaozhong Xu, Xin Zhao, and Shan Liu

## Slide 2: Subblock-Based Template-Matching for SbTMVP in Test 2.5a
One issue about template-matching for SbTMVP is addressed
  Inter Dir of subblock template is set same as Center Subblock
  For each Ref List LX, MVLX of subblock template is set to
    if RefIdx_LXAdjacent == RefIdxLXCenter Adjacent subblock MVLX
    otherwise MV(0, 0)
gray block: subblock template
(0,0) is the initialized MV at buffer initialization

## Slide 3: Proposed Subblock-Based Template-Matching for SbTMVP
MVA-L0
MVA-L1
MVB-L0
MVB-L1
MVC-L0
MVD-L0
MVE-L1
MVF-L1
MVG-L0
MVG-L1
MVA-L0
MVA-L1
MVB-L0
MVB-L1
MVC-L0
MVD-L0
MVA-L0
MVA-L1
MVE-L1
MVF-L1
MVG-L0
MVG-L1
Proposed modification of template-matching for SbTMVP
  MV of each subblock template is simply copied from the adjacent subblock MV
gray block: subblock template

## Slide 4: Simulation Results
Test 2.5a
Our modification over Test 2.5a
Test 2.5a | Random Access Main 10 |  |  |  | 
 | Over ECM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.10% | -0.23% | -0.05% | 101% | 102%
Class A2 | -0.11% | -0.09% | -0.19% | 101% | 102%
Class B | -0.07% | -0.11% | -0.23% | 102% | 102%
Class C | -0.20% | -0.18% | -0.21% | 103% | 103%
Class E |  |  |  |  | 
Overall | -0.12% | -0.15% | -0.18% | 102% | 102%
Class D | -0.12% | -0.11% | -0.05% | 103% | 103%
Class F | -0.03% | -0.13% | -0.05% | 102% | 102%
Test 2.5a | Low delay B Main10 |  |  |  | 
 | Over ECM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.08% | -0.16% | 0.31% | 103% | 102%
Class C | -0.27% | -0.28% | -0.20% | 105% | 106%
Class E | -0.04% | 0.76% | 0.54% | 103% | 102%
Overall | -0.14% | 0.03% | 0.20% | 104% | 104%
Class D | -0.16% | -0.06% | 0.82% | 104% | 105%
Class F | -0.12% | -0.46% | -0.41% | 102% | 104%
Test 2.5a-mod | Random Access Main 10 |  |  |  | 
 | Over Test 2.5a |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | 0.08% | 0.03% | 100% | 99%
Class A2 | 0.02% | 0.03% | 0.04% | 100% | 100%
Class B | 0.00% | 0.05% | -0.02% | 99% | 100%
Class C | 0.00% | 0.09% | 0.01% | 99% | 100%
Class E |  |  |  |  | 
Overall | 0.00% | 0.06% | 0.01% | 100% | 100%
Class D | -0.03% | -0.02% | -0.03% | 100% | 101%
Class F | -0.02% | 0.00% | -0.05% | 100% | 100%
Test 2.5a-mod | Low delay B Main10 |  |  |  | 
 | Over Test 2.5a |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.02% | -0.12% | 0.03% | 100% | 99%
Class C | -0.02% | 0.03% | 0.15% | 98% | 99%
Class E | 0.02% | -0.82% | -0.32% | 100% | 98%
Overall | -0.01% | -0.25% | -0.02% | 99% | 99%
Class D | -0.02% | -0.19% | -0.66% | 100% | 100%
Class F | -0.15% | -0.22% | 0.12% | 100% | 101%

## Slide 5: Conclusion
One issue on subblock-based template-matching for SbTMVP is addressed
  A modification is proposed on this issue
    No runtime impact
    Average results show that
      There is no BDBR impact for luma in RA and LB
      Slightly better coding gain for chroma in LB
    Better coding gain in class F
      -0.15%/-0.22%/0.12%
Recommended to adopt this modification to Test 2.5a
Thanks Bytedance for the crosscheck !