## Slide 1: JVET-AB0186: Modification of extended offline-filter taps for ALF
Ikram Jumakulyyev, Nan Hu, Vadim Seregin, Marta Karczewicz (Qualcomm)

## Slide 2: Online trained coefficients of ALF in ECM 6.0
Taps:
#0~#19: Applied to neighboring reconstructed samples
#20~#21: Applied to offline-filtered results
#22~#24: Applied to samples before
deblocking filter.

## Slide 3: Online trained coefficients of ALF in EE2-5.1
Taps:
#0~#19: Applied to neighboring reconstructed samples
#20~#27: Applied to offline-filtered results
#22~#24: Applied to samples before
deblocking filter.

## Slide 4: Our proposal: Offline-filtered taps further extended
Taps:
#0~#19: Applied to neighboring reconstructed samples
#20~#31: Applied to offline-filtered results
#22~#24: Applied to samples before
deblocking filter.

## Slide 5: Simulation Results
 | AI |  |  |  |  | RA |  |  |  |  | LDB |  |  |  | 
 | Over ECM-6.0 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.11% | 0.01% | 0.01% | 107% | 105% | -0.10% | -0.05% | 0.03% | 101% | 101% |  |  |  |  | 
Class A2 | -0.14% | 0.02% | 0.02% | 104% | 106% | -0.14% | 0.10% | 0.01% | 101% | 101% |  |  |  |  | 
Class B | -0.07% | 0.03% | 0.03% | 104% | 105% | -0.19% | 0.08% | -0.07% | 103% | 103% |  |  |  |  | 
Class C | -0.09% | 0.03% | 0.03% | 102% | 100% | -0.25% | -0.06% | -0.01% | 100% | 99% | -0.35% | -0.14% | 0.22% | 100% | 100%
Class E | -0.14% | 0.02% | 0.02% | 105% | 103% |  |  |  |  |  | -0.08% | 0.21% | 0.90% | 107% | 100%
Overall | -0.11% | 0.02% | 0.02% | 104% | 104% | -0.18% | 0.02% | -0.02% | 101% | 102% |  |  |  |  | 
Class D | -0.04% | 0.07% | 0.07% | 104% | 99% | -0.47% | -0.23% | -0.07% | 104% | 101% | -0.54% | -0.12% | 0.73% | 104% | 100%
Class F | -0.10% | 0.05% | 0.05% | 103% | 104% | -0.09% | 0.00% | 0.01% | 110% | 103% |  |  |  |  | 
Anchor results of random access with QP 22 are used for test for sequences Tango2, DaylightRoad2 and ParkRunning3.

## Slide 6: Simulation Results
 | AI |  |  |  |  | RA |  |  |  |  | LDB |  |  |  | 
 | Over EE2-5.1 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.02% | 0.01% | 0.01% | 103% | 103% | -0.03% | 0.19% | -0.03% | 99% | 101% |  |  |  |  | 
Class A2 | -0.03% | 0.01% | 0.01% | 102% | 104% | -0.03% | 0.02% | 0.07% | 99% | 100% |  |  |  |  | 
Class B | -0.01% | 0.01% | 0.01% | 102% | 103% | -0.02% | -0.07% | 0.02% | 102% | 101% |  |  |  |  | 
Class C | -0.03% | 0.01% | 0.01% | 101% | 101% | -0.10% | -0.03% | 0.00% | 100% | 99% | -0.08% | 0.43% | 0.10% | 98% | 98%
Class E | 0.00% | -0.02% | -0.02% | 102% | 101% |  |  |  |  |  | 0.01% | 0.02% | 0.78% | 102% | 99%
Overall | -0.02% | 0.01% | 0.01% | 102% | 102% | -0.04% | 0.01% | 0.01% | 100% | 101% |  |  |  |  | 
Class D | -0.01% | 0.02% | 0.02% | 102% | 99% | -0.26% | -0.08% | -0.15% | 101% | 99% | -0.24% | 0.14% | 0.35% | 100% | 98%
Class F | -0.03% | 0.02% | 0.02% | 102% | 102% | -0.05% | 0.00% | 0.09% | 104% | 101% |  |  |  |  | 
Anchor results of random access with QP 22 are used for test for sequences Tango2, DaylightRoad2 and ParkRunning3.

## Slide 7
Thank you for your attention!
Thanks to Ericsson for cross-checking!​