## Slide 1: JVET-aB0191 Non-EE2: Combined intra block copy and intra mode
Changyue Ma, Xiaoyu Xiu, Wei Chen, Che-Wei Kuo, Hong-Jheng Jhu, Ning Yan, Xianglin Wang

## Slide 2: Introduction
In ECM-6.0, CIIP combines inter merge mode and intra mode.
1) The inter merge mode can be regular merge mode or TM merge mode.
2) The intra mode can be PDPC mode or the TIMD.
3) If intra is planar mode, the weights for intra/inter samples are uniform in the whole CU.
4) If intra is angular mode, the weights for intra/inter samples are varying for different positions of the CU.
In ECM-6.0, IBC is utilized.
1) IBC AMVP and IBC merge.
2) Under CTC, IBC is enabled for SCC sequences but is disabled for natural sequences.

## Slide 3: Proposal
Combine IBC with intra prediction
The design of the proposed scheme is similar to that of the existing CIIP, except that the inter part in CIIP is replaced with the IBC.
The IBC regular merge mode or IBC TM merge mode is combined with the PDPC mode or the TIMD mode.
Current Syntax Change
  A flag is first signalled to indicate whether a combined IBC and intra prediction mode is applied.
  If this flag is true, another flag is signaled to indicate whether the intra part is based on the TIMD or the PDPC.

## Slide 4: Performance evaluation
Test 1: Proposed combined IBC and intra method
Over ECM6.0 IBC On |  |  |  |  |  |  |  |  |  | 
 | All Intra |  |  |  |  | Random Access |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.01% | -0.10% | 0.00% |  |  |  |  |  |  | 
Class A2 | -0.18% | -0.31% | -0.24% |  |  |  |  |  |  | 
Class B | -0.09% | -0.21% | -0.11% |  |  | -0.03% | -0.06% | 0.09% |  | 
Class C | -0.03% | -0.11% | -0.15% |  |  | 0.03% | -0.10% | -0.15% |  | 
Class E | -0.10% | -0.29% | -0.31% |  |  |  |  |  |  | 
Overall | -0.08% | -0.20% | -0.16% |  |  |  |  |  |  | 
Class D | 0.00% | -0.17% | 0.00% |  |  | -0.01% | 0.05% | -0.04% |  | 
Class F | -0.09% | -0.10% | 0.04% |  |  | 0.00% | -0.05% | 0.10% |  |