## Slide 1: Preliminary report on subjective performance evaluation of the ECM
JVET-AB0270
M. Wien, V. Baroncini

## Slide 2: Experts viewing in Mainz

## Slide 3: Test data
ECM6.0 vs. VTM-11.0 with ECM-compatible configuration
Bittreams generated and crosschecked by volunteers
Test set with 4 rate points per sequence sequence duration: 10sec
  UHD 2*7*4 = 56 rate points
  HD 2*2*3*4 = 48 rate points
Rate matching: ECM rate ≤ VTM rate (dev. max 2%)
Class | Sequence name | fps | Frames
UHD RA | Campfire | 30 | 300
UHD RA | CatRobot1 | 60 | 600
UHD RA | DaylightRoad2 | 60 | 600
UHD RA | DrivingPOV3 | 60 | 600
UHD RA | Marathon2 | 30 | 300
UHD RA | MountainBay2 | 30 | 300
UHD RA | TallBuildings2 | 30 | 300
HD RA | BQTerrace | 60 | 600
HD RA | Cactus | 50 | 500
HD RA | Meridian2 | 60 | 600
HD LD | Beatriz | 50 | 500
HD LD | EuroTruckSimulator2 | 60 | 600
HD LD | DOTA2 | 60 | 600

## Slide 4: Test Logistics in Mainz
Displays: 2× LG 65” E9, HDMI (3840×2160), 3 viewers each, at 1.5H; displays driven by PC with playout to HDMI via a video board
Viewers located at ±75°, 90°
24 experts, confirmed for visual acuity and normal colour vision

## Slide 5: Test setup
DCR method using the 11-grade scale
  “Original” (1sec)
  [uncompressed sequence] (10sec)
  “A” (1sec)
  [PVS] (10sec)
  “Vote <N>” (5sec)
UHD-RA: 3 test sessions with 24 basic test cells (BTCs)
HD-RA+LD: 3 test sessions with 21 BTCs

## Slide 6: Test design and data processing
Session design
  Stabilization phase (results not considered in evaluation)
  Include comparison original vs. original
Processing of results
  Total of 6 cases with viewers voting below score of 8 for the original: results of corresponding session not regarded
  Outlier detection, BT.500 method: triggered for one participant
  Further refinement: removal of isolated outliers

## Slide 7: HD-LD

## Slide 8: HD-LD

## Slide 9: HD-LD

## Slide 10: HD-RA

## Slide 11: HD-RA

## Slide 12: HD-RA

## Slide 13: UHD-RA

## Slide 14: UHD-RA

## Slide 15: UHD-RA

## Slide 16: UHD-RA

## Slide 17: UHD-RA

## Slide 18: UHD-RA

## Slide 19: UHD-RA

## Slide 20: Formal subjective assesment in Rome

## Slide 21: Logistics
Test conducted in the Rome VABTech test laboratory
Two viewing rooms
4K display (set to 1920x1080 resolution for HD test*)
Three subjects for each viewing room
Viewing distance: 1,5H for UHD; 3H for HD
24 viewers, all aging between 19 and 24 and visual checked for acuity and color blindness (18 females, 6 males)
Accurate viewers training with dedicated training session
Post test data processing and viewers screening (none excluded)
* 2K setting prevents from alias figures

## Slide 22: Test configurations
Same bitstreams used for expert viewing in Mainz (plus VVenc)
Two screen resolutions: HD, UHD
HD test
  ECM vs. VTM
  Two coding configurations: LD and RA
  Three test sequences for LD; three test sequences for RA
  Four bit rates
UHD test
  ECM vs. VTM vs. VVenc in RA configuration only
  Six test sequences (originally 7; one discarded)
  Four bit rates

## Slide 23: Test design
DSIS method (Rec. ITU-R BT 500-14)
11-grade scale
Paper scoring sheets
HD-RA+LD: 2 test sessions with 27 basic test cells (BTCs)
UHD-RA: 3 test sessions with 27 (BTCs)
Stabilization phase in each session made of three BTC
Intense and accurate viewers training

## Slide 24: Data processing
MOS; 5% CI
Pearson correlation (> 0.9 for all viewers)
Outlier detection (less that 15 scores over a total of 4023 scores)
Score consistency subject by subject and for each test case
Stabilization scores discarded

## Slide 25: HD test results - LD
 |  |  | QP | Mean | CI | bit rate
Beatriz | LD | ECM | qp30 | 7,43 | 0,24 | 524.565
 |  |  | qp34 | 5,79 | 0,32 | 273.125
 |  |  | qp38 | 4,21 | 0,27 | 166.421
 |  |  | qp42 | 3,21 | 0,20 | 109.779
 |  | VTM | qp30 | 6,71 | 0,22 | 505.629
 |  |  | qp34 | 4,93 | 0,28 | 250.524
 |  |  | qp38 | 3,29 | 0,34 | 145.182
 |  |  | qp42 | 2,21 | 0,41 | 87.073

## Slide 26: HD test results - LD

## Slide 27: HD test results - LD

## Slide 28: HD test results - RA

## Slide 29: HD test results - RA

## Slide 30: HD test results - RA

## Slide 31: UHD test results

## Slide 32: UHD test results

## Slide 33: UHD test results

## Slide 34: UHD test results

## Slide 35: UHD test results

## Slide 36: UHD test results

## Slide 37: Conclusions
Improved performance for ECM clearly demonstrated
Presented results preliminary, further study ongoing
Obvious differences between expert and naïve viewers
  Stronger opinions, expertise
  Personal interpretation of scale
  Naïve viewers more carefully obeying instructions received
Expert Viewing and Formal Subjective Assessment experiments provided results showing very consistent tendency!

## Slide 38: Thanks
Thanks to volunteers for ECM and VTM encoding, and crosscheck!
  Xiaomi, InterDigital, Bytedance, Qualcomm, Alibaba, Ericsson
Thanks for providing the equipment at meeting site!
  HHI
Thanks to Adam for support during test preparation!
Thanks to the 24 volunteers in Mainz!
Thanks to Vittorio for the laboratory test!