## Slide 1: JVET-AC0068 Non-EE2: multi-candidate IntraTMP Fan Wang Lai Zhang, Yue Yu, Haoping Yu, Dong Wang

## Slide 2: Single -> multiple
Current:
  IntraTMP selects only one BV with the smallest template matching cost.
Observation:
  In camera captured content, there are usually several blocks that are similar to the current block.
Proposed:
  This contribution proposes to use multiple candidates for IntraTMP.
    Select a shortlist of promising candidates with template matching.
    Allow the encoder to make the final decision.

## Slide 3: Signaling
Current:
  One block level flag to indicate using IntraTMP or not.
  No other signaling needed.
Proposed:
  An index to indicate which candidate BV is actually used for current block.
Syntax change example

## Slide 4: Searching process
Current:
  Sparse search: performed in the search range with sub-sampling by a factor of 2.
  Refinement search: performed around the best match in sparse search with a reduced search range.
Proposed:
  Sparse search: performed in the search range with sub-sampling by a factor of 3 and maintain 30 top BVs.
  Refinement search: check each 3x3 block around each of the 30 BVs and select the top 15 BVs.
Sparse search example refinement search example

## Slide 5: Test 1 results
Test: proposed multi-candidate IntraTMP over ECM-7.0
Anchor: ECM-7.0

## Slide 6: Enlarge the search range
Current:
  Besides the restriction of 4 CTU regions, the search range width and height are set proportional to the width and height of the current block, respectively, i.e. :
  SearchRangeWidth = a * BlkWidth
  SearchRangeHight = a * BlkHeight
  where ‘a’ is set as 5 in ECM-7.0.
Proposed:
  SearchRangeWidth = max(a * BlkWidth, minSearchRange)
  SearchRangeHight = max(a * BlkHeight, minSearchRange)
  where minSearchRange is set as 128.
  It enlarges the search range for the blocks with width or height smaller or equal to 16

## Slide 7: Test 2 results
Test: proposed multi-candidate IntraTMP with enlarged search range over ECM-7.0
Anchor: ECM-7.0

## Slide 8: Conclusion
This contribution proposes a multi-candidate IntraTMP method.
It is recommended to further investigate multi-candidate IntraTMP in the next EE.

## Slide 9
Thanks to vivo for crosschecking !