## Slide 1
JVET-AC0090
Neural Network-based Reference CU Quality
Enhancement for Motion Compensation Prediction
Yanhan Chu, Zhikui Wang,Wen Zhang, and Shuai Li

## Slide 2
Introduction
Motivation：
Motion estimation finds the reference CU in the reference frame which is most similar to the current CU.
Proposed：
Use neural network to enhance the reference CU.
The proposed method is applied on the luma CUs which is larger than 16×16.

## Slide 3
Proposed method
Embedding the neural network before motion compensation, as shown in Fig.1.
(a) Inter motion compensation
(b) Affine motion compensation
Fig. 1: motion compensation in VVC

## Slide 4
Proposed method
Neural network：
The proposed neural network architectures as shown in Fig. 2.
Fig. 2: The structure of the proposed neural network.

## Slide 5
Proposed method
Training：
Dataset：BVI-DVC
Net1: 64×64
Net2: 32×32
Net3: 16×16
Inference：
Net1: 64×64
Net2: 64×32, 32×64, 32×32
Net3: 16×64, 64×16, 32×16, 16×32, 16×16

## Slide 6
Result
Table 1. Performance of the proposed method (LDP)
 |  | Low delay P |  |  |  | 
 |  | Over VTM-11.0_nnvc-2.0 (QP 22, 27, 32, 37) |  |  |  | 
 |  | Y | U | V | EncT | DecT
Cass D | BasketballPass | -1.09% | 1.72% | -0.28% | 69314% | 18650%
 | BQSquare | -1.28% | 1.66% | 0.51% | 62348% | 30851%
 | BlowingBubbles | -0.70% | 0.59% | 1.59% | 61608% | 26800%
 | RaceHorses | -0.38% | 1.81% | 0.13% | 54884% | 25098%
overall |  | -0.86% | 1.44% | 0.44% | 57620% | 24264%

## Slide 7
Conclusion
This proposal presents a neural network based motion compensation enhancement method.
0.86% coding gains on the luma component of class D.
But the complexity of the method is high.

## Slide 8
THANKS