## Slide 1: JVET-AC0120 Non-EE2: template-based intra MPM list construction

## Slide 2: Introduction
In ECM, the following three aspects are considered to construct the MPM list:
  Planar, neighboring intra modes and DIMD modes
  The directional modes with added offset
  Default intra modes
PMPM
SMPM
22
6
16

## Slide 3: Proposed Method
The MPM list is constructed by the following three steps:
  The first entry in the general MPM list is always planar mode.
  The next entries are composed of neighboring intra modes and DIMD modes, which are sorted in ascending order of SAD cost. Up to 5 modes with the smallest SAD cost are added.
  The sorted directional modes with added offset are included into the general MPM list, and then the default modes, until the general MPM list with 22 entries is constructed.
Regarding the signalling method of the mode in SMPM list
  SMPM list is equally divided into four groups and the group index is parsed first. Then a mode index is parsed to indicate which modes in the selected group is used.

## Slide 4
Results
 | All Intra Main 10 |  |  |  | 
 | Over ECM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.07% | -0.16% | -0.12% | 104% | 102%
Class A2 | 0.02% | -0.02% | 0.00% | 104% | 102%
Class B | -0.02% | 0.01% | -0.10% | 104% | 103%
Class C | -0.11% | -0.06% | -0.21% | 103% | 106%
Class E | -0.17% | -0.15% | -0.14% | 103% | 103%
Overall | -0.07% | -0.07% | -0.12% | 104% | 103%
Class D | -0.15% | -0.25% | -0.09% | 103% | 106%
Class F | -0.09% | 0.05% | -0.10% | 102% | 102%
 | All Intra Main 10 |  |  |  | 
 | Over ECM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.07% | 0.01% | -0.19% | 104% | 101%
Class A2 | -0.03% | -0.09% | -0.05% | 103% | 101%
Class B | -0.05% | -0.09% | -0.14% | 104% | 101%
Class C | -0.11% | -0.11% | -0.18% | 103% | 104%
Class E | -0.10% | -0.04% | -0.08% | 103% | 101%
Overall | -0.07% | -0.07% | -0.13% | 103% | 102%
Class D | -0.13% | -0.14% | -0.22% | 103% | 105%
Class F | -0.10% | 0.09% | 0.04% | 102% | 102%
Test2: W*H > 32
Test1: W*H > 1024
 | Random Access Main 10 |  |  |  | 
 | Over ECM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.06% | -0.36% | -0.08% | 99% | 99%
Class A2 | -0.01% | 0.18% | -0.01% | 100% | 100%
Class B | -0.04% | -0.14% | -0.16% | 100% | 100%
Class C | -0.05% | 0.00% | -0.02% | 100% | 101%
Class E |  |  |  |  | 
Overall | -0.04% | -0.08% | -0.08% | 100% | 100%
Class D | -0.09% | 0.00% | -0.22% | 101% | 101%
Class F | -0.11% | -0.29% | -0.09% | 100% | 99%

## Slide 5: Conclusion
It is proposed to introduce a MPM list construction method.
On top of ECM-7.0, it achieves
AI {-0.07%, -0.07%, -0.13%}
It is suggested to investigate in the next round of EE2.
Thanks Qualcomm for cross-checking!

## Slide 6
THANK
YOU