## Slide 1: JVET-AC0126 EE1-related: Reduced complexity through channel redistribution in NN head
Per Wennersten, Jacob Ström, Du Liu
Ericsson

## Slide 2: Summary
Changed number of channels in NN head
Implemented on top of JVET-AC0089 (JVET-AB-EE1-1.5.3)
Compared to EE1-1.5.3:
  reduced kMacs by 9% to 615 kMAC/pix
  luma BD-rate: 0.01% RA, 0.08% AI, 0.12% LDB
Compared to Filter set #1:
  reduced kMacs by 7%
  luma BD-rate: -0.13% RA, 0.23% AI, 0.37% LDB

## Slide 3: Background
Implemented on top of JVET-AC0089 (JVET-AB-EE1-1.5.3)
JVET-AC0089: 96 channels per input out of first layer
96 channels between fuse and transition
96 channels in NN body

## Slide 4: Proposed Layout
First layer outputs different per input
  192 channels rec
  24 channels pred
  12 channels bs/qp/IPB
48 channels between fuse and transition
96 channels in NN body

## Slide 5: Complexity
Test/Luma model | Nbr. of models | kMAC/pix (Y) | kMAC/pix (YUV) worst case (frame-basis) | kMAC/pix (YUV) worst case (block-basis) | Num. of param. in total (106) | Total mem. in 16bit integer (106 bytes) | RA BDR-Y/U/V (vs. NNVC-3.0) | RA BDR-Y/U/V (vs. NNVC-3.0 filter set #1)
NNVC-3.0 filter set #1 | 4 | intra 415 inter 418 | 525 | 664 | 6.21 | 12.42 | ‑9.49%/ ‑20.71%/ ‑20.40% | 0
JVET-AB EE1-1.5.3: IPB luma + chroma noIPB | 2 | 425 | 532 | 673 | 3.10 | 6.21 | -9.60%/ ‑20.93%/ ‑21.49% | -0.13%/ ‑0.24%/ ‑1.41%
Proposed luma model | 2 | 379 | 486 | 615 | 3.03 | 6.06 | ‑9.60%/ ‑20.93%/ -21.41% | -0.13%/ -0.25%/ -1.32%

## Slide 6: Training information
Network Information in Training Stage |  | 
Mandatory | GPU Type | GPU: NVIDIA A100-PCIE-40GB
 | Framework: | PyTorch v1.9
 | Number of GPUs per Task | 1
 | Epoch: | 340
 | Batch size: | 32
 | Loss function: | Weighted L1 and L2
 | Training time: | 10.5 days
 | Training data information: | DIV2K, BVI-DVC
 | Training configurations for generating compressed training data (if different to VTM CTC): | VTM-11.0, JVET-W-EE1-1.6, qp {17, 22, 27, 32, 37, 42}
Optional |  | 
 | Number of iterations | 
 | Patch size | 256x256
 | Learning rate: | 1e-4 and 1e-5
 | Optimizer: | ADAM
 | Preprocessing: | 
 | Mini-batch selection process: | 
 | Other information: | 

## Slide 7: Inference information
Network Information in Inference Stage |  | 
Mandatory | HW environment: | 
 | GPU Type | N/A
 | Framework: | SADL [5]
 | Number of GPUs per Task | 0
 | Total Parameter Number | See Table 1
 | Parameter Precision (Bits) | Int16
 | Memory Parameter (MB) | See Table 1
 | Multiplay Accumulate (MAC) | See Table 1
Optional |  | 
 | Total Conv. Layers | 
 | Total FC Layers | 
 | Total Memory (MB) | 
 | Batch size: | 1
 | Patch size | 128x128, 256x256
 | Changes to network configuration or weights required to generate rate points | 
 | Peak Memory Usage (Total) | 
 | Peak Memory Usage (per Model) | 
 | Border handling | 
 | Other information: | 

## Slide 8: Results over JVET-AC0089
EncT/DecT unreliable
 | All intra |  |  |  | 
 | BD-rate Over JVET-AB-EE1-1.5.3 |  |  |  | 
 | Y-PSNR | U-PSNR | V-PSNR | EncT | DecT
Class A1 | 0.02% | -0.09% | -0.06% | 89% | 82%
Class A2 | 0.07% | 0.24% | 0.50% | 92% | 80%
Class B | 0.08% | -0.78% | -0.11% | 98% | 83%
Class C | 0.11% | -0.05% | -0.08% | 92% | 84%
Class E | 0.14% | 0.03% | 0.02% | 103% | 91%
Overall | 0.08% | -0.20% | 0.03% | 95% | 84%
Class D | 0.07% | 0.08% | 0.12% | 88% | 82%
Class F | 0.16% | 0.01% | 0.01% | 91% | 80%
 | Random access |  |  |  | 
 | BD-rate Over JVET-AB-EE1-1.5.3 |  |  |  | 
 | Y-PSNR | U-PSNR | V-PSNR | EncT | DecT
Class A1 | -0.09% | 0.02% | 0.15% | 86% | 80%
Class A2 | -0.03% | -0.02% | 0.02% | 87% | 76%
Class B | 0.01% | 0.06% | 0.14% | 88% | 82%
Class C | 0.10% | -0.12% | 0.06% | 91% | 87%
Class E |  |  |  |  | 
Overall | 0.01% | -0.01% | 0.10% | 88% | 82%
Class D | 0.18% | -0.14% | -0.03% | 89% | 86%
Class F | 0.16% | 0.07% | 0.04% | 86% | 75%
 | Low delay B |  |  |  | 
 | BD-rate Over JVET-AB-EE1-1.5.3 |  |  |  | 
 | Y-PSNR | U-PSNR | V-PSNR | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.05% | -0.11% | -0.41% | 82% | 80%
Class C | 0.17% | -0.44% | 0.16% | 82% | 75%
Class E | 0.17% | -0.10% | -0.10% | 75% | 71%
Overall | 0.12% | -0.26% | -0.16% | 80% | 76%
Class D | 0.25% | -0.63% | -0.23% | 82% | 77%
Class F | 0.26% | 0.51% | 1.07% | 79% | 67%

## Slide 9: Results over NNVC-3.0 filter set #1
 | All intra |  |  |  | 
 | BD-rate Over NNVC-3.0 filterset#1 |  |  |  | 
 | Y-PSNR | U-PSNR | V-PSNR | EncT | DecT
Class A1 | 0.06% | 2.09% | 2.54% | 108% | 100%
Class A2 | 0.22% | 1.52% | 3.65% | 105% | 96%
Class B | 0.21% | 4.72% | 0.46% | 108% | 100%
Class C | 0.31% | -0.34% | 0.02% | 110% | 104%
Class E | 0.35% | 1.46% | -1.94% | 112% | 108%
Overall | 0.23% | 2.08% | 0.84% | 109% | 102%
Class D | 0.24% | 0.27% | -2.03% | 109% | 107%
Class F | 0.27% | -3.80% | -3.17% | 109% | 104%
 | Random access |  |  |  | 
 | BD-rate Over NNVC-3.0 filterset#1 |  |  |  | 
 | Y-PSNR | U-PSNR | V-PSNR | EncT | DecT
Class A1 | 0.08% | -0.63% | -2.35% | 97% | 91%
Class A2 | 0.36% | -0.07% | 1.73% | 99% | 90%
Class B | -0.05% | 1.20% | -1.49% | 102% | 90%
Class C | -0.75% | -1.90% | -2.62% | 105% | 98%
Class E |  |  |  |  | 
Overall | -0.13% | -0.25% | -1.32% | 101% | 92%
Class D | -1.31% | -0.61% | -4.30% | 101% | 95%
Class F | -0.35% | -2.98% | -2.13% | 101% | 93%
 | Low delay B |  |  |  | 
 | BD-rate Over NNVC-3.0 filterset#1 |  |  |  | 
 | Y-PSNR | U-PSNR | V-PSNR | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.55% | -4.62% | -7.92% | 95% | 93%
Class C | 0.12% | -7.68% | -8.51% | 94% | 84%
Class E | 0.39% | -0.01% | -2.91% | 87% | 75%
Overall | 0.37% | -5.98% | -8.18% | 93% | 85%
Class D | 0.05% | -7.10% | -11.39% | 97% | 86%
Class F | -0.18% | -5.22% | -3.81% | 92% | 85%
EncT/DecT unreliable

## Slide 10: Conclusions
Modify the number of channels to reduce the complexity of the luma model.
By lowering the worst-case complexity to 91%, it is possible to maintain the performance -9.60% in RA as compared to JVET-AB-EE1-1.5.3.
Training time reduced 12%
Propose to include the test in the next EE.
Thanks to InterDigital for cross-checking.