## Slide 1: JVET-AC0138 Adjusting luma/chroma BD-rate balance in ECM
Y. Chen, E. Francois, C. Salmon-legagneur

## Slide 2
Observations: luma and chroma BDR-rate gains of ECM vs VTM are not well balanced, both for SDR and for HDR contents
SDR content
ECM7.0 vs VTM11.0ecm6
HDR content
ECM7.0 vs VTM11.0ecm6
Note*
HLG RA results are not yet available

## Slide 3
Investigate alternate balancing of luma and chroma BDR-rate gains of ECM vs VTM by tuning some following encoder cfg parameters
  Chroma QP offset parameters: CbQpOffset/CrQpOffset (-12,12)
    Increasing the CbQpOffset and CrQpOffset values  shifting chroma coding gains towards the luma
  LMCS chroma residual scaling parameter: LMCSOffset (-7,7)
    Decreasing the LMCSOffset value  shifting chroma coding gains towards the luma
    Gives finer tuning than Chroma QP offset

## Slide 4: SDR – tested configurations
Tested CbQpOffset, CrQpOffset, LMCSOffset parameters

## Slide 5: SDR – AI results
Original configuration has around 9-10% imbalance between luma and chroma
Tested configuration allows shifting around 7.5% chroma gain towards the 1% luma gain

## Slide 6: SDR – RA results
Original configuration has around 6-7% imbalance between luma and chroma
Tested configurations allow shifting around 2.4% chroma gain towards the 0.2% luma gain, or 9.6% chroma gain towards the 1.2% luma gain
Tested config 2 provides a stronger balance shift between luma and chroma
  Luma gain could be beyond 20%, while chroma gain would be lower than the luma gain

## Slide 7: SDR – LDB results
Original configuration has around 10% imbalance between luma and chroma
Tested configurations allow shifting around 4.4% chroma gain towards the 0.2% luma gain, or 11.2% chroma gain towards the 0.5% luma gain
Tested config 2 provides a stronger balance shift between luma and chroma
  Chroma gain would be slightly lower than the luma gain

## Slide 8: SDR – LDP results
Original configuration has around 9-10% imbalance between luma and chroma
Tested configuration allows shifting around 4.6% chroma gain towards the 0.2% luma gain
LDB and LDP had similar behavior, thus the tested configurations proposed for LDB could also be applied for LDP

## Slide 9: HDR – tested configurations
Tested CbQpOffset, CrQpOffset, LMCSOffset parameters
Tested configurations for PQ and HLG for AI/RA are unified

## Slide 10: HDR – AI results
Original configuration has around 21% wPSNR imbalance between luma and chroma for HDR PQ, and around 11% PSNR imbalance for HDR HLG
Tested configuration allows shifting around 16.2% chroma gain towards the 1.3% luma gain for HDR PQ, and around 9% chroma gain towards the 0.7% luma gain for HDR HLG

## Slide 11: HDR – RA results (incomplete)
Original configuration has around 20% wPSNR imbalance between luma and chroma for HDR PQ
Tested configuration allows shifting around 17.2% chroma gain towards the 1% luma gain for HDR PQ
Based on partial results, HDR HLG showed similar behavior as HDR PQ
Note*
HLG RA results are not yet available

## Slide 12
To get better balance between luma and chroma BDR variations when assessing ECM against VTM-11.0ecm6, it is observed that the ECM CTCs may be modified with as follows:
For SDR content For HDR content
Conclusion
Thanks Xiaomi for cross-check (JVET-AC0236)
Thanks Ericsson for additional help

## Slide 13
Additional data

## Slide 14: HLG RA
 | psnrY | psnrU | psnrV | avgUV
DayStreet2 | -16.23% | -34.91% | -27.84% | -31.37%
FlyingBirds3 | -13.36% | -20.26% | -32.23% | -26.25%
People2 | -15.01% | -24.53% | -21.73% | -23.13%
Sunset3 | #VALEUR! | #VALEUR! | #VALEUR! | #VALEUR!
partial avg | -14.87% | -26.57% | -27.27% | -26.92%
Reference
chQP 0, LMCSOffset 0
Test
chQP 1, LMCSOffset -1
 | psnrY | psnrU | psnrV | avgUV
DayStreet2 | -16.61% | -23.37% | -14.05% | -18.71%
FlyingBirds3 | -13.72% | -6.83% | -22.20% | -14.51%
People2 | -15.80% | -13.78% | -11.14% | -12.46%
Sunset3 | #VALEUR! | #VALEUR! | #VALEUR! | #VALEUR!
partial avg | -15.38% | -14.66% | -15.80% | -15.23%