## Slide 1: JVET-AC0163 Non-EE2:On non-separable primary transform for intra blocks
Ning Yan, Xiaoyu Xiu, Wei Chen, Hong-Jheng Jhu, Che-Wei Kuo, Changyue Ma, Xianglin Wang

## Slide 2: Introduction
In ECM7.0, DCT-II + LFNST and adaptive MTS are applied to de-correlate the residual samples of intra coded blocks.
In JVET-AA064 and JVET-AB0175, non-separable primary transforms have shown potentials to further improve the efficiency of intra coding.

## Slide 3: Proposal(1)
Non-separable primary transforms
  Non-separable transforms are applied to intra blocks with sizes 4x4, 4x8, 4x16, 8x4, 8x8, 8x16, 16x4, 16x8 and 16x16.
  For each block size, a total of 67 transform kernels are derived based on different intra prediction modes.
  For signaling, one additional flag is introduced after the existing MTS flag to indicate whether the proposed non-separable primary transform is applied.

## Slide 4: Proposal(2)
Transform kernel sharing
  Transform blocks with sizes 4x8, 4x16 and 8x16 share the same transform kernels with the transform blocks of 8x4, 16x4 and 16x8.
Transform coefficient zeroing-out
  Zero-out operation is applied to the block sizes 16x8, 8x16 and 16x16.
  The first 64 transform coefficients are retained while the rest coefficients are zeroed out.

## Slide 5: Performance Evaluation
ECM7.0 results
 | All Intra Main10 |  |  |  | 
 | Over ECM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.09% | -0.06% | -0.06% | 104% | 101%
Class A2 | -0.02% | 0.05% | 0.07% | 103% | 100%
Class B | -0.45% | -0.31% | -0.46% | 104% | 101%
Class C | -0.78% | -0.55% | -0.67% | 104% | 101%
Class E | -3.26% | -2.83% | -2.61% | 102% | 101%
Overall | -0.86% | -0.68% | -0.71% | 103% | 101%
Class D | -0.15% | -0.30% | -0.15% | 104% | 100%
Class F | -0.56% | -0.28% | -0.65% | 101% | 99%
Test #1: non-separable primary transforms
Test #2: Test #1 + transform kernel sharing
Test #3:
Test #1 + transform coefficient zero-out
Test #4:
Test #1 + transform kernel sharing + transform coefficient zero-out
 | All Intra Main10 |  |  |  | 
 | Over ECM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.39% | -0.31% | -0.27% | 103% | 101%
Class C | -0.64% | -0.44% | -0.44% | 103% | 100%
Class E | -2.59% | -2.25% | -2.14% | 102% | 100%
Overall | -0.68% | -0.56% | -0.53% | 103% | 101%
Class D | -0.10% | -0.25% | -0.06% | 103% | 99%
Class F | -0.44% | -0.21% | -0.22% | 101% | 99%
 | All Intra Main10 |  |  |  | 
 | Over ECM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.05% | 0.07% | -0.12% | 103% | 101%
Class C | -0.30% | -0.16% | -0.17% | 102% | 100%
Class E | -2.22% | -1.75% | -1.83% | 102% | 100%
Overall | -0.45% | -0.31% | -0.38% | 102% | 100%
Class D | 0.01% | 0.01% | -0.01% | 101% | 99%
Class F | -0.33% | 0.02% | -0.33% | 101% | 99%
 | All Intra Main10 |  |  |  | 
 | Over ECM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.01% | 0.05% | -0.14% | 102% | 101%
Class C | -0.18% | -0.07% | -0.15% | 101% | 101%
Class E | -1.63% | -1.40% | -1.40% | 101% | 100%
Overall | -0.31% | -0.23% | -0.30% | 102% | 100%
Class D | 0.01% | -0.14% | 0.04% | 101% | 101%
Class F | -0.16% | -0.02% | -0.07% | 100% | 100%

## Slide 6: Conclusion
Proposal
  Non-separable primary transform kernels are proposed for intra blocks
  0.86% gain for AI
  Recommendation
  Study the proposed methods in the context of EE2
Thanks to Google for the crosschecking!