## Slide 1: Non-EE2:Improvements on local illumination compensation in ECM7.0
Xiaoyu Xiu, Ning Yan, Hong-Jheng Jhu, Wei Chen, Che-Wei Kuo, Changyue Ma, Xianglin Wang

## Slide 2: Introduction
Local illumination compensation (LIC) in ECM-6.0
  Addressing the illumination variations in prediction blocks based on one linear model
  The scale and the offset are estimated based on the neighboring reconstructed samples
  Enabling scenarios:
    The LIC flag is explicitly signaled for AMVP inter CUs
    The LIC flag is inherited from one neighboring block for merge CUs
    The LIC is disabled for CIIP
  The LIC is only applicable to uni-predictive inter CUs
  Interaction between LIC and OBMC
    When LIC is enabled, OBMC is disabled
    When one neighboring block of the current CU applies the LIC, only its MVs are used to produce the corresponding prediction samples used for the OBMC process of the current CU

## Slide 3: Proposal
Aspect #1: Bi-predictive LIC
  Straightforward extension of the uni-predictive LIC to bi-prediction
  Same enabling scenarios:
    The LIC flag is explicitly signaled for AMVP inter CUs
    The LIC flag is inherited from one neighboring block for merge CUs
    Disabling the bi-predictive LIC for BDOF and DMVR
  LIC parameter derivation:
    Reuse the same linear model derivation of the uni-predictive LIC
    Derive the two linear model in L0 and L1 iteratively
Derive initial L0 linear model
Derive L1 linear model
Recalculate L0 linear model

## Slide 4: Proposal
Aspect #2: OBMC with LIC
    Enabling OBMC for LIC CUs where the OBMC is only applied to CU boundaries
    Besides the MVs, considering the LIC parameters to generate its corresponding prediction samples for the OBMC of the current CU

## Slide 5: Performance results
 | Random Access Main 10 |  |  |  | 
 | Over ECM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.65% | -0.38% | -0.43% | 108% | 101%
Class A2 | -0.31% | -0.04% | -0.15% | 108% | 103%
Class B | -0.44% | -0.21% | -0.31% | 108% | 102%
Class C | -0.25% | -0.17% | -0.10% | 106% | 99%
Class E |  |  |  |  | 
Overall | -0.40% | -0.20% | -0.25% | 107% | 101%
Class D | -0.24% | -0.25% | -0.02% | 106% | 101%
Class F | -0.42% | -0.37% | -0.32% | 106% | 102%
 | Low delay B Main 10 |  |  |  | 
 | Over ECM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
Class C | -0.42% | -0.44% | -0.46% | 108% | 102%
Class E | -0.39% | -0.73% | -0.76% | 109% | 101%
Overall | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
Class D | -0.19% | -0.09% | 0.16% | 108% | 102%
Class F | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #REF!
 | Random Access Main 10 |  |  |  | 
 | Over ECM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.65% | -0.38% | -0.43% | 108% | 101%
Class A2 | -0.31% | -0.04% | -0.15% | 108% | 103%
Class B | -0.44% | -0.21% | -0.31% | 108% | 102%
Class C | -0.25% | -0.17% | -0.10% | 106% | 99%
Class E |  |  |  |  | 
Overall | -0.40% | -0.20% | -0.25% | 107% | 101%
Class D | -0.24% | -0.25% | -0.02% | 106% | 101%
Class F | -0.42% | -0.37% | -0.32% | 106% | 102%
 | Low delay B Main 10 |  |  |  | 
 | Over ECM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.37% | -0.51% | -0.58% | 108% | 103%
Class C | -0.42% | -0.44% | -0.46% | 108% | 102%
Class E | -0.39% | -0.73% | -0.76% | 109% | 101%
Overall | -0.39% | -0.54% | -0.58% | 108% | 102%
Class D | -0.19% | -0.09% | 0.16% | 108% | 102%
Class F | -0.35% | -0.48% | -0.74% | 107% | 102%
Missing points are copied from anchors
Performance on ECM7.0

## Slide 6: Closing
Proposal
  Extension of the existing uni-predictive LIC to bi-prediction
  OBMC with LIC
  ~0.40% gains for RA and LD
  Recommendation
  Study the proposal in the context of EE2