## Slide 1: JVET-AC0173: Non-EE2: ALF classification based on residual data
Ikram Jumakulyyev, Nan Hu, Zhi Zhang, Vadim Seregin,
Marta Karczewicz, Han Huang

## Slide 2: Luma ALF classifiers
ECM two-classifier method for each 2x2 block
  Laplacian based classifier
  Band based classifier
  Switched at CTU level
Proposed third classifier
  Sum of absolute values of residual samples in 8x8 window is calculated
  Class index is derived as
classIdx = sum >> (sample bit depth – 2)

## Slide 3: Online trained luma filter shape
Taps:
#0~#19: Applied to neighboring reconstructed samples
#20~#27: Applied to offline-filtered results
#28~#30: Applied to samples before
deblocking filter.
Taps:
#0~#9: Applied to neighboring reconstructed samples
#10~#29: Applied to offline-filtered results
#30~#32: Applied to samples before
deblocking filter.
Two more coefficients compared to anchor
ECM shape
Proposed shape

## Slide 4: Results
 | All Intra Main10 |  |  |  | 
 | Over ECM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.00% | 0.00% | 100% | 101%
Class A2 | 0.00% | 0.00% | 0.00% | 101% | 100%
Class B | 0.00% | 0.00% | 0.00% | 101% | 101%
Class C | 0.00% | 0.00% | 0.00% | 100% | 101%
Class E | 0.00% | -0.01% | -0.01% | 101% | 101%
Overall | 0.00% | 0.00% | 0.00% | 100% | 101%
Class D | 0.00% | 0.00% | 0.00% | 100% | 100%
Class F | 0.00% | 0.00% | 0.00% | 100% | 101%
Random Access Main 10 |  |  |  | 
Over ECM-7.0 |  |  |  | 
Y | U | V | EncT | DecT
-0.12% | -0.09% | 0.04% | 100% | 101%
-0.09% | 0.00% | -0.09% | 101% | 101%
-0.10% | -0.07% | -0.10% | 101% | 101%
-0.21% | 0.03% | 0.02% | 100% | 100%
-0.13% | -0.03% | -0.04% | 100% | 101%
-0.17% | 0.03% | -0.06% | 101% | 101%
-0.08% | 0.03% | -0.01% | 101% | 101%
Low delay B Main10 |  |  |  | 
Over ECM-7.0 |  |  |  | 
Y | U | V | EncT | DecT
-0.18% | -0.10% | -0.51% | 101% | 102%
-0.50% | 0.20% | -0.10% | 100% | 100%
-0.23% | -0.63% | -0.45% | 101% | 100%
-0.30% | -0.13% | -0.36% | 101% | 101%
-0.23% | -0.25% | -0.49% | 101% | 101%
-0.01% | 0.12% | 0.23% | 100% | 101%
Classifier (missing 2 points in LDB, copied from anchor)
Low delay B Main 10 |  |  |  | 
Over ECM-7.0 |  |  |  | 
Y | U | V | EncT | DecT
0.03% | -0.12% | -0.26% | 99% | 101%
-0.13% | 0.48% | 0.06% | 104% | 103%
0.01% | -0.02% | 0.19% | 102% | 102%
-0.03% | 0.10% | -0.04% | 102% | 102%
-0.25% | 0.19% | 0.16% | 100% | 102%
-0.20% | -0.57% | -0.73% | 103% | 103%
 | All Intra Main 10 |  |  |  | 
 | Over ECM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.03% | 0.00% | 0.00% | 101% | 100%
Class A2 | -0.02% | 0.00% | 0.00% | 100% | 101%
Class B | -0.01% | 0.00% | 0.00% | 100% | 102%
Class C | -0.03% | 0.00% | 0.00% | 101% | 102%
Class E | 0.01% | 0.00% | 0.00% | 100% | 102%
Overall | -0.01% | 0.00% | 0.00% | 101% | 102%
Class D | -0.02% | 0.01% | 0.01% | 100% | 99%
Class F | -0.02% | 0.01% | 0.01% | 102% | 103%
Random access Main 10 |  |  |  | 
Over ECM-7.0 |  |  |  | 
Y | U | V | EncT | DecT
-0.09% | -0.12% | -0.03% | 102% | 102%
-0.01% | -0.05% | -0.05% | 100% | 100%
-0.01% | 0.03% | -0.10% | 101% | 102%
-0.15% | -0.04% | 0.04% | 99% | 101%
-0.06% | -0.04% | -0.04% | 100% | 101%
-0.34% | -0.04% | 0.08% | 99% | 100%
-0.06% | 0.02% | 0.09% | 101% | 101%
Shape

## Slide 5: Results of combined methods
 | All Intra Main 10 |  |  |  | 
 | Over ECM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.03% | 0.00% | 0.00% | 101% | 101%
Class A2 | -0.02% | 0.00% | 0.00% | 101% | 101%
Class B | -0.01% | 0.00% | 0.00% | 101% | 101%
Class C | -0.03% | 0.00% | 0.00% | 101% | 98%
Class E | 0.02% | -0.01% | -0.01% | 101% | 98%
Overall | -0.01% | 0.00% | 0.00% | 101% | 100%
Class D | -0.02% | 0.01% | 0.01% | 101% | 97%
Class F | -0.02% | 0.01% | 0.01% | 100% | 100%
Random access Main 10 |  |  |  | 
Over ECM-7.0 |  |  |  | 
Y | U | V | EncT | DecT
-0.17% | -0.10% | -0.02% | 101% | 101%
-0.09% | 0.04% | -0.02% | 101% | 102%
-0.12% | 0.13% | -0.10% | 100% | 101%
-0.34% | -0.02% | 0.03% | 99% | 100%
-0.18% | 0.02% | -0.03% | 100% | 101%
-0.46% | 0.04% | 0.18% | 101% | 99%
-0.18% | -0.09% | -0.06% | 101% | 102%
Low delay B Main 10 |  |  |  | 
Over ECM-7.0 |  |  |  | 
Y | U | V | EncT | DecT
-0.58% | -0.09% | -0.14% | 100% | 101%
-0.14% | 0.50% | 0.61% | 102% | 100%
-0.42% | 0.33% | 0.12% | 98% | 97%