## Slide 1
Lei Zhao, Kai Zhang, Zhipin Deng, Li Zhang
ByteDance Inc.
Non-EE2: Template matching-based subblock motion refinement
JVET-AC0187

## Slide 2: Summary
Proposed methods
  TM-based affine control points refinement
  TM-based SbTMVP motion shift refinement
Experimental results
  RA: -0.09%, -0.12%, -0.14%, 107%, 102%
  LDB: -0.13%, -0.12%, -0.33%, 111%, 108%

## Slide 3: Proposed method
TM-based affine control points refinement
  Applied for uni-directional affine candidates
  A same MV offset is assigned to all the CPMVs of an affine candidate
  The optimal CPMV offset with the minimum TM cost is conditionally used to refine the corresponding affine candidate if , where COri and Crefined denote the TM cost before and after refinement, and T is a constant threshold
TM-based motion shift refinement for SbTMVP
  The refined motion shift will be utilized to derive subblock motion
  CTU row restriction is imposed to get SbTMVP motion

## Slide 4: Simulation results
Experimental results (ECM7.0 as the anchor)
 | Random access Main10 |  | Random access Main10 |  | 
 | Over ECM7.0 |  | Over ECM5.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.09% | -0.24% | -0.04% | 106% | 102%
Class A2 | -0.11% | -0.04% | -0.15% | 105% | 102%
Class B | -0.05% | -0.02% | -0.21% | 107% | 102%
Class C | -0.10% | -0.20% | -0.11% | 108% | 104%
Class E |  |  |  |  | 
Overall | -0.09% | -0.12% | -0.14% | 107% | 102%
Class D | -0.09% | -0.16% | 0.00% | 108% | 104%
Class F | -0.05% | 0.08% | 0.23% | 105% | 103%
 | Low delay B Main10 |  | Low delay B Main10 |  | 
 | Over ECM5.0 |  | Over ECM5.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.10% | -0.19% | -0.46% | 109% | 107%
Class C | -0.17% | 0.01% | -0.04% | 113% | 109%
Class E | -0.12% | -0.16% | -0.50% | 112% | 109%
Overall | -0.13% | -0.12% | -0.33% | 111% | 108%
Class D | -0.22% | 0.70% | 0.51% | 114% | 118%
Class F | -0.14% | -0.03% | -0.32% | 108% | 108%
Missing points are copied from anchors

## Slide 5: Conclusion
TM-based subblock motion refinement is presented
0.09%/0.13% coding gain in RA/LDB configurations with 107%/102% and 111%/108% complexity
Recommend to study the proposed method in EE
Appreciate Alibaba for crosschecking