## Slide 1
JVET-AC0328
EE1-related: Combination of EE1-1.1 and EE1-1.2
Renjie Chang, Liqiang Wang, Xiaozhong Xu, Shan Liu (Tencent)

## Slide 2
Introduction
1
This contribution reports the combination test results of EE1-1.1.2 and EE1-1.2.1.
EE1-1.1.2 optimizes the performance by retraining the model based on new training scripts.
EE1-1.2.1 proposes a NN filter which is involved in the encoder decision process for partitioning.

## Slide 3
Results
1
Performance of EE1-1.1.2 + EE1-1.2.1 anchored on NNVC-3.0
Thanks OPPO and Ericsson for crosschecking.
 | Random access Main10 |  |  |  | 
 | BD-rate Over NNVC-3.0 anchor |  |  |  | 
 | Y-PSNR | U-PSNR | V-PSNR | EncT | DecT CPU
Class A1 | -10.09% | -16.20% | -20.25% | 170% | 59782%
Class A2 | -10.46% | -19.83% | -15.90% | 162% | 57248%
Class B | -9.45% | -22.00% | -20.98% | 166% | 59030%
Class C | -10.23% | -24.41% | -23.53% | 144% | 48286%
Class E |  |  |  |  | 
Overall | -9.99% | -21.05% | -20.50% | 160% | 55750%
Class D | -11.35% | -23.71% | -23.40% | 143% | 42810%
Class F | -4.76% | -14.64% | -12.57% | 196% | 24752%
 | All Intra Main10 |  |  |  | 
 | BD-rate Over NNVC-3.0 anchor |  |  |  | 
 | Y-PSNR | U-PSNR | V-PSNR | EncT | DecT CPU
Class A1 | -7.28% | -15.38% | -18.01% | 222% | 42064%
Class A2 | -6.92% | -17.00% | -14.37% | 175% | 34191%
Class B | -7.11% | -16.85% | -17.16% | 166% | 31296%
Class C | -8.26% | -17.29% | -19.55% | 146% | 21884%
Class E | -10.63% | -17.29% | -18.09% | 174% | 36353%
Overall | -7.95% | -16.80% | -17.52% | 172% | 31594%
Class D | -8.14% | -16.43% | -18.99% | 140% | 19913%
Class F | -5.00% | -13.71% | -12.59% | 126% | 26176%
Performance of EE1-1.1.2 + EE1-1.2.1 anchored on EE1-1.1.2
 | All Intra Main10 |  |  |  | 
 | BD-rate Over EE1-1.1.2 |  |  |  | 
 | Y-PSNR | U-PSNR | V-PSNR | EncT | DecT CPU
Class A1 | -0.33% | -0.14% | -0.09% | 113% | 101%
Class A2 | -0.44% | -0.07% | -0.18% | 116% | 100%
Class B | -0.47% | -0.03% | -0.21% | 117% | 99%
Class C | -0.54% | 0.32% | 0.13% | 121% | 100%
Class E | -0.58% | -0.25% | -0.30% | 117% | 101%
Overall | -0.47% | -0.01% | -0.12% | 117% | 100%
Class D | -0.49% | 0.56% | 0.55% | 120% | 99%
Class F | -0.32% | -0.06% | 0.06% | 107% | 100%
 | Random access Main10 |  |  |  | 
 | BD-rate Over EE1-1.1.2 |  |  |  | 
 | Y-PSNR | U-PSNR | V-PSNR | EncT | DecT CPU
Class A1 | -0.11% | -0.01% | -0.02% | 104% | 100%
Class A2 | -0.29% | 0.06% | 0.06% | 105% | 100%
Class B | -0.27% | 0.11% | 0.14% | 106% | 100%
Class C | -0.35% | 0.02% | 0.01% | 107% | 100%
Class E |  |  |  |  | 
Overall | -0.26% | 0.05% | 0.05% | 105% | 100%
Class D | -0.43% | 0.07% | 0.14% | 107% | 100%
Class F | -0.16% | -0.21% | 0.23% | 104% | 99%
It is suggested to adopt this contribution into the NNVC common software.