## Slide 1: JVET-AC0355 EE1-related: Improvement over combination of EE1-1.5 and EE1-1.7
Zhihuang Xie, Yue Yu, Haoping Yu, Dong Wang

## Slide 2: Introduction
In JVET-AC0310, a combination of EE1-1.5 and EE1-1.7 is proposed to reduce the model memory and improve coding performance of NNVC-3.0 filter set #1.
        In EE1-1.5, a combined intra and inter model is designed to handle different type of slices. The luma network is shown in Fig.1.
        In EE1-1.7, an additional model, shown in Fig.2, is introduced to further improve the coding performance.
Compared with EE1-1.5.3, this combination provides 0.73% luma gain for RA and 0.42% luma gain for LB.
Fig.2 Architecture of multiple frame-based CNN model in EE1-1.7
Fig.1 Luma network in EE1-1.5

## Slide 3: Proposal in JVET-AC0066
For B slices with Tid <= 2, it is proposed to adaptively switch between the original inter-luma model and the multiple frame-based model in EE1-1.7 at slice level. A slice-level flag is needed to indicate which model is used.
If the picture POC from RPL0 is equal to the picture POC from RPL1 and there are at least two reference pictures in RPL1, then the second reference picture is taken as Col_1.
Proposal in this contribution
For B slices with Tid <= 2, it is proposed to adaptively switch between the luma model in EE1-1.5 and the multiple frame-based model in EE1-1.7 at slice level. A slice-level flag is needed to indicate which model is used.
If the picture POC from RPL0 is equal to the picture POC from RPL1 and there are at least two reference pictures in RPL1, then the second reference picture is taken as Col_1.

## Slide 4: Simulation results
 | Random Access Main 10 |  |  |  | 
 | Over EE1-1.7.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.00% | 0.00% | 100% | 100%
Class A2 | 0.00% | 0.00% | 0.00% | 100% | 100%
Class B | 0.00% | 0.00% | 0.00% | 100% | 100%
Class C | 0.00% | 0.00% | 0.00% | 100% | 100%
Class E |  |  |  |  | 
Overall | 0.00% | 0.00% | 0.00% | 100% | 100%
Class D | 0.00% | 0.00% | 0.00% | 100% | 100%
Class F | 0.00% | 0.00% | 0.00% | 100% | 100%
 | Low delay B Main10 |  |  |  | 
 | Over EE1-1.7.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.71% | 0.21% | -0.01% | 103% | 98%
Class C | -0.77% | -0.24% | 0.16% | 102% | 98%
Class E | -1.54% | -0.42% | 0.12% | 104% | 109%
Overall | -0.93% | 0.01% | 0.06% | 103% | 100%
Class D | -0.60% | 0.23% | 0.53% | 103% | 96%
Class F | -0.62% | 0.92% | 0.55% | 105% | 100%
JVET-AC0066 over EE1-1.7.1 (joint aspect 1 and aspect 2)
 | Random Access Main 10 |  |  |  | 
 | Over combination of EE1-1.5 and EE1-1.7 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
Class A2 | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
Class B | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
Class C | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
Class E |  |  |  |  | 
Overall | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
Class D | 0.00% | 0.01% | 0.00% | 101% | 99%
Class F | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
 | Low delay B Main10 |  |  |  | 
 | Over combination of EE1-1.5 and EE1-1.7 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
Class C | -1.48% | 0.54% | -0.24% | 110% | 100%
Class E | -1.55% | -0.30% | -0.39% | 106% | 114%
Overall | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
Class D | -1.35% | 0.50% | -0.81% | 110% | 100%
Class F | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
Improvement over the combination of EE1-1.5 and EE1-1.7

## Slide 5: Simulation results
 | Random Access Main 10 |  |  |  | 
 | Over NNVC-3.0 filter set 1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
Class A2 | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
Class B | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
Class C | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
Class E |  |  |  |  | 
Overall | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
Class D | -2.15% | -0.80% | -4.28% | 91% | 88%
Class F | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
 | Low delay B Main10 |  |  |  | 
 | Over NNVC-3.0 filter set 1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
Class C | -1.93% | -6.95% | -8.69% | 97% | 92%
Class E | -1.95% | -0.23% | -2.94% | 95% | 101%
Overall | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
Class D | -1.77% | -6.36% | -11.18% | 98% | 90%
Class F | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
The proposed over NNVC-3.0 (NnlfOption = 2)
 | Random Access Main 10 |  |  |  | 
 | Over NNVC-3.0 anchor |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
Class A2 | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
Class B | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
Class C | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
Class E |  |  |  |  | 
Overall | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
Class D | -13.36% | -24.23% | -27.25% | 156% | 29434%
Class F | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
 | Low delay B Main10 |  |  |  | 
 | Over NNVC-3.0 anchor |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
Class C | -10.89% | -21.35% | -22.02% | 158% | 28489%
Class E | -10.57% | -17.38% | -19.86% | 315% | 29033%
Overall | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
Class D | -12.41% | -24.53% | -27.75% | 156% | 26768%
Class F | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
The proposed over NNVC-3.0 anchor

## Slide 6: Conclusion
This contribution presents the results of JVET-AC0066 on top of the combination of EE1-1.5 in JVET-AC0089 and EE1-1.7 in JVET-AC0177, i.e. AC0310.
On top of the combination, the proposed method can retain the coding gain or even better.
It is suggested to adopt this method into NNVC software.
Thanks to Bytedance for crosschecking!