## Slide 1: JVET-AD0022 EE1: Summary report of exploration experiment on neural network-based video coding
E. Alshina, F. Galpin, Y. Li, D. Rusanovskyy, M. Santamaria, J. Ström, L. Wang and Z. Xie

## Slide 2: NNVC-4.0 tools performance – complexity RA configuration
Performance-complexity trade-off of NN tools in NNVC-4.0

## Slide 3: No re-training NN-Filter required
Applicable to (almost) any filter architecture

## Slide 4: EE1-1.2& NNVC-4.0 tools
Key aspects: Content additivity (residual offset adjustment and combination with chroma order adjustment) provides 0.5% gain in LD-B cfg, decoder run time increment 10-15% (due to more frequent use of NN-based filter). Method efficient for both filter architectures in NNVC-4.0. Gain for RA and AI is minor.

## Slide 5: Some details of EE1-1.2
 | Complexity |  | Random Access (CTC) |  |  | LDB (CTC) |  | 
Contribution | Total Number of Parameters (Millions) | Worst Case Complexity (kMAC/pixel) | Y | Cb | Cr | Y | Cb | Cr
NNVC-filter set#0 | 1.9 | 615 | -9.8% | -21.1% | -20.5% | -8.9% | -17.8% | -19.2%
EE1-1.2.1 | 1.9 | 615 | -9.8% | -21.4% | -20.7% | -9.5% | -19.1% | -19.7%
EE1-1.2.3 | 1.9 | 615 | -9.8% | -21.8% | -21.2% | -9.6% | -21.3% | -20.1%
NNVC-filter set#1 | 3.1 | 673 | -9.6% | -20.9% | -21.5% | -8.3% | -19.8% | -20.7%
EE1-1.2.2 | 3.1 | 673 | -9.6% | -21.0% | -21.6% | -8.8% | -20.5% | -21.5%
EE1-1.2.4 | 3.1 | 673 | -9.6% | -21.9% | -21.8% | -8.8% | -22.5% | -22.9%
offset candidates are {1, 2}
the input/output order switch
between the U and V
EE1-1.2.1 EE1-1.2.2
EE1-1.2.3 EE1-1.2.4
additionally

## Slide 6: EE1-1.8& NNVC-4.0 tools
Key aspects: ~0.2% (RA), 0.4% (LDB) performance improvement for filter set#0 demonstrated with content adaptation with flipping, encoder run-time compared to anchor 102% (RA), 104% (LDB)

## Slide 7: Some details of EE1-1.8
CTU
CTU
Left - CTUs used for encoder decision in previous design, right – CTUs used for encoder decision in this EE1 test
 | Complexity |  | Random Access (CTC) |  |  | LDB (CTC) |  | 
Contribution | Total Number of Parameters (Millions) | Worst Case Complexity (kMAC/pixel) | Y | Cb | Cr | Y | Cb | Cr
NNVC-filter set#0 | 1.9 | 615 | -9.8% | -21.1% | -20.5% | -8.9% | -17.8% | -19.2%
EE1-1.8.2 (EncNnlfOpt=0) | 1.9 | 615 | -9.9% | -21.3% | -20.8% | -9.3% | -18.5% | -20.3%
EE1-1.8.1 (EncNnlfOpt=1) | 1.9 | 615 | -10.1% | -21.3% | -20.8% | -9.5% | -18.2% | -19.9%

## Slide 8: EE1-1.9& NNVC-4.0 tools
Key aspects:~1.4% (LDB) performance improvement for filter set#1 demonstrated with encoder run-time increment by 3%, no performance improvement in RA cfg

## Slide 9: Some details of EE1-1.9
 | Complexity |  | Random Access (CTC) |  |  | LDB (CTC) |  | 
Contribution | Total Number of Parameters (Millions) | Worst Case Complexity (kMAC/pixel) | Y | Cb | Cr | Y | Cb | Cr
NNVC-filter set#1 | 3.1 | 673 | -9.6% | -20.9% | -21.5% | -8.3% | -19.8% | -20.7%
NNVC-filter set#1 multi frame | 4.7 | 682 | -10.2% | -20.9% | -21.4% | -8.7% | -19.7% | -20.7%
EE1-1.9 | 4.7 | 682 | -10.2% | -20.9% | -21.4% | -10.0% | -19.8% | -21.0%

## Slide 10: NN-filter architecture tests
Re-training is required

## Slide 11: EE1 tests performance – complexity AI and RA configuration, YUV metric (6Y+U+V)/8
Major trend of the latest EE1 development:
  Performance improvement over the benchmarks
  Complexity reduction of the NN models
  Significant disbalance in luma/chroma gains between tests (weighted bd-rate gain is shown) [ITU-T HSTP-VID-WPOM]

## Slide 12: EE1-1.1& NNVC-4.0 tools
Key aspects: very low complexity (16kMAC/pxl) was achieved by decomposition of convolutions; 5 .2% (int 16) gain RA cfg
Simulation results
  Complexity ~16 kMAC/pixel
  Coding gain: ~5.2% in RA configuration vs. AhG11 anchor

## Slide 13: EE1-1.1 test description
Number of hidden layers: n = 11
Feature maps and rank: K = 24, R = 24, M = 72
Model complexity = 16.2 kMAC/pixel

## Slide 14: EE1-1.3& NNVC-4.0 tools
Key aspects: Proponents combine multiple ideas: starting from filter set#1 (separate Luma and Chroma filtering), add ”long-activation from filter set#0, removes partitioning information, unify intra-inter models; further simplify by decomposing 33 convolutions (like in EE1-1.1.1) . BS is used as input. Further improvement are in EE-related input.
Simulation results:
  Test 1.3.5.b reports -0.3% weighted bd-rate gain in RA vs. Filter Set #1 with 35% complexity reduction.
  Significant difference in luma/chroma gains: -2% chroma bd-rate gain on average vs. Filter Set #1

## Slide 15: EE1-1.3 test description
EE1-1.3.1 - baseline (JVET-AC0155)
EE1-1.3.2a - removal spatial processing of constant inputs (e.g. QP)
EE1-1.3.2b removes the partitioning input,
EE1-1.3.3 unified IPB models, (~50% memory requirements)
EE1-1.3.5a decomposes 3x3 convolutions into separable 3x1/1x3, (kMAC/pixel and memory reduced by >30%)
EE1-1.3.5b - model combining simplifications from these sub-tests.
EE1-1.3: architecture unification:
  Combines elements of Filter Set #0 and Filter Set #1
  Complexity reduction, decompositions.

## Slide 16: EE1-1.4& NNVC-4.0 tools
Key aspects: redistribution the number of channels in the head of NNLF allows reduction of computational complexity by ~10% with ~0.1% performance drop (filter set#1 architecture).
Simulation results:
  Complexity reduction ~10%.
  Performance impact: penalty ~0.1% vs Filter Set #1

## Slide 17: EE1-1.4 test description
 | d1 | d2 | d3 | d4 | kmacs/pixel | #parameters
Test EE1-1.4.1 | 192 | 24 | 12 | 48 | 480 | 1471k
Test EE1-1.4.2 | 192 | 16 | 8 | 48 | 478 | 1470k
Test EE1-1.4.3 | 128 | 16 | 8 | 64 | 481 | 1483k
Filter set #1 | 96 | 96 | 96 | 96 | 538 | 1549k
 | d1 | d2 | d3 | d4 | d5 | kmacs/pixel | #parameters
Test EE1-1.4.4 | 96 | 192 | 24 | 12 | 48 | 123 | 1482k
Test EE1-1.4.5 | 64 | 128 | 16 | 8 | 64 | 123 | 1492k
Filter set #1 | 96 | 96 | 96 | 96 | 96 | 135 | 1555k

## Slide 18: EE1-1.5& NNVC-4.0 tools
Key aspects: transformers contribute ~1.2% gain (all intra cfg), many tests are not yet finished. Attention mechanism in this scheme is usefull for Chroma coding. Inference uses PyTorch and float models (would be interesting to see an effect of quantization AB uses non integer friendly operations. Would be interesting to see effect of quantization.
Simulation results:
  Transformers reportedly provide ~1.2% gain in AI.
  Float32, PyTorch inference.
  Complexity number may not be directly comparable to SADL kMAC/pixel reported for other tests.

## Slide 19: EE1-1.5 test description

## Slide 20: EE1-1.6& NNVC-4.0 tools
Key aspects: proponents combine the strengths of residual blocks in filter set #1 (large receptive field) and filter set #0 (wide activation), process intra and inter with unified model, aggressively simplify the chroma model in EE1-1.6.1. EE1-1.6.2 takes BS as extra input for NNLF, providing additional 0.2% gain in RA, 0.1% gain in all-intra, and 0.2% loss in LDB.
Simulation results:
  -1.4% weighted bd-rate gain in RA reported comparing to Filter Set #1 with 19% complexity reduction.

## Slide 21: EE1-1.6 test description
EE1-1.6: architecture unification:
  Wide activation of Filter Set #0
  Large receptive field of Filter Set #1
  Joint processing of input data
  BS as input tested in EE1.6.2
  Mutli-scale elements added to the backbone block.

## Slide 22: EE1-1.7& NNVC-4.0 tools
Key aspects: 0.6% (RA), 0.8% (LDB), and 0.4% (all intra) performance improvement for filter set#0 demonstrated with modified training strategy. Addition transformers to the residual block of filterset#0 improved performance further by {1.2%, 11.2%, 10.9%} for YUV under RA configuration with almost 14% lower kMAC/pxl and 16% lower model memory (total params). Test c is based on transformer network and is implemented in PyTorch in float
Simulation results:
  New training: 0.6% (RA), 0.8% (LDB), and 0.4% (all intra)
  Test 1.7c (PyTorch float32) reports weighted bd-rate gain of 3.7%.
Chart: Random Access
| 3.8 | 3.8 | 3.8 | 3.8 | 3.8 | 6.56 | 3.8 | 3.8 | 6.2 | 6.2 | 6.2 | 6.0519999999999996 | 6 | 6 | 5.8 | 5.8 | 4.1079999999999997 | 4.1100000000000003 | 9.32 | 9.32 | 0.21026400000000001 | 11.2 | 11.2 | 11.2 | 5.6 | 8.1999999999999993 | 16 | 8 | 11.6 | 13.6 | 15.2 | 15.2
Loop Filter | -0.097501 | 0 | 0 | -0.10109 | -0.10271 | -0.10826 | 0 | 0 | -0.096014 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Post Filter | -0.0479
Super Resolution | -0.0213
NN Intra | -0.018108
NN Inter

## Slide 23: EE1-1.7 test description
EE1-1.7: Filter Set #0 improvements:
  Test 1.7a: Fine-tune the model by updating the dataset (alignment with training scripts from NNVC-4.0)
  Test 1.7b: Filter Set #0 with extended training set of I slices
  Test 1.7c: Further development of Filter Set #0: adding Transformer into residual block
    Float32, PyTorch model

## Slide 24: NN-Inter

## Slide 25: EE1-2.1& NNVC-4.0 tools
Key aspects: ~4.3% (RA), 3.2% (LDB) gain over AhG11 anchor. Tests use PyTorch in float for inference.

## Slide 26: Some details of EE1-2.1

## Slide 27: Conclusion
2 types of in NN-filter tests:
  “Architectural changes” defines filter architecture:
    Tests EE1-1.1, 1.3, 1.4, 1.5, 1.6, 1.7 - trade-off between complexity and performance
      Decomposed convolution, large (wide) activation, redistribution for number of channels, different type of attention, transformers, residual block with enlarged receptive field....
    “low operation point” ~5% gain vs VVC (RA), ~20 kMac/Pxl
    “high operation point” ~10% gain vs VVC (RA), ~500 kMac/pxl
    Recommendation: define default configuration of filter in NNVC, no more than 2: low and high operating point (BoG in needed)
  Content adaptivity design elements” applicable to any filter architecture:
    Tests EE1-1.2, 1.8, 1.9
      flipping, swapping Chroma, offsets, extra input from different POC, RDO...
    Main improvements in this EE round visible in LDB cfg (~0.5%)
    Recommendation: Consider adoption for design elements applicable to any filter type independent from filter architecture change (can be added to NNV later, after default filter configuration is defined)
Not NN-filter tests:
  NN-Inter:
    ~5% gain vs VVC (RA), ~900 kMac/Pxl
    Inference successfully cross-checked, float point implementation
    Recommendation: Continue investigation of NN-Inter, focusing on kMAC/pxl reduction.

## Slide 28: Filter architecture tests & NNVC-4.0 tools
Only Integer, Only SADL, Only cross-checked training, only architectural changes
Short list:
  X-checked, Int16 SADL, selected by proponents or best subtest.
  Combined YUV metrics: bd-rate (6Y+U+V)/8, complexity: YUV 4:2:0 kMAC/pixel

## Slide 29: Filter architecture tests & NNVC-4.0 tools
Only Integer, Only SADL, Only cross-checked training, only architectural changes
Short list:
  X-checked, Int16 SADL, selected by proponents or best subtest.
  Combined YUV metrics: bd-rate (6Y+U+V)/8, complexity: YUV 4:2:0 kMAC/pixel

## Slide 30: NN Filter aspects
 | Y and VV separate? | Intra = Inter model? | Long Skip | Long/wide Activation | #RBs | Part. | BS | Pred. | QP | Chanels # variable | Transformers | CONV decompoed
Filter set#0 | no |  |  |  |  |  |  |  |  |  |  | 
Filter set#1 | yes |  |  |  |  |  |  |  |  |  |  | 
EE1-1.1 |  |  |  |  |  |  |  |  |  |  |  | 
EE1-1.4 |  |  |  |  |  |  |  |  |  |  |  | 
EE1-1.5 |  |  |  |  |  |  |  |  |  |  |  | 
EE1-1.6 |  |  |  |  |  |  |  |  |  |  |  | 
EE1-1.7 |  |  |  |  |  |  |  |  |  |  |  |