## Slide 1
BBAAD9C20180234D78A0072836F0B3D0B2B9B20E1D588B80A6D98633B1632B763B49B8389164AB0322992F08C846F5EB8AF9210AA1D0AB611BBFC213736E25D824F696AD582596B794A028E767D246FE7E02E0E17042018528CAA19A31EE9C28DE16269C4E3
AHG 8: A preprocessing software implementation for OFM
Binzhe Li, Shurun Wang, Jie Chen, Yan Ye, Shiqi Wang
Apr. 2023

## Slide 2: Outline
Architecture
Analysis and Processing
Usage and Configuration
Performance
Conclusion

## Slide 3: Architecture
The architecture of software implementation:
  Machine-oriented analysis
  Machine-oriented pre-processing
    Block-based processing
    Feature-based blurring
  Encoder and Decoder (VTM)
  Machine consumption

## Slide 4: Outline
Architecture
Analysis and Pre-processing
Usage and Configuration
Performance
Conclusion

## Slide 5: Analysis and Preprocessing
Analysis: distinguish videos with different characteristics and use corresponding pre-processing methods.
  Characteristics :
    Average object ratio: object ratio at picture level-measuring the machine-oriented spatial complexity
    Temporal complexity: video temporal variation-measuring the temporal complexity
Pre-processing
  Block-based pre-processing
  Blurring-based pre-processing
An example pipeline of the ROI based pre-processing
  Basically same as JVET-AC0086 and current CE1.2 in VCM of MPEG4

## Slide 6: Outline
Architecture
Analysis and Processing
Usage and Configuration
Performance
Conclusion

## Slide 7: Usage and Configuration
Repository:
  https://vcgit.hhi.fraunhofer.de/jvet-ahg-ofm/vtm-ofm/-/tree/JVET-AC0086
Installation:
  Detectron2 is also required in analysis and pre-processing.
  An installation file, “install.sh”, is prepared for the virtual environment setup and the software installation.
Configuration
  The default preprocess is “Process_Blur”. The input argument “--Preprocess” can be specified to invoke the pre-processing method.
Scripts
  Example scripts (batch_run_JVET_(SFU_yuv/track).py) of SFU-HW and TVD datasets are provided in the source code.

## Slide 8: Outline
Architecture
Analysis and Processing
Usage and Configuration
Performance
Conclusion

## Slide 9: Performance: SFU-HW dataset, object detection task
The overall Pareto BD-rate savings over VVC are 14.64%, 11.59% and 22.78% under random access (RA), low delay (LD) and all intra (AI) configurations, respectively.
Coding efficiency especially high for Class A and Class B
 | RA |  |  | LD |  |  | AI |  | 
 | BD-Rate (6 points) | BD-Rate Pareto | BD-mAP | BD-Rate (6 points) | BD-Rate Pareto | BD-mAP | BD-Rate (6 points) | BD-Rate Pareto | BD-mAP
Class A | / | -52.07% | 3.35 | -13.83% | -13.83% | 2.14 | / | -39.33% | 6.56
Class B | / | -29.59% | 4.71 | -24.95% | -24.95% | 3.84 | -33.96% | -33.96% | 6.74
Class C | -4.97% | -4.97% | 0.77 | / | -6.49% | 0.19 | -16.47% | -16.47% | 2.49
Class D | 0.00% | 0.00% | -0.55 | -2.60% | -2.65% | -0.22 | -13.78% | -13.78% | 2.33
Average | / | -14.64% | 1.78 | / | -11.59% | 1.34 | / | -22.78% | 4.06
*The ‘/’ means non-monotonous performance.

## Slide 10: Performance: TVD dataset, object tracking task
The overall Pareto BD-rate savings over VVC are 57.61%, 43.25% and 63.82% under RA, LD and AI configurations, respectively.
Substantial rate savings for 1080p resolution
 | RA |  |  | LD |  |  | AI |  | 
 | BD-Rate (6 points) | BD-Rate Pareto | BD-MOTA | BD-Rate (6 points) | BD-Rate Pareto | BD-MOTA | BD-Rate (6 points) | BD-Rate Pareto | BD-MOTA
TVD-01_1 | / | -82.98% | 12.78 | / | -65.38% | 14.33 | -87.72% | -87.72% | 24.79
TVD-01_2 | -76.08% | -76.08% | 9.06 | / | -70.85% | 8.54 | -85.77% | -85.77% | 22.67
TVD-01_3 | -56.02% | -56.02% | 8.25 | / | -26.38% | 4.10 | -74.59% | -74.59% | 14.26
TVD-02_1 | 0.00% | 0.00% | 0.00 | 0.00% | 0.00% | 0.00 | 0.00% | 0.00% | 0.00
TVD-03_1 | -51.21% | -51.21% | 7.58 | -29.32% | -29.32% | 5.31 | -56.68% | -56.68% | 12.42
TVD-03_2 | -68.08% | -68.08% | 6.70 | / | -45.67% | 5.82 | -65.84% | -65.84% | 10.77
TVD-03_3 | -68.89% | -68.89% | 7.96 | -65.14% | -65.14% | 6.14 | -76.10% | -76.10% | 14.58
Average | / | -57.61% | 7.48 | / | -43.25% | 6.32 | -63.82% | -63.82% | 14.21
*The ‘/’ means non-monotonous performance.

## Slide 11: Outline
Architecture
Analysis and Processing
Usage and Configuration
Performance
Conclusion

## Slide 12: Conclusion
Simulation shows that pre-processing is effective and achieves superior performance to VVC on various machine tasks, test datasets and coding configurations.
Based on the performance, it can be seen that the proposed method achieves substantial compression efficiency improvement, especially for high resolution videos.
It is suggested to include information about the software in the technical report for optimization of encoders and receiving systems for machine analysis of coded video content.

## Slide 13
Thanks
BBAAD9C20180234D78A0072836F0B3D0B2B9B20E1D588B80A6D98633B1632B763B49B8389164AB0322992F08C846F5EB8AF9210AA1D0AB611BBFC213736E25D824F696AD582596B794A028E767D246FE7E02E0E17042018528CAA19A31EE9C28DE16269C4E3

## Slide 14: Performance
Performance comparison on SFU-HW Dataset.
  The proposed preprocessing software is more effective at high resolution.
 | RA |  |  | LD |  |  | AI |  | 
 | BD-Rate (6 points) | BD-Rate Pareto | BD-mAP | BD-Rate (6 points) | BD-Rate Pareto | BD-mAP | BD-Rate (6 points) | BD-Rate Pareto | BD-mAP
Class A | / | -52.07% | 3.35 | -13.83% | -13.83% | 2.14 | / | -39.33% | 6.56
Class B | / | -29.59% | 4.71 | -24.95% | -24.95% | 3.84 | -33.96% | -33.96% | 6.74
Class C | -4.97% | -4.97% | 0.77 | / | -6.49% | 0.19 | -16.47% | -16.47% | 2.49
Class D | 0.00% | 0.00% | -0.55 | -2.60% | -2.65% | -0.22 | -13.78% | -13.78% | 2.33
Average | / | -14.64% | 1.78 | / | -11.59% | 1.34 | / | -22.78% | 4.06
 | RA |  |  | LD |  |  | AI |  | 
 | BD-Rate (6 points) | BD-Rate Pareto | BD-mAP | BD-Rate (6 points) | BD-Rate Pareto | BD-mAP | BD-Rate (6 points) | BD-Rate Pareto | BD-mAP
Class A | -6.94% | -6.94% | 0.28 | -9.83% | -9.83% | 1.08 | -20.74% | -20.74% | 3.31
Class B | -18.58% | -18.58% | 3.08 | -17.22% | -17.33% | 4.08 | -17.64% | -17.64% | 3.66
Class C | -11.41% | -11.41% | 1.49 | -14.35% | -14.35% | 2.17 | -11.68% | -11.68% | 1.75
Class D | / | -17.27% | 1.46 | / | -17.41% | 1.53 | -1.33% | -1.33% | 0.14
Average | / | -15.07% | 1.87 | / | -15.86% | 2.48 | -11.03% | -11.03% | 1.96
Table 2. JVET-AB0275-b (CE1.5–b) Result
Table 1. Proposed Result (JVET-AD0047)

## Slide 15: Performance
Performance comparison on TVD video Dataset.
  The proposed preprocessing software is more effective.
 | RA |  |  | LD |  |  | AI |  | 
 | BD-Rate (6 points) | BD-Rate Pareto | BD-MOTA | BD-Rate (6 points) | BD-Rate Pareto | BD-MOTA | BD-Rate (6 points) | BD-Rate Pareto | BD-MOTA
TVD-01_1 | / | -82.98% | 12.78 | / | -65.38% | 14.33 | -87.72% | -87.72% | 24.79
TVD-01_2 | -76.08% | -76.08% | 9.06 | / | -70.85% | 8.54 | -85.77% | -85.77% | 22.67
TVD-01_3 | -56.02% | -56.02% | 8.25 | / | -26.38% | 4.10 | -74.59% | -74.59% | 14.26
TVD-02_1 | 0.00% | 0.00% | 0.00 | 0.00% | 0.00% | 0.00 | 0.00% | 0.00% | 0.00
TVD-03_1 | -51.21% | -51.21% | 7.58 | -29.32% | -29.32% | 5.31 | -56.68% | -56.68% | 12.42
TVD-03_2 | -68.08% | -68.08% | 6.70 | / | -45.67% | 5.82 | -65.84% | -65.84% | 10.77
TVD-03_3 | -68.89% | -68.89% | 7.96 | -65.14% | -65.14% | 6.14 | -76.10% | -76.10% | 14.58
Average | / | -57.61% | 7.48 | / | -43.25% | 6.32 | -63.82% | -63.82% | 14.21
 | RA |  |  | LD |  |  | AI |  | 
 | BD-Rate (6 points) | BD-Rate Pareto | BD-MOTA | BD-Rate (6 points) | BD-Rate Pareto | BD-MOTA | BD-Rate (6 points) | BD-Rate Pareto | BD-MOTA
TVD-01_1 | -33.60% | -33.60% | 3.29 | / | -44.54% | 9.34 | -38.93% | -38.93% | 5.86
TVD-01_2 | -34.19% | -34.19% | 3.67 | -39.73% | -39.73% | 4.94 | -37.94% | -37.94% | 6.00
TVD-01_3 | -37.26% | -37.26% | 3.76 | -34.13% | -34.13% | 3.72 | -42.14% | -42.14% | 4.71
TVD-02_1 | -17.32% | -17.32% | 1.44 | / | -33.93% | 0.89 | -15.84% | -15.84% | 1.10
TVD-03_1 | -20.32% | -20.32% | 2.78 | -14.43% | -14.43% | 3.13 | -37.29% | -37.29% | 6.98
TVD-03_2 | -26.85% | -26.85% | 1.96 | / | -13.12% | 3.40 | -37.95% | -37.95% | 5.26
TVD-03_3 | -32.45% | -32.45% | 2.49 | -55.44% | -55.44% | 5.16 | -40.52% | -40.52% | 5.19
Average | -28.86% | -28.86% | 2.77 | / | -33.62% | 4.37 | -35.80% | -35.80% | 5.01
Table 1. Proposed Result (JVET-AD0047)
Table 2. JVET-AB0275-b (CE1.5–b) Result