## Slide 1: AHG10: Improvement of Input Video Padding in VTM
Junqi Liao, Li Li, Dong Liu, Houqiang Li, Feng Wu
University of Science and Technology of China
JVET-AD0129

## Slide 2: Input video padding in VTM
In order to adapt the encoder to inputs of different sizes, VTM pads the input video to a size that is a multiple of 8 and the minimum CU size after reading it.
The right-side padding and bottom-side padding are performed sequentially.

## Slide 3: Original implementation
The right-side padding
  The pixels in the right side are padded with the upper right pixel, which does not make any sense.
The bottom-side padding
  The pixels in the bottom side are padded with the last row of pixels, which is the normal replicate padding.

## Slide 4: Fix the right-side padding
The right-side padding
  The pixels in the right side are padded with the upper right pixel the last column of pixels.
The bottom-side padding
  The pixels in the bottom side are padded with the last row of pixels.

## Slide 5: Test sequences
Since the normal size of CTC sequences does not trigger the implementation of padding, we test the performance on CTC sequences cropped with a reduction of 4 in both original width and height.

## Slide 6: Test sequences
To eliminate the impact of the dataset cropping method on performance, we test the performance on CTC sequences cropped respectively with the center point (CT) and upper left corner (UL) as the center.
4 pixels
4 pixels
CT
UL
2 pixels
2 pixels
2 pixels
2 pixels

## Slide 7: Test results (CT)
 | Over VTM19.2 anchor |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.37% | -0.55% | -0.62% | 99% | 99%
Class A2 | -0.07% | -0.28% | -0.25% | 101% | 100%
Class B | -0.19% | -0.54% | -0.28% | 101% | 100%
Class C | -0.01% | -0.43% | -0.54% | 101% | 104%
Class E | -0.25% | -0.14% | -0.09% | 102% | 99%
Overall | -0.17% | -0.41% | -0.36% | 101% | 101%
Class D | 0.00% | -0.53% | -0.83% | 104% | 97%
 | Over VTM19.2 anchor |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.58% | -0.88% | -0.77% | 92% | 93%
Class A2 | -0.40% | -0.51% | -0.54% | 85% | 91%
Class B | -0.50% | -1.08% | -1.13% | 103% | 105%
Class C | 0.14% | -0.31% | 0.01% | 100% | 101%
Class E |  |  |  |  | 
Overall | -0.33% | -0.72% | -0.64% | 96% | 99%
Class D | 0.05% | -0.24% | 0.22% | 118% | 115%
 | Over VTM19.2 anchor |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.60% | -0.73% | -0.69% | 100% | 100%
Class C | 0.12% | -0.90% | 0.10% | 100% | 101%
Class E | -0.39% | -0.08% | -1.51% | 101% | 103%
Overall | -0.31% | -0.62% | -0.63% | 100% | 101%
Class D | -0.13% | -0.35% | -1.03% | 102% | 107%
All intra
Random access
Low delay B

## Slide 8: Test results (UL)
All intra
Random access
Low delay B
 | Over VTM19.2 anchor |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.35% | -0.99% | -0.81% | 99% | 100%
Class A2 | -0.07% | -0.13% | -0.27% | 100% | 100%
Class B | -0.19% | -0.30% | -0.45% | 100% | 101%
Class C | 0.00% | -0.37% | -0.29% | 101% | 105%
Class E | -0.19% | -0.31% | -0.46% | 101% | 97%
Overall | -0.16% | -0.41% | -0.45% | 100% | 101%
Class D | 0.01% | -1.06% | -0.65% | 103% | 97%
 | Over VTM19.2 anchor |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.62% | -0.72% | -0.38% | 100% | 97%
Class A2 | -0.38% | -0.67% | -0.08% | 95% | 103%
Class B | -0.59% | -0.87% | -0.76% | 89% | 92%
Class C | 0.12% | -0.33% | 0.14% | 94% | 94%
Class E |  |  |  |  | 
Overall | -0.36% | -0.65% | -0.31% | 93% | 95%
Class D | 0.23% | -1.41% | -0.22% | 102% | 99%
 | Over VTM19.2 anchor |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.58% | -0.84% | -0.73% | 99% | 99%
Class C | 0.19% | -0.18% | -0.46% | 100% | 101%
Class E | -0.41% | 0.05% | -1.13% | 101% | 100%
Overall | -0.28% | -0.39% | -0.74% | 100% | 100%
Class D | -0.06% | -1.81% | -0.33% | 101% | 100%

## Slide 9: Thank you!