## Slide 1: JVET-aD0216 Non-EE2:IBC with Non-ADJACENT SPATIAL CANDIDATES
Changyue Ma, Xiaoyu Xiu, Wei Chen, Hong-Jheng Jhu, Che-Wei Kuo, Ning Yan, Xianglin Wang

## Slide 2: Introduction
IBC candidate list in ECM8.0:
Only spatial adjacent candidates are used to generate IBC AMVP/merge candidate list.
Spatial non-adjacent candidates are also used to generate regular AMVP/merge candidate list.
It is straightforward to extend spatial non-adjacent candidates for IBC mode.

## Slide 3: Proposal
Spatial non-adjacent candidates are used to generate IBC AMVP/merge candidate list.
Spatial non-adjacent candidates are inserted between spatial adjacent candidates and HBVP candidates.
Similar grid pattern used for spatial non-adjacent candidates of regular inter is reused for IBC mode.
Distances between non-adjacent candidates and current block are defined based on current block size.

## Slide 4: Performance evaluation
Summary of results
 | All Intra Main 10 |  |  |  | 
 | Y | U | Y | Enc. T | Dec. T
Class F | -0.34% | -0.35% | -0.42% | 100% | 102%
Class TGM | -0.42% | -0.37% | -0.35% | 100% | 106%
 | Random Access Main 10 |  |  |  | 
 | Y | U | Y | Enc. T | Dec. T
Class F | -0.26% | -0.54% | -0.24% | 100% | 101%
Class TGM | -0.31% | -0.34% | -0.41% | 99% | 101%

## Slide 5: Performance evaluation
Overall results of combining the proposed method with enhanced IBC-GPM proposed in JVET-AD0215
 | All Intra Main 10 |  |  |  | 
 | Y | U | Y | Enc. T | Dec. T
Class F | -0.51% | -0.62% | -0.69% | 101% | 102%
Class TGM | -0.90% | -0.78% | -0.73% | 101% | 105%
 | Random Access Main 10 |  |  |  | 
 | Y | U | Y | Enc. T | Dec. T
Class F | -0.38% | -0.80% | -0.53% | 100% | 101%
Class TGM | -0.67% | -0.54% | -0.61% | 100% | 101%

## Slide 6: Performance evaluation
Summary:
It is proposed to use spatial non-adjacent candidates for IBC AMVP/merge candidate list construction.
Achieve promising coding benefits without noticeable enc/dec runtime.
It is recommended to study the proposed method in the next round of EE.
  Thanks to ByteDance for the crosschecking!